## Slide 1: Coordinated Transmission Scheme for 11be
Date: 2019-05-16
Authors:

## Slide 2: Introduction
A number of contributions showed that Multi-AP coordination has benefit [1-5]
However, there remains many complicated problems to solve
  Centralized scheduling and control of multiple APs
  Obtaining channel feedback from STAs to multiple APs
  Handling multi-AP management information and STA data
  General MAC issues
    EDCA events, sequence control
It is good to start with a simplified approach
In this contribution we introduce a simple coordinated transmission scheme
  Requiring less change on the current PHY and MAC
  Requiring less signaling overhead

## Slide 3: The Proposed Coordinated Transmission Scheme (1)
AP1 has granted a TXOP for DL transmission
If an RU of AP1’s DL PPDU meets any of the following conditions, AP2 can participate coordinated transmission
  The RU is empty (Coordinated OFDMA)
    Preamble puncturing or RU allocation granularity
  The recipient of the RU is isolated from AP2 by distance (Coordinated Spatial Reuse)
APs can share each other's TXOP opportunistically
AP1
TXOP holder
AP2
Coordinated DL
contention
contention
contention
contention
Coordinated DL
TXOP holder
AP1
AP2
STA1
STA2
STA3

## Slide 4: The Proposed Coordinated Transmission Scheme (2)
Assuming that, each AP can know which STA is isolated from itself
At the beginning of the TXOP, AP1 may transmit an AP Trigger frame soliciting coordinated transmission
  Providing information corresponding to its own transmission
    PPDU length, RU Allocation, common preamble information
  The TXOP holder does not consider the scheduling of the other AP
Upon the reception of the AP Trigger frame, AP2 determines whether it can participate coordinated transmission
  Based on the information provided from the AP Trigger
AP Trigger
STA2
STA1 Ack
STA1
AP1
STA3 Ack
STA3
AP2
EHT Preamble
EHT Preamble
EHT Preamble
EHT Preamble
STA2 Ack
CCA
AP1
AP2
STA1
STA2
STA3

## Slide 5: Determining isolated STAs
AP can determine a STA is isolated based on the RSSI level
  Receiving a short packet from the STA is enough to measure the RSSI
Leveraging NDP Feedback Report will enable AP to get RSSI feedback from a massive number of STAs at once
  Multiple APs can jointly transmit NFRP Trigger frame to solicit NFR across different BSSs
AP can trigger a joint feedback polling periodically or at the beginning of a TXOP
  The collected feedback can be shared among multiple APs
    by round robin, or
    Piggybacked in the AP Trigger frame for coordinated transmission
ATF
Joint NFRP
AP1
AP1, AP2
BSS1 NFR
BSS2 NFR

## Slide 6: Benefit of the proposed scheme
Increase channel occupancy of AP with low cost
  After sharing a TXOP of a nearby AP, the participant AP can continue its EDCA behavior
Less signaling overhead
  Channel feedback overhead is greatly reduced compare to joint MU-MIMO
    An existing scheme, such as NFRP, can maximize the efficiency of feedback collection
  Not requiring centralized scheduling
    RU allocation can be done by each participating AP
    Reducing the requirements on the backhaul link between APs
Less requirement on synchronization
  The recipients of each AP are decoupled

## Slide 7: Conclusion
In this contribution, we have proposed a simple coordinated transmission scheme
  The TXOP holder AP provides information corresponding to its own transmission
  A nearby AP participates coordinated transmission opportunistically if:
    An RU is empty (Coordinated OFDMA)
    The recipient of an RU is isolated (Coordinated Spatial Reuse)
An existing scheme, such as NFRP can be extended to efficiently collect feedbacks for the coordinated transmission

## Slide 8: References
[1] Distributed MU-MIMO and HARQ Support for EHT, 11-18/1116r0
[2] Multi-AP Enhancement and Multi-Band Operations, 11-18/1155r1
[3] Considerations on AP Coordination, 11-18/1576
[4] Terminology for AP Coordination, 11-18/1926r2
[5] Joint Processing MU-MIMO Update, 11-19/384r0