## Slide 1
Authors:
Discussion on Multi-band/Multi-channel Access Method
Date: 2019-05-16
Name | Affiliation | Address | Phone | Email
Liuming Lu | ZTE Corporation | No.889 Bibo Road, Shanghai, P.R.China |  | lu.liuming@zte.com.cn
Liquan Yuan | ZTE Corporation | No.889 Bibo Road, Shanghai, P.R.China |  | yuan.liquan@zte.com.cn
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 1

## Slide 2: Introduction
Multi-band/multi-channel aggregation and operation has been proposed as a main candidate feature for EHT, showed in the EHT proposed PAR. And the support for real-time applications(RTA) needs to be considered for EHT.
This contribution proposes multi-band/multi-channel access method which aim is to improve worst case latency and jitter and to increase the reliability of the real-time transmission of RTA data.

## Slide 3: Background
EHT needs to support real-time applications
  New high-throughput, low latency applications will proliferate such as virtual reality or augmented reality, gaming, remote office and cloud computing.
  Enhanced reliability, reduced latency and jitter in supporting the applications need to be considered in the next-generation WLAN standards.
  EHT aims to provide further improvement of aggregate throughput and latency to ensure competitiveness of IEEE Std. 802.11 in coming years. At least one mode of operation capable of improved worst case latency and jitter will be defined[1,2].

## Slide 4: Background
Existing Channel Access Method
  EDCA, a contention based channel access method, required for prioritized QoS Services ; but cannot guarantee the requirement of the real-time transmission of RTA data for low latency and jitter.
  HCCA, controlled channel access method, required for parameterized QoS Services; a BSS using HCCA might schedule traffic in its own BSS to "guarantee" a service, but if two HCCA BSSs overlap and they do not coordinate their scheduled TXOPs, then a degradation of QoS might result[3].
  Triggered uplink access (TUA) , one or more STAs transmit HE TB PPDUs simultaneously after receiving the trigger frame sent by HE AP. But the transmission of the trigger frame is contention-based, therefore the uplink access is not strictly scheduled.

## Slide 5: Channel Access Method to be optimized
What needs to be considered
  Different transmission requirements of the current and future applications especially including virtual reality or augmented reality, gaming, remote office and cloud computing should be satisfied.
  Because Wi-Fi uses the unlicensed spectrum the interference from OBSS and other sources would usually exist, therefore how to avoid or reduce the impact of the inference on the scheduled transmission is of vital importance.
  Backward compatibility and coexistence with legacy channel access methods would guarantee the STAs operating with different access methods operate in the same BSS or coordinated BSSs.

## Slide 6: Multi-channel Access Method
PHY1
PHY2
Contention-based Channel Access
AP
RF a
@Band1
RF b
@Band2
Scheduled Channel Access
RF a
@Band1
RF b
@Band2
MAC1
Coordinator
MAC2
MAC1
MAC2
PHY1
PHY2
STAs
Service Classifier
Contention-based Channel Access
Scheduled Channel Access
Service Classifier
Coordinator
Two functional modules with different access methods are used respectively to handle the data with different types of services, which are real-time and non-real-time applications.
The functional module of Scheduled Channel Access is responsible for the scheduled transmission of the data of real-time applications through the schedulable TXOPs (such as CAPs) from multi-band channels.
The functional module of Contention-based Channel Access is responsible for the best-effort transmission of the data of non-real-time applications mainly through the CSMA TXOPs from multi-band channels.

## Slide 7: Multi-Channel Access Method
Channel@Band1
AP
Channel@Band2
STAs
CSMA TXOPS
Scheduled MSDUs
MSDUs through contention-based access
CAP
TXOPi
TXOPj
TXOPi
TXOPj
TXOPi
TXOPj
TXOPi
TXOPj
TXOPi: TXOP allocated for Service i of STA1
CAP
CAP
CSMA TXOPS
CSMA TXOPS
CAP
TXOPi
TXOPj
Channel@Band1
Channel@Band1
TXOPj: TXOP allocated for Service j of STA2
MSDUs from real-time applications are scheduled for transmission during the CAPs (Controlled Access Phase) of multi-band channels; MSDUs from non-real-time applications can be transmitted during the CAPs or CSMA TXOPs of multi-band channels.
For MSDUs transmitted in the CAPs of one channel , the duplicates of the MSDUs can also been transmitted in the CAPs of other channels at the same time in order to increase the reliability of the transmission of the MSDUs at scheduled time.

## Slide 8: Conclusions
Current channel access methods need to be optimized to reduce worst-case latency and jitter and enhance the reliability of the data transmission of real-time applications.
Multi-band/Multi-channel access method uses the schedulable TXOPs (such as CAPs) from multi-band channels to transmit data of real-time applications so as to to increase the robustness of the transmission of the MSDUs at scheduled time.

## Slide 9: References
11-18-1231-06-0eht-eht-draft-proposed-par, 802.11 EHT Proposed PAR
11-18-1233-07-0eht-eht-draft-proposed-csd, IEEE 802.11 EHT draft Proposed CSD
IEEE P802.11ax D4.1

## Slide 10
Thank you!