## Slide 1: SIG-A Changes for Ranging NDP
Date: 2019-06-12
Authors:

## Slide 2: Problem in SIG-A with Ranging NDP
Repetition of HE-LTFs
  Pre-11az STAs will decode LSIG length
  Compare with NSTS in SIG-A
  Interpret extra HE-LTFs as Data field
  Will also affect 11ax based sniffers
Desirable to have 11az Wave 1 devices with minimal PHY changes
  Will potentially ignore NDPs with repeated HE-LTFs
  Not easy to link PHY processing to parameters received in NDP-A

## Slide 3: Solution
Modify SIG-A NSTS
  Include repetitions of non-secure HE-LTFs in SIG-A NSTS
  Non-secure HE-LTFs can be limited to 8 to fit SIG-A NSTS subfield
    Typically used for 1x1 and 2x2 STAs to improve SNR
    If repetition is a 2-power, fits P matrix
  Simply change interpretation
    Instead of thinking of a N_STS=2 with LTF_REP=2 of two 2x2 P-matrices stacked
    Interpret as first two columns of 4x4 P-matrix
    N_STS=4 with zero power on 3rd and 4th stream
    Still “correct” use of NSTS subfield by 11ax standard

## Slide 4: Additional Enhancements
Most subfields in HE SIG-A not used in HE NDPs
  Could reuse some subfields to explicitly encode
    True N_STS
    LTF_REP
  Example
    MCS not used for NDPs (4 bit)
    DCM not used (1 bit)
    Coding not used (1 bit)

## Slide 5: Strawpoll I
Do you support to limit the total number of HE-LTFs in non-secure HE Ranging NPDs to a maximum of 8?
Yes: No: Abstain:

## Slide 6: Strawpoll II
Do you support to change the NSTS encoding in HE SIG-A for HE Ranging NPDs, to include all non-secure HE-LTFs, including repeated HE-LTFs?
For example: a N_STS=2 and N_REP=2 would encode the NSTS subfield as if there were 4 spatial streams.
Yes: No: Abstain:

## Slide 7: Strawpoll III
Do you support to reuse some of the HE-SIG-A field in HE Ranging NDPs to encode the true N_STS and N_REP?
For example, use MCS, DCM, coding subfields.
Yes: No: Abstain: