## Slide 1: Preamble Design Harmonization
Date: 2019-06-07
Authors:
Name | Affiliations | Address | Phone | Email
Sameer Vermani | Qualcomm |  |  | 
Alice Chen |  |  |  | 
Bin Tian |  |  |  | 
Menzo Wentink |  |  |  | 
Youhan Kim |  |  |  | 
Notes: September 2012

## Slide 2: Preamble for EHT: Desirable Traits
High level design goals for EHT preamble
  Minimal design burden and easy implementation
  Good classification performance
  Enough bits to accommodate new EHT features
  Desire to solve the auto-detection issue for multiple standards starting with EHT, together
Necessitates
a paradigm
shift

## Slide 3: Traditional 802.11 auto-detection
Every new standard after 11a has been introducing new auto-detection markers
  11n
    Q-BPSK rotation on symbol after L-SIG
  11ac
    Q-BPSK rotation on the second symbol after L-SIG
    L-SIG length to be a multiple of 3
  11ax
    RL-SIG
    Non-multiple of 3 length in L-SIG
Problem with this approach
  The auto-detection scheme takes up spec development time in every 802.11 generation
  The classification engine keeps getting more and more complicated

## Slide 4: Preamble Design Harmonization across Generations
Starting with EHT, fix the preamble auto-detection marker across multiple 802.11 generations
  Maintain a common auto-detection signature  Need to maintain a common structure for a few symbols after L-SIG, for multiple 802.11 generations
Classification of future generations based on a PHY version identifier field (e.g., 3-4 bits) in the PHY header
  Value of the version identifier field differentiates between EHT and future standards
  Same auto-detection method can be used for all standards starting with EHT
Benefit: The auto-detection problem is solved for multiple 802.11 generations together
Legacy preamble
(may include RL-SIG)
Common structure for EHT and beyond
802.11be preamble
New PHY header
New SIG contains a
PHY Version Identifier
whose value identifies this as 11be

## Slide 5: Summary
We proposed a paradigm shift in the preamble design
  Harmonization of auto-detection for multiple standards, starting with EHT
    Introduce a PHY version identifier field in the PHY header

## Slide 6: Straw-poll 1
Do you agree to incorporate a PHY version identifier field as one of the fields in the EHT preamble?
  The intent is to solve the auto-detection problem of multiple 802.11 generations together
  Size of this field is TBD