## Slide 1: NDP Power Control for EVM
Date: 2019-06-11
Authors:

## Slide 2: Need for Power Control
Trade-off between Tx power and Tx EVM
  In any wireless communication
    Especially OFDM in WiFi, has large peak-to-average power ratio (PAPR)
    Needs power amplifier to back off more (so peaks avoid non-linear region)
  Maximizing Tx power usually reduces signal quality
    Typically sacrifice back-off
    Power amplifier will go (more often) into non-linear region
  Tx signal distortion is measured as Error Vector Magnitude (EVM)
    Typical range -10 to -30 dB
    WiFi’s 11ax has increased EVM range (1024 QAM, MU-MIMO, etc)

## Slide 3: Typical Approach Based on ACK
Most WiFi Packets are acknowledged
  If no ACK is received, packet was most likely lost
  Typically due to insufficient SINR at receiver to decode packet
  Required SINR to decode a packet depends on the Modulation and Coding Scheme (MCS) used
  Definition of receiver sensitivity maps required SINR for each MCS
  Given required SINR
    Maximize Tx power
    Keeping EVM below required SINR (reduces SINR by at most 3 dB)
  If packet is lost, drop MCS (assumes SINR is fixed) and adjust Tx power

## Slide 4: EVM on Channel Sounding Packets
Channel Sounding
  In WiFi uses Null Data Packets (NDP)
  No data in packet, no frame check sequence (FCS)
    There is no “correct” reception of NDP
    SNR will gradually change quality of channel estimates (no cut-off)
  To set Tx power and EVM correctly, transmitter needs to know the pathloss or get some other feedback (to replace the ACK)
Estimate pathloss
  Receiver can measure RSSI, but needs to know Tx power

## Slide 5: Effect of EVM on SINR
Effective Signal-to-Interference+Noise Ratio (SINR)
  Received power (Tx power minus path loss )
  EVM is part of the interference ()
  Other interference and receiver thermal noise
  For example at
    dBm
    dB
    dBm
    dB
    SNR = 19.6 dB (dominated by Tx EVM)

## Slide 6: Optimize EVM in Non-TB Ranging
Each STA transmits one data packet and one NDP
  Best to measure RSSI of NDP packets
  Pathloss is symmetric (assume tx/rx antenna gain symmetric)
  Data packets could either include
    RSSI (of some previous NDP)
    Tx power level of NDP

## Slide 7: Proposal
Add Tx power in NDP-A
  Reuse format of trigger frame “AP Tx Power” subfield is 6 bit, mapping values of 0:60 to -20:40 dBm; would have to add an extra “STA Info” 32 bit, similar to SAC
  Alternatively only use 4 MSB of “AP Tx Power” subfield, mapping 0:4:60 to -20:4:40 dBm, can fit into 4 reserved bits in “STA Info SAC”, which would then be always present

## Slide 8: Proposal (cont.)
Add RSSI in LMR
  7 bits (0:127)
  Map to 0:-1:-127 dBm RSSI
Alternatives
  Add Tx Power
  Add pathloss (Tx Power – RSSI)
 | Category | Public Action | Dialog Token | ToD |  | ToA | ToD Error | ToA Error | RSSI
Octets: | 1 | 1 | 1 | 6 |  | 6 | 1 | 1 | 1
 | CFO Parameter | Secure LTF Parameter (optional) | AoA Feedback (optional) |  |  |  |  |  | 
Octets: | 2 | 13 | 9 |  |  |  |  |  | 

## Slide 9: How to Set EVM at Tx Side
Tx side can control EVM
  Maps Tx Power to EVM
  Some dependence on modulation used
How to optimize SINR?
  Tx side does not know receiver noise figure
  Related to receiver sensitivity
Options
  Receiver shares N0 in negotiation

## Slide 10: Strawpoll I
Do you support to add subfields in Ranging NPD-A and LMR to facilitate tx-power and EVM optimization in Non-TB Ranging?
Yes: No: Abstain:

## Slide 11: Strawpoll II
Do you support to add the AP Tx Power subfield in the Ranging NPD-A as presented in Option
Option I (6 bits) Option II (4 MSBs)
Option III (Appendix)
I: II : III: Abstain:

## Slide 12: Strawpoll III
Do you support to add the following field in the LMR frame from non-TB Ranging
Option I: AP Tx Power
Option II: RSSI
Option III: Pathloss
I: II : III: Abstain:

## Slide 13: Appendix
Alternatively place Tx Power on top of “Offset”
  Only used in TB Ranging