## Slide 1: LC-optimized PHY proposal for TGbb
Date: 2019-07-01
Authors:

## Slide 2: Abstract
The submission presents the proposal of an LC-optimized PHY for TGbb based on G.9991 PHY 1 [1].

## Slide 3: Characteristics of LC PHYs
LC requires a non-negative and real-valued baseband-signal.
Bipolar signals can be turned non-negative by adding a DC-bias before transmission.
It is removed by using a high-pass filter before reception.
Photo-diode
TX
DSP
Driver & LED
DC
+
optical
channel
RX
DSP
High-pass

## Slide 4
Complex OFDM-baseband signals are real-valued after up-conversion to the carrier frequency fc.
For LC, one can change fc to a low carrier (“low IF”), yielding a real-valued baseband signal.
Reuse of any OFDM PHY for LC
Re(.)
LED
IFFT
CP
Up-con-
version
fc
Data

## Slide 5
RF frontend up-converts baseband signals onto e.g. fc=2.4 GHz.
LC frontend up-converts baseband onto low IF e.g. fc=BW/2 (+ Δ).
  Δ0 for analog upconversion
  Δ=0 for oversampled digital upconversion
Allows reuse of existing 802.11 PHYs for LC

## Slide 6: Why an optimized PHY is needed for LC?
In RF NLOS channels, bit-interleaved coded modulation (BICM) works well. BICM is the concept behind all existing 802.11 OFDM PHYs.
BICM first creates redundancy and then permutes the bits in a code-word randomly over all subcarriers. In a rare fading event, lost bits can be repaired by the FEC using the redundant bits.
LC NLOS channels are 1st order low-pass in general [1], therefore the concept of BICM is likely to fail. Assuming 100 MHz bandwidth and 20 MHz cut-off frequency, 80% of bits are lost.
RF
LC

## Slide 7: Use G.9991 as realize LC-optimized PHY
LC-optimized PHY needs adaptive bitloading
  Seamless operation in both, LOS and NLOS channel conditions
802.11 has discussed but never supported adaptive bitloading
  Adaptive bitloading brings additional complexity and overhead
Ways to bring adaptive bitloading into 802.11
  Integrate G.9991 as LC-optimized PHY under 802.11 MAC
    G.9991 is already used in many LC demos and early products
    Next-gen G.9991 will have 1 GHz bandwidth (based on G.hn2 coax) - use of lasers
  Integrate adaptive bitloading in next-gen 802.11 RF PHY  SG EHT
    Next-gen RF PHY is limited to 320 MHz and unlikely revised for LC

## Slide 8
802.11 MAC could integrate existing 802.11 and LC-optimized PHY
Use existing and LC-optimized PHY under 802.11 MAC

## Slide 9: Straw Poll from May 2019 meeting
Are you interested in further presentations discussing the potential suitability
of the G.9991 PHY for 802.11bb?
Y / N / A: 6 / 0 / 5

## Slide 10: Outline
LC-optimized waveform
  1.1. Main characteristics
  1.2. Forward Error Correction
  1.3. Adaptive Bitloading
  1.4. OFDM modulator
PPDU format
  2.1. Synchronization header
  2.2. Physical layer header, HCS
  2.3. MIMO CE symbols
  2.4. PHY payload
Preamble
CE
symbols
SHR
PHY header
HCS
MIMO CE symbols
PHR
PSDU
PHY payload
SISO
optional MIMO

## Slide 11: 1. LC-optimized waveform
Based on G.9991 aka “G.vlc”
  ITU-T Recommendation (Q18/15 “In-premises networking”)
  G.vlc project started in 2015, was approved on 01/04/2019
  G.9991 is largely based on G.9960/61 (aka “G.hn”)
  Leverage the highly flexible OFDM engine provided by G.hn
Use of G.9991 PHY 1 for light medium approved by ITU-T and tested in devices
  DCO-OFDM & frequency-upshift with fupshift=B/2, B is bandwidth defined by band plan
  G.9991 brings bitloading capability for LC-optimized waveform
Key is reuse of the existing waveform
  Corresponding to PMA & PMD from G.9991
  Existing LC prototypes from several vendors prove functionality and high performance
  Reuse of G.9991 implies no compromise for the performance

## Slide 12: 1.1. Main characteristics of G.9660 PHY
System architecture and PHY layer
  LDPC Forward Error Correction (FEC)
  Windowed OFDM (Orthogonal Frequency Division Multiplexing)
  QAM modulation up to 12 bit/s/Hz
  ACK-based selective retransmissions
  AES128 encryption algorithm
  MIMO-capable

## Slide 13: Parameters
Area | Value | Notes
Modulation type | DCO-OFDM | Configurable OFDM parameters (cyclic prefix, per-subcarrier PSD, etc)
Max modulation | Up to 12 bits/subcarrier | Each sub-carrier is modulated with a different number of bits, depending on SNR (Bitloading), Odd constellations are optional
FEC | LDPC | FEC rates (1/2, 2/3, 5/6, 16/18, 20/21) and block sizes dynamically selected
Spectrum | 5-200 MHz is used for LC | Individual sub-carriers can be notched to coexist with other services
Bandplans | 50, 100, 200 MHz, … | 256,512 and 1024 subcarriers respectively, fully interoperable
Subcarrier spacing | 195 kHz (LC) | Sub-carrier spacing optimized for the expected delay spread in LC medium
Notches | Yes | Partial spectrum can be notched
Min SNR for frame detection | -3 dB | 
Bidirectional traffic | Yes | Specific PHY frame for bidirectional traffic

## Slide 14: Functional model
Reuse the lower parts from G.9991 PHY 1
  G.9991 is a specific profile for LC based on G.9960
  Reuse only PMA and PMD
Integrate into 802.11 MAC
  Proposed interface lies at the a-reference point
G.9960
G.9961

## Slide 15: G.9960 PHY description

## Slide 16: Transmission frame format in G.996x vs. 802.11bb
Preamble
Header
ACE
symbols
Payload
Phy Frame
MPDU
ADPU
ADPU (data) or LCDU (LLC control)
LLC frame
LFH
LLC frame f
LLC frame f+1
….
Padding
LLC frame block
Segment h
Segment h+1
Segment h+2
Segment h+3
Segment h+4
LPDU
Segment h+1
LPH
CRC
LPDU h
LPDU h+1
LPDU h+2
LPDU h+3
LPDU h+4
Application
Entity
Ethernet frame
LPDU size = FEC block size (120 or 540 bytes)
Pad
DLL layer
PHY layer
APC sublayer
LLC sublayer
MAC sublayer
LLC frame g
Encrypted LLC frame has also CCMP header and MIC fields
Replaced by 802.11 MAC
From G.9960 PHY
Notes: In the transmission direction, application data primitive (ADP) sets enter the DLL from the AE through the A-interface. Every incoming ADP set meets the format defined by the particular application protocol; for an Ethernet type AE, the ADP set has one of the standard Ethernet formats. Each incoming ADP set is converted by the APC into APC protocol data units (APDUs), which include all parts of the ADP set intended for communication to the destination node or nodes. The APC also identifies ADP classification primitives (e.g., priority tags), which can be used by the LLC to support QoS requirements assigned to the service delivered by the ADP. Furthermore, the APC is responsible for establishing flows of APDUs between peer APCs and assigning one or more queues for these flows according to the classification information associated with each APDU.
The APDUs are transferred to the LLC across the x1 internal reference point, which is independent of both application and medium. Additionally, LLC receives management data primitives from the DLL management entity intended for LLC control frames, which are mapped into Link Control Data Units (LCDU). The LLC is responsible for establishing flows of LCDU (control frames) between peer LLCs.
In the LLC sublayer, the incoming APDU and LCDU are converted into LLC frames and might be encrypted using assigned encryption keys. LLC frames are subject to concatenation and segmentation. Segments are transformed into LLC Protocol Data Units (LPDUs) by adding an LPDU header (LPH) and CRC. The size of the segment shall be equal to the size of the FEC block minus the size of the LPDU header and minus the size of the LPDU check sequence. LPDUs are then passed to the MAC across the x2 reference point. The LLC is responsible for retransmission and relay operations too.
The MAC sublayer is responsible for concatenating LPDUs into MAC Protocol Data Units (MPDUs) and then conveying these MPDUs to the PHY in the order determined by the LLC (scheduling, using number of transmission queues) and applying medium access rules established in the domain by the DM.
In the PHY layer, a PHY frame consists of a preamble, header, additional channel estimation (ACE) symbols (optional field, its presence is frame type dependent) and payload. The Payload includes one MPDU composed of one or more LPDUs (LLC Protocol Data Unit). Each LPDU carries a segment of the transmitted data, a header identifying the carried segment, and the CRC to detect “errored” LPDU for selective retransmission.

## Slide 17: 1.2. Forward error correction
FEC allows to recover messages that have been affected by errors
LDPC (Low-Density Parity Check) are used
  LDPC works better than other alternatives over a wide range of media (powerline, phoneline, coaxial and LC) and operation points (both low and high block error rates)
  LDPC is the only code that works well at very high data rates (hundreds of Mbps) because it is easier to parallelize
  LDPC is used by many other very high data rate standards such as 10GBase-T Ethernet (802.3an), WiMAX (802.16e), (802.11n,ac,ax) and 5G NR
  G.9960 FEC comprises Scrambler, LDPC encoder and Segmentation to OFDM symbols

## Slide 18: Scrambler
All data starting from the first bit of the PHY-frame header and ending by the last bit of the payload are scrambled.
Using a pseudorandom sequence generated by the linear feedback shift register (LFSR) with the polynomial p(x) = x23 + x18 + 1.
There are different ways to initialize the LFSR for header and payload data.

## Slide 19: G.9960 LDPC code (I)
3 block sizes: 168, 960 and 4320 bits
3 mother code rates: 1/2, 2/3 and 5/6
Apart from the mother codes, 2 more rates are available by puncturing 5/6 rate (16/18 and 20/21)
Puncturing is used to generate higher rates by simply discarding some of the encoded bits. Puncturing is applied to both payload and parity bits.
Unpuncturing consists of inserting a zero-valued LLR in those codeword positions that were punctured at the encoder
Block length (bits) | Codeword length (bits) | Rate | Expansion Factor
168 | 336 | 1/2 | 14
960 | 1920 | 1/2 | 80
960 | 1440 | 2/3 | 60
960 | 1152 | 5/6 | 48
960 | 1080 | 16/18 | 48
960 | 1008 | 20/21 | 48
4320 | 8640 | 1/2 | 360
4320 | 6480 | 2/3 | 270
4320 | 5184 | 5/6 | 216
4320 | 4860 | 16/18 | 216
4320 | 4536 | 20/21 | 216

## Slide 20: G.9960 LDPC code (II)
All the parity-check matrices in their compact form have 24 columns; depending on the rate, they have 12 rows (1/2), 8 rows (2/3) and 4 rows (5/6)
The parity-check matrices for the 1/2 and 2/3 rate are quite sparse. However, the ones for the 5/6 rate are pretty dense (see the examples below).
N = 1920 ; R = 1/2
N = 5184 ; R = 5/6

## Slide 21: G.9960 LDPC performance: pre-FEC BER vs. post-FEC BLER
code rate 1/2 allows robust transmission for small block size (header)
code rate 5/6 maximizes the throughput for large block size (payload)
further resilience is reached through fast repetition
P. W. Berenguer et al., "The benefit of frequency-selective rate adaptation for optical wireless communications," 2016 10th International Symposium on Communication Systems, Networks and Digital Signal Processing (CSNDSP), Prague, 2016.

## Slide 22: G.9960 LDPC and Shannon bound
Points marked with “o” in the curve of each code rate represent 4QAM, 16QAM, 64QAM, 256QAM and 1024 QAM constellations respectively
minimal SNR for BLER 1e-3
BPC | FEC RATE |  |  |  | 
 | 1/2 | 2/3 | 5/6 | 16/18 | 20/21
12 | 24 | 28.6 | 33.6 | 35.6 | 38.2
10 | 19.9 | 24.1 | 28.3 | 30.1 | 32.5
8 | 15.6 | 19.3 | 22.9 | 24.6 | 26.7
6 | 11.3 | 14.5 | 17.6 | 19 | 21
4 | 6.75 | 9.4 | 12 | 13.2 | 15
3 | 4.1 | 6.5 | 8.9 | 10 | 11.7
2 | 1.44 | 3.5 | 5.7 | 6.7 | 8.4
1 | -1.5 | 6 | 2.7 | 3.7 | 5.4

## Slide 23: Repetition encoding

## Slide 24: 1.3. Adaptive Bitloading
PSD
(dBm/Hz)
f(MHz)
TX spectrum
RX spectrum
in STA #1
RX spectrum
in STA #2
Noise spectrum
Noise spectrum
SNR at
STA #1
SNR at
STA #2
Bitloading
for STA #1
Bitloading
for STA #2
Signal Received
by STA #1
Signal Received
by STA #2
Different STAs are using different modulations!!
Adaptive bitloading algorithm
Tone mapping
Constellation encoding
Frequency-domain transmit power shaping
Constellation scrambling
data
(from FEC)
symbols/subcarrier
(to OFDM modulator)
July 2019

## Slide 25: Benefits of G.9960 bitloading mechanism
System is constantly measuring SNR between all nodes (in both directions) and adapting the bit-loading in real-time.
In this way, the system becomes resilient against any problems in the medium.
  Works well despite severe frontend impairments (high-pass and low-pass, non-linear LED and driver characteristics).
  Works well despite severe multipath propagation in some LC channels (LOS+NLOS).
STAs can use their best possible modulation allowed by own SNR.
  No need to add SNR margin to ensure far-away STAs get zero packet-loss.
July 2019

## Slide 26: Tone mapping
Tone mapping is based on bit allocation tables (BATs)
Transmitter-defined BATs are typically pre-defined (same modulation on all subcarriers).
Runtime BATs can be defined by the transmitter or receiver (variable modulation on each subcarrier) where number of bits depends on signal-to-noise ratio (SNR) on each subcarrier.
Unloaded subcarriers are loaded with a pseudorandom binary sequence using linear feedback shift register (LFSR) with the polynomial p(x) = x23 + x18 + 1.
BAT_ID | Type | Content
0 | predefined | uniform 1-bit loading on all subcarriers
1 | predefined | uniform 2-bit loading on all subcarriers,
2 to 7 | predefined | reserved
8 to 31 | runtime | see below

## Slide 27: Constellation encoding
b=1
b=2
b=3
b=4 (first quadrant)
Square constellations for even number of bits (b=2, 4, 6, 8, 10, 12)
  mandatory at Tx and Rx
Cross-shaped constellations for odd number of bits (B= 1, 3, 5, 7, 9, 11)
  mandatory at Tx, optional at Rx

## Slide 28: Frequency-domain transmit spectrum shaping
Achieved by a scaling factor tss defined on each subcarrier.
Set by the transmitter between 0 and -30 dB in steps of -0.5 dB.
Allows vendors to statically pre-distort the transmitted signal and adapt it to non-ideal driver + LED characteristic
Allows dynamic fine tuning of BER per subcarrier via adaptive power loading

## Slide 29: Constellation scrambling
Constellation scrambling is useful to randomize interference from other APs/STAs.
The phase of constellation points is shifted according to the PRBS generated by a LFSR by using the polynomial g(x) = x13 + x12 + x11 + x8 + 1.
The LFSR is advanced by two bits for supported and masked subcarriers. The two LSBs of the LFSR are taken to determine the phase shift of the constellation scrambler.
LFSR output |  | Phase shift (rad)
s2 | s1 | 
0 | 0 | 0
0 | 1 | π/2
1 | 0 | π
1 | 1 | 3 π/2

## Slide 30: Bitloading example
PSD
(dBm/Hz)
TGbb channel model for industrial wireless
Channel frequency responses seen by the different receiver photodiodes D1-D8
Channel frequency response for receiver at D2
Shows strong fade at around 65 MHz  Fewer bits are loaded around this frequency
Frequency-selective transmit power shaping makes BER on all subcarriers equal, i.e. FEC faces AWGN-like error statistics despite multipath fading in the channel
P. W. Berenguer et al., "The benefit of frequency-selective rate adaptation for optical wireless communications," 2016 10th International Symposium on Communication Systems, Networks and Digital Signal Processing (CSNDSP), Prague, 2016.
July 2019

## Slide 31: 1.4. OFDM modulator
Start is complex OFDM waveform with IFFT and CP
Windowing avoids EMI over phone and power line, not used for coax and LC
Frequency upshift to realize real-valued passband signal
DC-offset realizes non-negative waveform for POF, LC

## Slide 32: Numerology for LC-optimized PHY
Waveform |  |  | DC biased OFDM |  | 
Subcarrier Spacing FSC |  |  | 195.3125 KHz |  | 
OFDM Symbol Duration |  |  | 5120 ns |  | 
Cyclic Prefix length for header (payload) |  |  | 1.280 (k*160) ns, k=1…8 |  | 
Number of bits/subcarrier |  |  | 1, 2, 3, 4, 5, 6, 7, 8, 9, 10, 11, 12 |  | 
FEC, Information Block Size |  |  | LDPC, 21, 120 or 540 bytes |  | 
Code Rates |  |  | 1/2, 2/3, 5/6, 16/18, 20/21 |  | 
Bandplan / MHz | Clock cycle / ns | Frequency up-shift FUS / MHz | N (Nsupported) / clock cycles | Gross data rate / Mbit/s | 
 |  |  |  | Min. | Max.
50 | 20 | 25 | 256 (245) | 23 | 530
100 | 10 | 50 | 512 (501) | 47 | 1084
200 | 5 | 100 | 1024 (1013) | 96 | 2192

## Slide 33: IDFT
IDFT converts N complex input symbols Zi,l into N complex output samples Xn,l.
The input symbols Zi,l contain the ith data symbol mapped onto the ith modulated subcarrier of the lth OFDM signal, where i = 0, 1, … N–1 is the subcarrier index and l is the number of the OFDM symbol.
N-point IDFT is given by
.
The value of Zi,l for masked subcarriers (MSC) is set to 0.

## Slide 34: Cyclic prefix
The CP provides a guard interval between adjacent OFDM symbols to protect against inter-symbol interference (ISI).
The CP is implemented by prepending the last NCP samples of the IDFT output to its output N samples. The first sample is the IDFT output sample N-NCP. The last sample of the CP is the IDFT output sample N-1. The next sample is the IDFT output sample 0.
Total OFDM symbol duration is NW = N + NCP samples. The value of NCP varies during a frame.
In the header and first two symbols after the header, NCP=NGI-HD=N/4. All the rest of the payload has the same value NCP=NGI.

## Slide 35: Frequency upshift
Frequency up-shift moves the spectrum of the transmit signal by FUS = m*FSC where m=N/2. Real and imaginary components of the signal are given by
The transmitted real-valued output signal is given by
where Xn/p is Xn after interpolation with factor p being equal to or higher than 2.
.

## Slide 36: 2. PPDU structure
SISO = single-input single-output
MIMO = multiple-input multiple-output
SHR = Synchronization header
CE = Channel estimation
PHR = Physical layer header
HCS = Header check sequence
PSDU = PLCP Service Data Unit
PLCP = Physical layer convergence protocol
Preamble
CE
symbols
SHR
PHY header
HCS
MIMO CE symbols
PHR
PSDU
PHY payload
SISO
optional MIMO

## Slide 37: 2.1. Synchronization header (SHR)
Preamble time domain generation
Synch preamble
CE symbols
N1 = 10
N2 = 4
N3 = 2.5
b = 0 for coax, LC

## Slide 38: Synch preamble
The synch preamble consists of two sections.
  First section comprises 10 repetitions of an OFDM symbol S employing subcarrier spacing 4 × FSC, where FSC denotes the subcarrier spacing.
  The second section comprises 4 repetitions of the inverted symbol -S.
The synch preamble uses the subcarriers with indices 4, 8, 12, 16, …, N-4.
  At first, bit sequence of all ones is mapped using the 1-bit constellation.
  Next, the LFSR generator of the constellation scrambler is initialized as 16E616=1011011100110. The LFSR is advanced by two bits per subcarrier.
  The output of the mapper is rotated using the two LSBs of the LFSR.
The resulting constellation sequence is finally fed into the OFDM modulator.

## Slide 39: CE symbols
The CE sequence is usded for detection of the header.
  It comprises 2.5 repetitions of an OFDM symbol S employing subcarrier spacing 1 × FSC, where FSC denotes the subcarrier spacing.
  The number of repetitions is a non-integer number to indicate that two OFDM symbols are used so that the CP is the same as in the PHY header, i.e. NCP=NGI-HD=N/4.
In the channel estimation preamble, all subcarriers are used.
  A bit sequence of all ones is mapped using the 1-bit constellation.
  Next, the LFSR generator of the constellation scrambler is initialized as 110516= 1000100000101. The LFSR is advanced by two bits for all subcarriers.
  The output of the mapper is rotated using the two LSBs of the LFSR.
The resulting constellation sequence is finally fed into the OFDM modulator.

## Slide 40: 2.2. PHY header
Core part: Common to all PHY frames
Frame-type specific: Specific for each PHY frame type
Domain identifier
Frame type
Source node
Destination node
Header segmentation indication
Extended header Indication
Duration
Multicast indication
Frame-specific fields
Header check sequence

## Slide 41: Header check sum (HCS)
The HCS uses CRC-16.
  It starts with LSB of first field and ends with the MSB of last field of PHY frame header.
The HCS is computed using the following generator polynomial:
G(x) = x16 + x12 + x5 + 1
  The value of the HCS shall be the remainder after the contents (treated as a polynomial where the first input bit is associated with the highest degree, XPHYH–17, where PHYH is the header length in bits, and the last input bit is associated with X0) of the calculation field is multiplied by x16 and then divided by G(x).
The HCS field is transmitted starting with the coefficient of highest order term.
  The HCS bits shall be processed in the transmitted order.
The registers shall be initialized to all ones.

## Slide 42: Header encoding
The size of the FEC code word is 168 bit and coding rate is ½.
The header repetition encoder (HRE) works as follows
  The FEC codeword is first copied M times, where M = ceiling (kH/NFEC), kH is the number of bits to be loaded on to the OFDM symbol carrying the header (i.e. 336).
  The first encoded header block is formed by concatenation of M copies of the header FEC encoder output. The bits (bi) within each codeword are cyclically shifted by 2 bits as follows
    1st copy is {b0, b1, …, bNFEC–2, bNFEC–1}.
    2nd copy is {b2, b3, …, bNFEC –1, b0, b1}.
    3rd copy is {b4, b5, …, bNFEC–1, b0, b1, b2, b3}.
    Mth copy, where M > 3, is {b(2×M–2), b(2×M–1), …, bNFEC–1, b0, b1, …, b(2×M–4), b(2×M–3)}.
  There is a similar rule if there is a second encoded header block, se G.9660.

## Slide 43: Header segmentation
The encoded header block is segmented into symbol frames.
Header symbol frames are passed to the adaptive bitloading using a fixed constellation of 2 bits per subcarrier.
The encoded header block is segmented into D = 1, 2 OFDM symbol frames.
  First kH bits of the first encoded header block is mapped into the first symbol frame, so that b0 is transmitted first.
  If D = 2, the first kH bits of the second encoded header block is mapped into the second symbol frame, so that bNFEC/2 is transmitted first.
  The rest of the bits of the first and the second encoded header blocks are discarded.

## Slide 44: 2.3. MIMO CE symbols
Motivation
LC can have many spot lights in one room that could be considered as remote optical front ends controlled by the same AP. The number of LEDs should be in the order of 100 and even more. The 802.11 way of defining MIMO CE symbols would 100s of MIMO reference symbols which is not adequate.
We can pack MIMO reference symbols denser in the frequency domain.
Not all subcarriers must contain pilots to identify the channel to one LED. Only every N/NCP=5120 ns/ (k*160) ns = 32/kth subcarrier actually needs a pilot, as there can be no more taps in the channel than samples in the guard interval.
The idea is a comb of equally-spaced subcarriers used as pilots. A cyclic shift in the frequency domain applies in order to identify different LEDs.

## Slide 45: Orthogonal combs with frequency reuse
Each combs identifies another LED. One comb is reserved for noise estimation.
The channel is interpolated between non-zero subcarriers.
Classical frequency reuse schemes are applied for pilot assignment to LEDs.

## Slide 46: Basic definition of MIMO CE symbols
Construction of MIMO RS starts from the LFSR also used in the SHR.
RS for the first LED use the subcarriers with indices Δ, 2Δ, 3Δ, 4Δ, …, N-Δ, where Δ is the comb spacing. The value of Δ is defined by higher layers taking the Δ≤N/NCP into account.
  A bit sequence of all ones is mapped onto used subcarriers using the 1-bit constellation.
  The LFSR generator of the constellation scrambler is initialized as 16E616=1011011100110.
  The LFSR is advanced by two bits per subcarrier. The output of the mapper is rotated using the two LSBs of the LFSR.
The resulting constellation sequence is finally fed into the OFDM modulator.
For CS≥1, a cyclic shift of the comb is performed so that subcarriers with indices CS, Δ+CS, 2Δ+CS, 3Δ+CS, 4Δ+CS, …, N-Δ+CS are used.
  By using a single RS, up to CSmax ≤Δ-1 streams or transmitters can be identified.

## Slide 47: MIMO CE for more than Δ-1 LEDs
The MAC layer will add more RSs for more streams or transmitters as indicated by NRS. In this way, up to NRS*(Δ-1) streams can be identified.
Decompose the identifier of the ith stream or transmitter as
i=a*(Δ-1)+b where b<Δ-1
The comb shift is then CS=b. The corresponding RS is now multiplied as a while with the entries in the ath row of the MxM Hadamard matrix HK where M=2K. HK is obtained by incrementing k from k=1…K as

## Slide 48: 2.4. PHY payload
The PHY payload is divided into sequential blocks of information bits, K bits per block each encoded by the FEC. The table shows valid values of K, block size NFEC, and code rate R.
  In normal mode (REP = 001 in PHY header), codewords are passed directly to the output.
  In robust mode, each FEC codeword is repeated REP times and concatenated at the output.
For more details on the sophisticated repetition scheme, see G.9660.
Block length (bits) | Codeword length (bits) | Rate | Expansion Factor
168 | 336 | 1/2 | 14
960 | 1920 | 1/2 | 80
960 | 1440 | 2/3 | 60
960 | 1152 | 5/6 | 48
960 | 1080 | 16/18 | 48
960 | 1008 | 20/21 | 48
4320 | 8640 | 1/2 | 360
4320 | 6480 | 2/3 | 270
4320 | 5184 | 5/6 | 216
4320 | 4860 | 16/18 | 216
4320 | 4536 | 20/21 | 216

## Slide 49: Summary
It is proposed in TGbb to integrate lower parts (PMA and PMD) from ITU-T Rec. G.9991 as new LC-optimized PHY under 802.11 MAC.
This PHY is also used by G.vlc and in IEEE P802.15.13 which use different MAC layer protocols. As these standards address different market segments, using the same PHY allows coexistence and interoperability between devices.
A detailed functional description was given, mostly based on G.9991 and G.9660 recommendations of ITU-T.
High performance is proven by numerous demos, prototypes and products from several vendors.
This slideset is followed by simulation results detailed in doc. 11-19/1054rx.

## Slide 50: References
[1] V. Jungnickel, V. Pohl, S. Nonnig and C. von Helmolt, "A physical model of the wireless infrared communication channel," in IEEE JSAC, vol. 20, no. 3, pp. 631-640, April 2002.
[2] V. Jungnickel, K.L. Bober, A. Paraskevopoulos, N. Serafimovski, H. Haas, “Proposed way forward on PHY in TGbb”, doc. 11-19/0388r0.
[3] K.L. Bober, M.Emmelmann, V. Jungnickel, A. Corici, D. Xiong; “LC- optimized PHY for TGbb”, doc. 11-19/0865r1.
[4] ITU-T G.9991 - https://www.itu.int/rec/T-REC-G.9991-201903-P
[5] ITU-T G.9660 - https://www.itu.int/rec/T-REC-G.9960
[6] P. Wilke Berenguer et. al.: The benefit of frequency-selective rate adaptation for optical wireless communications, IEEE CSBDSP 2016.
[7] https://www.photonics21.org/ppp-projects/workgroup-4/Eliot.php