## Slide 1: Tone Plan Discussion
Date: 2019-07-15
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinmin Kim |  |  |  | jinmin1230.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
In [1], three options for a 320MHz BW tone plan design were discussed
  Option 1 : Reuse the 11ax 80MHz tone plan four times
  Option 2 : Design a new 160MHz tone plan and repeat it twice
  Option 3 : Design a new 320MHz tone plan
In [2], new BW modes and their tone plan were proposed
  New BW modes: 320MHz, 160+160MHz
  Tone plan: Use HE160 in each PHY 160MHz subband
In this presentation, we further discuss new BW modes and tone plan designs

## Slide 3: Proposals
New BW modes
  320MHz, 160+160MHz
  240MHz, 160+80MHz
Tone plan designs
  Repeat the 11ax 80MHz tone plan for OFDMA tone plans in all new BW modes
  Define a new RU for SU (or MU MIMO using entire BW) tone plans in contiguous 240MHz, 320MHz and even in contiguous 160MHz

## Slide 4: New BW Modes
Two types of larger BW modes have many benefits
  Larger BW modes can increase the peak throughput and improve the transmit range at high PHY rates [1][2]
  Utilizing two larger BW modes (240MHz, 320MHz) in both SU and MU transmissions can provide better throughput (maximum 12% gain) and efficiency compared to using only the 320MHz mode [1]
  Considering incumbents in 6GHz, available channels may be restricted, and thus, adopting various BW modes may be more beneficial to channel availability
  Adopting two larger BW modes can give vendors a chance to consider various implementation choices
    For example, 240MHz / 320MHz / both BWs capable devices can be considered for better throughput than 11ax
Non-contiguous BW modes can enhance efficiency
  Other non-contiguous BW modes (e.g., 80+80+80+80MHz) may not be preferable from a hardware viewpoint
  For further efficiency, preamble puncturing can be utilized

## Slide 5: Tone Plan Designs (1/3)
Basically, we propose to repeat the 11ax 80MHz tone plan to build up OFDMA tone plans in all new contiguous / non-contiguous BW modes
  It guarantees that all 80MHz segments have the same tone plan which results in a simple hardware implementation regardless of the BW modes
  It can also give a chance to transmit data to HE and EHT STAs simultaneously in larger BWs which results in an efficiency and throughput enhancement
11ax 80MHz tone plan

## Slide 6: Tone Plan Designs (2/3)
For SU (or MU MIMO using whole BW) tone plans in the contiguous BW modes, we propose to define new RUs, for example as shown in the next slide
  Only EHT STAs can be assigned to 240/320MHz SU or MU MIMO transmission, and thus, we can use new RUs for them
  By using new RUs, throughput and efficiency can be further enhanced
    Assuming 16 SS transmission in 320MHz, a new RU can roughly achieve an additional 1Gbps* increase in peak rate compared to 4x996-tone RU
  We can also benefit from new RUs in the future extension
    In a much wider BW (> 320MHz), repeating 996-tone RU leads to too many null tones which can result in a throughput degradation
    Whereas by using these new RUs as one of the RUs in the future, more efficient OFDMA tone plans can be expected
996
5 null
996
5 null
23 null
996
5 null
996
5 null
23 null
23 DC
12 guard
11 guard
* Additional 1.294Gbps (3.37%) increase in peak rate when using 4068-tone RU with 16 pilots, MCS11, 0.8us GI and 16SS

## Slide 7: Tone Plan Designs (3/3)
New RU examples for SU (or MU MIMO using whole BW) tone plans
  320MHz
  240MHz
  160MHz
   The number of DC tones (as well as guard tones) needs to be further studied
4068 or 4066 or …
DC: 5 or 7 or …
12 left guard
11 right guard
3044 or 3042 or …
DC: 5 or 7 or …
12 left guard
11 right guard
2020 or 2018 or …
DC: 5 or 7 or …
12 left guard
11 right guard

## Slide 8: Summary
We have proposed new BW modes and tone plan designs
  New BW modes
    320MHz, 160+160MHz
    240MHz, 160+80MHz
  Tone plan designs
    Repeat the 11ax 80MHz tone plan for OFDMA tone plans
    Define a new RU for SU (or MU MIMO using entire BW) tone plans in contiguous BW modes

## Slide 9: SP #1
Do you agree to add the following text to the TGbe SFD?
  11be supports 320 MHz and 160+160 MHz PPDU
Y/N/A : //

## Slide 10: SP #2
Do you agree to add the following text to the TGbe SFD?
  11be supports 240 MHz and 160+80 MHz transmission
    Whether 240 / 160+80 MHz is formed by 80MHz channel puncturing of 320 / 160+160 MHz is TBD
Y/N/A : 25/0/10

## Slide 11: Motion #1
Move to add the following text to the TGbe SFD
  11be supports 240 MHz and 160+80 MHz transmission
    Whether 240 / 160+80 MHz is formed by 80MHz channel puncturing of 320 / 160+160 MHz is TBD
Moved by: Eunsung Park
Second:
Y/N/A :

## Slide 12: SP #3
Do you agree to add the following text to the TGbe SFD?
  For the OFDMA tone plan in 320MHz and 160+160MHz, 11ax 80MHz tone plan is duplicated four times
Y/N/A : //

## Slide 13: SP #4
Do you agree to add the following text to the TGbe SFD?
  For the OFDMA tone plan in 240MHz and 160+80MHz, 11ax 80MHz tone plan is duplicated three times
Y/N/A : //

## Slide 14: SP #5
Do you agree to add the following text to the TGbe SFD?
  TBD-tone RU is used for the SU PPDU transmission in contiguous 320MHz BW
  Note: This RU is not constructed from duplicating the 11ax 80MHz tone plan four times
Y/N/A : //

## Slide 15: SP #6
Do you agree to add the following text to the TGbe SFD?
  TBD-tone RU is used for the SU PPDU transmission in contiguous 240MHz BW
  Note: This RU is not constructed from duplicating the 11ax 80MHz tone plan three times
Y/N/A : //

## Slide 16: SP #7
Do you agree to add the following text to the TGbe SFD?
  TBD-tone RU is used for the SU PPDU transmission in contiguous 160MHz BW
  Note: This RU is not constructed from duplicating the 11ax 80MHz tone plan twice
Y/N/A : //

## Slide 17: References
[1] 802.11-19/0778r0 Consideration on 320MHz Bandwidth and 16 Spatial Streams
[2] 802.11-19/0797r0 320MHz Channelization and Tone Plan