## Slide 1: NGV Midamble Choice
Date: 2019-07-15
Authors:

## Slide 2: Introduction
In May meeting, Midamble has been agreed to be supported in 11bd [1].
Different channel condition and MCS level prefer different Midamble periods.
The choice of Midamble periods for 11bd is discussed in this contribution.

## Slide 3: Design of Midamble Periods
Number of Midamble periods:
  The more supported Midamble periods, the more transmitter/receiver complexity needs.
  More signaling bits are needed.
We think two periods can be a good number.
  One sparse period for lower MCSs or low-Doppler channel
  One dense period for higher MCSs or high-Doppler channel.
Simulations are followed to make the choice.

## Slide 4: Simulation Settings
10MHz DSRC channel @5.9GHz.
OFDM numerology: 11ac 20MHz DC2.
1x1-1ss, LDPC.
Pkt size: 300 bytes.
No impairments.
Ideal timing.
Goodput is the maximum achievable effective data rate.
Goodput(SNR, M) = maxMCS{Rate(MCS) * (1-PER(MCS, SNR, M))* M/(M+1)}
  M is the midamble period

## Slide 5: Rural LOS
Period 10 is good for all SNR/MCS range.

## Slide 6: Urban Approaching LOS
Period 10 is good for all SNR/MCS range.

## Slide 7: Urban Crossing NLOS
Period 10 is good for SNR up to 20dB.
Period 5/6/7 are good for high SNR

## Slide 8: Highway LOS
Period 10 is good for SNR up to 19dB.
Period 5/6 are good for high SNR

## Slide 9: Highway NLOS
Period 10 is good for SNR up to 17dB.
Period 4/5 are good for high SNR.

## Slide 10: Summary
In this contribution, we simulated the performance of 11bd 10MHz PPDU with different Midamble periods.
The results show that two periods is good tradeoff between complexity/signaling and performance.
Period 10 and 5 is a good candidate pair for the two periods.

## Slide 11: Reference
[1] Dongguk Lim and etc., “Performance evaluation of Midamble”, IEEE 802.11-19/0740.

## Slide 12: Straw Poll 1
Do you agree to add the following text into Section 3 of SFD?
  “11bd shall support two Midamble periods.”
Y:
N:
A:

## Slide 13: Straw Poll 2
Do you agree to add the following text into Section 3 of SFD?
  “One of the two Midamble periods is 10 for single stream transmission.”
Y:
N:
A:

## Slide 14: Straw Poll 3
Do you agree to add the following text into Section 3 of SFD?
  “One of the two Midamble periods is 5 for single stream transmission.”
Y:
N:
A: