## Slide 1: Medium Access with 20MHz BW
Date: 2019-07-01
Authors:

## Slide 2: Recap: >10MHz Operation in NGV Channels
11bd allows 20MHz transmission in two 10MHz channels that legacy 11p STAs and 11bd 10MHz STAs exist.
  The medium access procedure should be defined to allow such operation.
>20MHz operation in 2.4/5/6GHz bands
  One 20MHz primary channel is defined, other 20MHz channels of the BSS operating channel are secondary 20MHz channels
  The backoff and NAV operation are based on:
    The Duration detected in the PPDU that covers the primary 20MHz channel.
    The PHY CCA detection in the primary 20MHz channel.
  The busy/idle detection in 20MHz channels other than the primary 20MHz channel is based on idle/busy checking within PIFS before the transmission.
  Several contributions in 11ac discussed the CCA improvement for legacy device coexistence, e.g. [1].

## Slide 3: Method 1: Same Secondary 10MHz Channel Operation as Baseline
When the backoff in primary channel becomes 0 and the idle/busy checking in secondary 10MHz channel indicates idle within PIFS before the 20MHz transmission, the 20MHz PPDU can be transmitted.
  If 10MHz secondary channel is busy and the backoff counter becomes 0, 10MHz PPDU can be transmitted in primary 10MHz channel.
With this method, the transmission in secondary 10MHz channel may be ignored by 20MHz 11bd STA because of short CCA detection time, higher CCA level.
Primary 10MHz channel
secondary 10MHz channel
CCA idle with PIFS

## Slide 4: Method 2: Same CCA Level in Secondary and Primary 10MHz Channel
A 20MHz STA does backoff in primary 10MHz channel per the current 10MHz operation.
A 20MHz STA avoids back off in primary 10MHz channel and frame transmission by using 20MHz PPDU when 11p/NGV PPDU in secondary 10MHz channel is detected:
  Option 1: A 20MHz STA can decode 11p SIG in secondary 10MHz channel.
Primary 10MHz channel
secondary 10MHz channel
PHY CCA in secondary channel indicates idle medium.
Decoding 11p SIG in secondary 10MHz channel
Assume medium busy.
  Option 2: 20MHz STA assume the medium busy until the end of OFDM symbol pattern detection when 802.11 OFDM symbol pattern is identified.

## Slide 5: Method 2: Same CCA Level in Secondary and Primary 10MHz Channel (Cont’d)
With this method, the transmission in secondary 10MHz channel is protected. However the TXOP protection per NAV is not provided.
  20MHz STA assume the medium busy until the end of the PPDU in 10MHz secondary channel.
  Other enhancement to avoid collision may be also added, e.g. EIFS defer after the end of the detected PPDU in secondary 10MHz channel.

## Slide 6: Reference
[1] 11-10/0744r1