## Slide 1: HARQ Simulation Results
Date: 2019-07-15
Authors:

## Slide 2: Presentation Outline
Introduction
Simulation Assumptions
Throughput Comparisons of ARQ, HARQ-PCC and HARQ-IR under various simulation conditions
  In each case we compare HARQ to ARQ under the same simulation conditions
Comparison of Max-2 and Max-4 HARQ Transmissions

## Slide 3: Introduction
Here we investigate the throughput performance of HARQ
We consider both Punctured Chase Combining (PCC) and Incremental Redundancy (IR)
  For both PCC and IR we support puncturing of code bits in the retransmission of a codeword
We compare HARQ to ARQ as a baseline
We support three types of rate selection/adaptation techniques
  Fixed MCS
  Variable MCS based on long-term SNR
  Optimal Rate Adaptation, based on HARQ Feedback, which can include information like the short-term SNR
Beyond the intrinsic uncertainty in the long-term SNR, we also support addition SNR uncertainty
Here we focus on the Data Field. In another presentation [1] we will consider the overhead of other fields

## Slide 4: Punctured Chase Combining and Incremental Redundancy
HARQ Design | Initial Transmission | Retransmission
Punctured Chase Combining (PCC) | Send all code bits of the LDPC codeword | Resend a subset of the code bits For example, resend 25% or 50% of the code bits
Incremental Redundancy (IR) | Send all the systematic bits and a subset of the parity bits. The bits not transmitted were punctured. For example, send a total of 80% of all the code bits. For Rate ½ code, that would mean 100% of the systematic bits and 60% of the parity bits. | Send the bits that were punctured (not transmitted) in the Initial Transmission. Our simulation also support resending some bits that were sent the first time. For example, resend 25% of the code bits.

## Slide 5: MCS & Puncturing Selection
MCS Selection | Initial Transmission MCS Selection | Retransmission MCS Selection
Fixed MCS | Optimum MCS Selection based on Long-Term SNR | Same MCS as Initial Transmission
Variable MCS | Jointly Optimal MCS for Initial TX & Retransmission based on Long-Term SNR | Jointly Optimal MCS for Initial TX & Retransmission based on Long-Term SNR
Feedback-Based Rate Adaptation | MCS based on Long-Term SNR | Optimum MCS for Retransmission based on Feedback, including ST SNR
Here the term “MCS” is a broad term capturing both the MCS and Codeword Puncturing

## Slide 6: Additional SNR Uncertainty
There may be some Additional SNR Uncertainty used in the Initial Transmission MCS selection
  We include this in our simulations
The following models were considered for the Additional SNR Uncertainty
  0 dB
  U(-3, 3) dB
  U(-5,5) dB
We expect that in practice the additional SNR uncertainty would be less than 5 dB

## Slide 7: Impacts of Additional SNR Uncertainty
Blue: SNR uncertainty of instantaneous SNR given long-term SNR
Red: Long-term SNR uncertainty plus additional uniform, , SNR uncertainty

## Slide 8: HARQ Simulation
Up to two total transmissions
  One Initial Transmission
  One (Possible) Retransmission
LDPC Codes
  Reuse the current LDPC Codes
    Code Rates: 1/2, 2/3, 3/4, 5/6
    Codeword Length: 1944 bits
  Puncture codes to change the code rate
  No need to design new LDPC codes

## Slide 9: HARQ Simulation
Punctured Chase Combining
  Transmit the full codeword in the Initial Transmission
  Supports several puncturing rates in the Retransmission
  Modulation order can also be modified in the Retransmission
Incremental Redundancy
  Puncture the codeword in the initial transmission
  Send punctured bits along with some of the unpunctured bits in the Retransmission
  Modulation order can also be modified in the Retransmission
  Puncture ratio of the 1st and 2nd transmissions are optimized

## Slide 10: Simulation Assumptions
20 MHz bandwidth
Channel Model D
2 TX Antennas
2 RX Antennas
2 Spatial Streams
1000 Byte Payload

## Slide 11: Comparison of ARQ, PCC and IR Under Different Simulation Conditions

## Slide 12: Fixed MCS, No Additional SNR Uncertainty
PCC Gains around 1 dB
IR Gains around 2 to 3 dB

## Slide 13: Variable MCS, No Additional SNR Uncertainty
Here we allow the MCS to change in the retransmission based on long-term SNR

## Slide 14: Variable MCS, Additional SNR Uncertainty
Throughput drops with increased additional SNR Uncertainty

## Slide 15: Variable MCS, Additional SNR Uncertainty
Throughput drops with increased additional SNR Uncertainty

## Slide 16: Feedback-Based Rate Adaptation, No Additional SNR Uncertainty
Here we allow the MCS to change in the retransmission based on short-term SNR
PCC and IR show more gains with Feedback-Based Rate Adaptation

## Slide 17: Feedback-Based Rate Adaptation Additional SNR Uncertainty
Throughput drops with increased additional SNR Uncertainty

## Slide 18: Feedback-Based Rate Adaptation Additional SNR Uncertainty
Throughput drops with increased additional SNR Uncertainty

## Slide 19: Comparison Max-2 Versus Max-4 HARQ TX

## Slide 20: Comparison between Max-2 and Max-4 HARQ Transmissions
So far we have considered a maximum of two total HARQ transmissions (Max-2), consisting of one initial transmission and one (possible) retransmission
Here we consider a maximum of four HARQ transmissions (Max-4) as suggested in [2]. This allows for one initial transmission and up to three (possible) retransmissions
In this comparison we consider the Fixed MCS case
Here we are considering the Data Field only, like in [2]
Overhead for Max-4 TX is expected to be higher than for Max-2 TX, so the gains with overhead will be lower than those shown here for the Data Field only

## Slide 21: Throughput Comparison
Small Gains in PCC and IR when increasing from Max-2 to Max-4 HARQ Transmissions
Loss in ARQ when increasing from Max-2 to Max-4 HARQ TX. Based on same MCS.

## Slide 22: Conclusions
Incremental Redundancy consistently outperforms Punctured Chase Combining
  Our Incremental Redundancy approach is a superset of PCC, since in addition to sending the punctured code bits in the HARQ retransmission, we also allow for repeated transmission of other code bits
Gains for IR and PCC both increase with increasing Additional SNR Uncertainty
  Losses in ARQ are more than losses in HARQ with increased SNR uncertainty
  HARQ is more robust to SNR uncertainty
Gains for IR and PCC both increase with the use of Feedback-Based Rate Adaptation
The difference between the gains for Max-2 and Max-4 HARQ Transmissions are small (e.g. less than 0.5 dB)

## Slide 23: References
Steve Shellhammer, et. al., “HARQ Gains with Overhead Considered,” IEEE 802.11-19/1079r0, July 2019
Yan Zhang, et. al., “Comparisons of HARQ transmission schemes for 11be,” IEEE 802.11-19/792r1, May 2019