## Slide 1: Multi-Link Operation: Dynamic TID Transfer
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
George Cherian | Qualcomm Inc. |  |  | 
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
Duncan Ho | Qualcomm Inc. |  |  | 
Date: 2019-08-22

## Slide 2: Overview
Multi-link operation (MLO) has been discussed in the past with the focus on packet-level aggregation [1]
In this document, we discuss how the unified (MLO) framework can support dynamic transfer of a TID between links

## Slide 3: TID Link Switch
MLO framework would need to have the ability to seamlessly move a TID from one link to another link based on a certain condition
  E.g., transferring a TID from a link on 2.4GHz to a link on 5GHz without requiring reassociation
A TID may be transferred for reasons such as load balancing or congestion
  E.g., 2.4GHz link is congested or becomes unavailable
Different from packet-level aggregation where both links are utilized for aggregation
Packet-level agg
TID Link Switch

## Slide 4: Recap: 3-tier hierarchy [1][2]
STA (MAC-PHY instance): There is one STA (MAC/PHY instance) per link
  Each STA has its own per-link MAC/PHY attributes/capabilities
  The MAC address of each STA may be same or different
Multi-Link Logical Entity (MLLE): An MLLE is affiliated with one or more STAs
  An MLLE has an externally addressable unique MAC address which is the MAC-SAP endpoint
  Common BA session, security and SN across all STAs affiliated with an MLLE
MLO-Device: An MLO-Device is a collection of MLLEs
  An MLO-Device may have multiple MAC-SAP endpoints
  Enables common mgmt. signaling across all MLLEs for power-save reasons

## Slide 5: Example of unified MLO framework to support pkt-level / TID Link switching
Packet-level Aggregation
Dynamic TID Link Switch

## Slide 6: Summary
The contribution introduces a high-level design to support dynamic TID transfer between links with MLO framework

## Slide 7: Straw Poll 1
Do you support that the 802.11be amendment shall define mechanism(s) for multi-link operation that enables the following:
  Negotiate capabilities and operating parameters for multiple links during a single setup signaling exchange.
  Signaling to dynamically enable/disable link(s)
  An operational mode for concurrently exchanging frames on more than one link for a TID
  An operational mode for restricting outstanding MPDUs of a TID to be on one link at a time
  Dynamically change the mapping of MPDUs of a TID from one set of links to another set of links
  Y:
  N:
  A:

## Slide 8: Reference
[1]: 11-19/0823
[2]: 11-19-773