## Slide 1: Coexistence in 6 GHz License-exempt Spectrum
Date: 2019-07-17
Authors:

## Slide 2: Unlicensed Spectrum - Principles
Same carrier can be accessed by multiple networks or operators
Networks and carriers can use different technologies
  Not limited only to IEEE and 3GPP technologies
No restrictions on the operation mode of networks and devices
  Networks can be managed or ad-hoc
    IEEE networks are optimized for ad-hoc operation
    3GPP networks are optimized for managed operation

## Slide 3: Regulations for unlicensed spectrum in 6 GHz
Regulations should be simple
  The ETSI BRAN Harmonized Standard for 5 GHz includes technology specific exemptions and is too complex to build conformance tests
  Better to focus on key aspects and avoid unnecessary complexity
Regulations should be testable
  Simple regulations allow the key aspects to be tested and enforced
  Reliance only on declaration of compliance to regulations undermines the effectiveness of the regulatory requirements
Regulations should be identical for all devices, networks and technologies
  No exceptions should be provided to any technology or device

## Slide 4: Unlicensed spectrum in 6 GHz – Key features
No RLAN technologies already deployed
  Opportunity for enhancing spectrum efficiency by using modern technology neutral coexistence
Coexistence with incumbent services is critical
  Needs some form of AFC (automatic frequency coordination)
  Discussions are ongoing in regulatory bodies on how this is to be achieved
The range of spectrum made available for unlicensed operation is still under discussion
  6.425 GHz to 7.125 GHz could be assigned as licensed spectrum in some regions
  5.925 GHz to 6.425 GHz expected to be assigned as unlicensed spectrum in both US and Europe

## Slide 5: 3GPP Technologies – Channel Access in 5 GHz
Coexistence with a large number of devices already deployed in 5 GHz was a key design constraint for LTE-LAA
  The design criterion adopted was to not harm a Wi-Fi network more than another Wi-Fi network
  The design criterion was biased towards already deployed networks to ensure they were not affected was adopted
    e.g., an LTE-LAA network with zero throughput would meet the criterion
Channel access procedures aligned with IEEE 802.11 on most aspects
  Such alignment was prioritized over optimizing the performance of 3GPP networks in many cases

## Slide 6: 3GPP Technologies – Channel Access in 5 GHz
Started from a clean slate with several fundamental aspects discussed
  LBT Protocol
    Load based vs. Frame based
      Frame based was an attractive choice due to frame structure of LTE
    LBT types: Random back-off with a contention window of fixed size (cat. 3 LBT) vs. variable size with exponential backoff (cat. 4 LBT)
      Cat. 3 LBT was better suited to the frame structure of LTE
    Slot size: 9 µs vs. 20 µs
      20 µs better suited for LTE with 1 ms subframes
    Contention window sizes: EDCA vs. other options
      Shorter contention window size very attractive for LTE UL and control
  Maximum Channel Occupancy Time (MCOT)
    Channel occupancy times aligned with ETSI BRAN harmonized standard
  Energy detection thresholds
    An absolute and calibrated ED threshold that is 10 dB lower than Wi-Fi
  Multi-carrier operation
    Wi-Fi channel bonding sets adopted for LTE UL

## Slide 7: 3GPP Technologies – Channel Access in 5 GHz
Remaining differences in channel access design are mainly due to one or more of the following
  Fundamental differences between a managed and an ad-hoc network
    LTE and NR UEs do not transmit any data on their own unless explicitly granted by a supervising node
  Performance considerations
  Complexity considerations
Coexistence depends on sensing threshold, LBT protocol and transmit duration
The most significant remaining difference between IEEE 802.11 and 3GPP technologies is the differing sensing thresholds used by 802.11 nodes to 802.11 and non-802.11 nodes
  IEEE 802.11 devices defer to 802.11 devices at a lower sensing threshold and all other devices at a higher sensing threshold
  LTE (and NR-U) devices defer to all devices at the same threshold

## Slide 8: 3GPP Technologies – Channel Access in 5 GHz
For 3GPP technologies, a single energy detection threshold of −72 dBm/20 MHz was chosen to be in between the energy and preamble detection thresholds for IEEE 802.11 devices to enable a long term convergence for all technologies to a single harmonized threshold
  IEEE 802.11ac was an already deployed technology at the time LTE-LAA was developed
  Adoption of ED at −72 dBm/MHz was considered a possibility for IEEE 802.11ax in 5 GHz
    This was also part of an agreement in ETSI BRAN (BRAN(15)000200r3, “Agreed Compromise on Adaptivity”, ETSI BRAN 85)
3GPP RAN1 requested the IEEE to adopt the aligned energy detection threshold of −72 dBm. The IEEE declined this request and explained it as follows [1]:
  “IEEE 802 declined 3GPP RAN1’s request because it would put 802.11ax systems at a disadvantage compared to billions of existing and future 802.11a/n/ac systems using an ED threshold of −62 dBm and at a disadvantage to any LAA systems not detecting 802.11 preambles at −82 dBm.”

## Slide 9: Coexistence in 6 GHz
Unlicensed spectrum in 6 GHz does not have any already deployed RLAN devices preventing the adoption of a single threshold
  No issue with existing IEEE 802.11n/ac devices that use a higher ED threshold => ED threshold can be reduced to −72 dBm
  Preamble detection threshold can optionally be raised to −72 dBm at least for other IEEE 802.11ax networks (no legacy 80211n/ac devices)
The 6 GHz band provides an excellent opportunity to converge to a single common maximum harmonized energy detect (ED) threshold for all devices
  Ensures truly fair coexistence for all current and future technologies operating in this spectrum
In greenfield 6 GHz unlicensed spectrum, setting sensing thresholds based on the characteristics of neighboring nodes is NOT the right solution (no legacy devices)
  If a particular technology or network implements different sensing thresholds to different types of nodes, the maximum sensing threshold used should be identical for all nodes and technologies

## Slide 10: Coexistence in 6 GHz
A single common maximum energy detection threshold has the following advantages:
  Fundamentally fair coexistence
    It enables all nodes to be respected at the same energy level regardless of which technology they use.
  Superior performance (addressed in companion document)
  Simpler compliance verification
  Flexible technology innovation
    Each technology can develop preambles or other signals/protocols that provide benefits such as power saving, system performance improvements etc. without concerns on coexistence
    Coexistence is decoupled from the use of preambles
The ED threshold used in any network can be adapted to be below the common maximum threshold if it benefits system performance
  Allows control of reuse within the network.
  Threshold can always be raised to the common maximum threshold if and when needed
  Energy detection is feasible at reasonably low levels

## Slide 11: Summary
Regulatory framework should be simple, testable, technology neutral and be future proof to allow any new technologies to use the spectrum without the constraints of older technologies
Coexistence with existing (e.g. fixed) services in the band is important to consider
Greenfield spectrum provides an excellent opportunity for truly fair coexistence between RLANs operating in the band
A single common maximum energy detection threshold for all devices and technologies is crucial to ensure fairness and performance benefits for all users of unlicensed spectrum in 6 GHz

## Slide 12: References
[1] IEEE EC-17-0064-00-00EC, Liaison Statement to 3GPP RAN/RAN1/RAN4 related to PD & ED issues, 22 March 2017