## Slide 1: Joint Transmissions: Backhaul and Gain State Issues
Date: 2019-06-07
Authors:
Name | Affiliations | Address | Phone | Email
Sameer Vermani | Qualcomm |  |  | 
Bin Tian |  |  |  | 
VK Jones |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
Joint processing transmission (JT) has been discussed as a candidate technology to be adopted in the EHT standard
  Substantial gains are on offer due to degrees of freedom gain from pooling together the antennas of multiple APs
Presentations so far have focused on the following set of challenges
  Inter-AP synchronization of phase, frequency and timing
These slides are an attempt to highlight
  The backhaul requirements of this technology
  Sensitivity to gain state errors across APs

## Slide 3: Need for Backhaul
In JT, data of one user in transmitted from multiple APs
  Data of all participating STAs needs to be available at all APs (shared over backhaul)
  MU-MIMO using one giant precoder over the combined array consisting of the Tx antennas of all APs
AP1
AP2
BSS1
BSS2
Backhaul Link

## Slide 4: Backhaul Burden
In both retail and carrier markets, we have to assume the backhaul happens over the air
Two possible deployment models
  Backhaul uses the same channel as fronthaul
  Backhaul uses a different channel as fronthaul
In scenario a), the impact on capacity is very direct, where as in b), it’s an indirect impact

## Slide 5: Key Observation about Backhaul Requirement
The backhaul has to pump the same data that eventually gets transmitted from multiple APs in the downlink over the front-haul
  Assuming a model where the master AP is broadcasting the data of all users to slave APs
  The sum throughput across all recipient STAs over the front-haul needs to be supported over the backhaul as well
    Think of it like data being pumped into multiple APs, and the same data eventually being sprinkled onto recipient STAs over front-haul

## Slide 6: Example Case of four APs, 4 Tx each
One of the APs is the master AP, and is connected to the internet backbone
  Needs to share the raw data of all participating users available at all APs
  Broadcasts the data of all STAs to the slave APs over backhaul
Backhaul Data rates needed for Joint Transmissions at 80MHz
  Function of sum PHY data rates being supported over front-haul
    About 3.27 Gbps if using MCS5 (for 12ss total across APs)
    About 3.68 Gbps if using MCS6 (for 12ss total across APs)
    About 4.08 Gbps if using MCS7 (for 12ss total across APs)
  Note that this technique might need to send the precoder as well, but that should lead to negligible additional burden
To support the backhaul data rates with 4ss, need 160MHz and MCS9

## Slide 7: Amount of Backhaul Needed: General Trends
Factors to consider about the backhaul link
  Limited by the number of spatial streams that can be supported at ONE AP
    AP with the min number of antennas limits the # of spatial streams in the backhaul link
  Maybe able to support a higher MCS since it is an open loop transmission
Since factor A. is more dominant, we need more bandwidth in the backhaul than the front-haul
  The more the number of APs participating in a JT, the greater this discrepancy
    Factor A becomes more and more severe as number of APs grow
  E.g. For the 4 AP case, 80MHz Joint transmissions will not work with a 80MHz backhaul as shown in the last slide
Note: Assumption of an AP being able to broadcast to all other APs at a high MCS (e.g., 4ss MCS9 as assumed in last slide) is already optimistic

## Slide 8: Gain State Related Issues
These issues mainly affect JT (and not other AP coordination flavors)
Relative gain state during sounding stage across APs cannot be very different from that during actual transmission
  The relative gain of the channel across APs which is used for precoding should be very close to relative gain at the time of transmission
    Any difference beyond 0.8 dB needs to be corrected
    See next slide
Sources of gain state difference
  The PA gain state of AP can be different during sounding and actual transmission
  AGC gains can be different at different APs for implicit sounding
Moreover, difference in AGC gain state at a slave AP trying to phase synchronize to the master can also impact phase synch
  Changes in gain state for two consecutive sync signals can lead to phase shifts
  Might need to use a fixed AGC state at slave APs when receiving synch signals

## Slide 9: Gain Offset Impact: Joint Transmissions in DL
Relative gain state during sounding stage across APs modeled to be different from that during actual transmission
Below we show the sensitivity to relative gain state errors as a function of pathloss
2 BSSs: Each equipped with 8 antenna AP
[2 2 2 2 2 2] Joint Transmission
40MHz BW
Relative AGC state error Across APs in dB

## Slide 10: Conclusions
In these slides we showed the following for JT
  Backhaul requirements
    For retail and carrier markets, where backhaul is over-the-air, backhaul needs higher BW than front-haul
      80MHz JT needs 160MHz backhaul
  Sensitivity to PA or AGC gain state errors
    Sub-dB level accuracy needs to be maintained

## Slide 11: APPENDIX
Feeding back precoded samples

## Slide 12: Other approach of doing backhaul
Precoded data from a central processor to a 80MHz, four 4 Tx APs
  Assuming 80MHz, 980 tones need to be sent in 14.4 us (assuming 1.6 us CP)
  If 4 antennas at each AP are active, then every AP will be sent 4x980 I, Q samples in 14.4 us
  Assuming 8 bit I and 8 bit Q, this means 4x4x980x16 =62720*4 bits in 14.4 us = 17.4 Gbps
  This is independent of data rate being supported in the actual transmission (if bit-widths stay constant)