## Slide 1: Acknowledgement for HARQ Transmission
Date: 2019-07-02
Authors:

## Slide 2: Background
Dozens of contributions [1-4] have demonstrated the gain for HARQ.
HARQ is regarded as one promising solution to make link adaptation more robust and efficient by providing an extended set of MCSs with finer granularity besides throughput gain and range extension
In this contribution, we make an analysis for the possible acknowledgement schemes for HARQ transmission

## Slide 3: Acknowledgement for HARQ
There may exists two possible acknowledgments for HARQ transmission
  MPDU based acknowledgement (MA) as today
  Codeword based acknowledgement (CA) [5]
  One of the main motivations to have CA for HARQ is to reduce memory required at the receiver side
  However, some fatal flaw related to CA can also be observed
  For example, without SN for tracking each codeword
  In the following slides, a comprehensive comparison between CA and MA is provided

## Slide 4: Acknowledgement for HARQ
Memory required at the receiver
  CA can avoid to store LLR of the correct codewords within the failed MPDU such that to require small memory
  Assume it can guarantee undetected error probability of very low value （may need extra CRC）
  On the other hand, it is also unnecessary to keep the LLR of correct codewords in the failed MPDU for MA with the same assumption on error detection of a codeword
  Instead, keep the correct decoded info bits
  From another angle, CA requires additional memory to create new scoreboard to maintain the reception status of codewords compared with MA
In a word, CA does not show advantage on the required memory compared with MA, but instead has some defect.

## Slide 5: Acknowledgement for HARQ
Retransmission size at transmitter
  Actually, retransmission size depends on comparison between the size of info bits in a codeword and the MPDU size
  Both two cases can be observed in the real transmission
  When the size of info bits in a codeword is smaller than the MPDU size, advanced MAC mechanisms can be used to reduce retransmission size for MA, i.e., fragmentation
  The motivation of original fragmentation is used to reduce transmission size at low SNR
  It is difficult to say that CA or MA has obvious gain on retransmission size compared with the other
  Moreover, codeword retransmission would complicate transmission procedure .

## Slide 6: Acknowledgement for HARQ
Besides the discussion before, additional comparison between MA and CA is provided as following
 | CA | MA
Feedback | Create new feedback, difficult to determine the size which may be too large | Reuse Ack and Block Ack
Code scheme support | Only LDPC | Both LDPC and BCC
Track tag | Without SN for acknowledgement | With SN for acknowledgement
Error detection | Not robust if only using parity check matrix, without CRC | Robust with FCS
Additional required change | I. Block Ack setup, including TX/RX window, scoreboard maintaining ; II. Acknowledge frame, including Ack, Block Ack and so on; III. Block Ack Request frame | No additional change

## Slide 7: Summary
Two acknowledgement schemes for HARQ transmission are compared
To incorporate HARQ scheme to 802.11be without obvious complexity, recommend to reuse MPDU based acknowledgement for HARQ transmission

## Slide 8: References
[1] IEEE 802.11-18/1587r1 HARQ for EHT
[2] IEEE 802.11-18/1955r0 HARQ for EHT – Further Information
[3] IEEE 802.11-18/2029r1 HARQ in EHT
[4] IEEE 802.11-18/1992r1 HARQ feasibility
[5] IEEE 802.11-18/0873r0 HARQ framing

## Slide 9: SP 1
Which acknowledgement scheme do you prefer to use for HARQ transmission
  Option 1: MPDU based acknowledgement
  Option 2: Codeword based acknowledgement