## Slide 1: Preamble Structure
Date: 2019-07-15
Authors:
Name | Affiliation | Address | Phone | Email
Ross Jian Yu | Huawei Technologies | F3-6A, Huawei Base, Bantian, Shenzhen |  | ross.yujian@huawei.com
Ming Gan |  |  |  | 

## Slide 2: Background
Each standard has its specific preamble, which provides functions including synchronization, AGC, time/frequency correction, channel estimation, auto-detection and signaling etc.
Regarding auto-detection, 11n and 11ac PPDU rely on the phase rotation to do auto-detection:

## Slide 3: Background
11ax relies on L-SIG length and RL-SIG (symbol repetition) to first identify 11ax PPDU, and further relies on format subfield in HE-SIG-A, and the phase rotation of HE-SIG-A2 to identify four different HE formats:

## Slide 4: Preamble structure in 11be
Several aspects are discussed in this presentation:
  L-preamble
  Auto-detection: potential methods to identify EHT PPDU
  How many EHT modes
  EHT-SIG-A/SIG-B

## Slide 5: L-preamble
According to the PAR [1], EHT/11be should ensure backward compatibility and coexistence with legacy IEEE Std. 802.11 compliant devices operating in the 2.4 GHz, 5 GHz, and 6 GHz bands.
Hence L-preamble is still needed in at least one mode of EHT PPDU.
L-preamble is duplicated when BW > 20MHz. For EHT PPDU that is <=160Mhz, can reuse the existing tone rotation γ_(k,BW). For PPDU that is >160Mhz, new γ_(k,BW) is needed.

## Slide 6: EHT Auto-detection
Several aspects need to be considered regarding auto-detection:
  It was discussed in 11ax [2] and 11ba[3] that the first symbol after L-SIG should be BPSK modulated to spoof HT devices so that HT devices will respect the length in L-SIG. Hence BPSK modulated symbol after L-SIG shall also be used in 11be.
  RL-SIG: outdoor operation is still within the focus of the 11be PAR [1]. RL-SIG may still be needed. Whilst in order to differentiate from 11ax, a different version of RL-SIG may be needed, e.g., negative L-SIG or other sequence masked L-SIG.
    Other features like phase rotation can further help 11be PPDU to differentiate from 11ax.
  A signature/mark symbol with fixed bits [3,4] can also be considered as a way to do EHT auto-detection.

## Slide 7: EHT PPDU formats
Non-HT has one format; HT has one MF format and one GF format; VHT has one single format which supports both SU and MU MIMO; whilst HE has four formats: SU, MU, TB and ER SU.
For EHT, DL/UL OFDMA and MU-MIMO features should be still considered. Hence EHT MU and EHT TB PPDU formats should be still considered. As outdoor operation is still needed, EHT ER SU PPDU formats should also be considered, together with EHT SU PPDU format.
For AP coordination, if a new PPDU format or preamble structure is needed can be further discussed:
  Can reuse the above mentioned format and be transparent to STAs.
  Can design a new preamble which contains signaling information from multiple APs.

## Slide 8: EHT-SIG-A/SIG-B
More bits are likely needed for 11be to support features like:
  320Mhz (larger BW bitwidth, more OFDMA users)
  16SS (larger Nsts/spatial configuration bitwidth)
  HARQ (RV, HARQ process ID…)
  AP coordination (TBD)
Hence, a way of transmitting signaling field more efficiently is needed, e.g.,:
  Previously, SIG-A and SIG-B are encoded based on a 20MHz unit. For EHT, part of EHT-SIG-A/SIG-B can be encoded based on 40MHz or larger unit.
  Larger number of content channels for EHT-SIG-B
Also, because different features need very different number of signaling bits, a EHT-SIG-A field with variable number of OFDM symbols may also be needed.

## Slide 9: Wrap up
Several aspects regarding preamble structure are discussed in presentation.
More work regarding solution details and simulations need to be done later.

## Slide 10: SP1
Do you agree that for at least one mode of EHT PPDU, L-STF, L-LTF and L-SIG shall be transmitted at the beginning of the EHT PPDU?

## Slide 11: SP2
Do you agree that for at least one mode of EHT PPDU, the first symbol after L-SIG shall be BPSK modulated?

## Slide 12: Reference
802.11 EHT Proposed PAR, 18/1231-r6, Laurent Cariou (Intel)
Preamble design and auto-detection, 15/579r4, Hongyuan Zhang (Marvel)
A comparison of BPSK-Mark Options, 18/1156r1, Alphan Sahin (InterDigital)
Autodetection with signature symbol, 15/0643r0, Sriram Venkateswaran (Broadcom)