## Slide 1: Further investigation of Mid-amble performance
Date: 2019-07-15
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Insun Jang |  |  |  | Insun.jang@lge.com
Suhwook Kim |  |  |  | Suhwook.kim@lge.com
Jeongki Kim |  |  |  | Jeongki.kim@lge.com
Jinsoo choi |  |  |  | js.choi@lge.com
July 2019

## Slide 2: Introduction
The following issues related to mid-amble have been discussed in the previous meeting.
  Mid-amble periodicity [1,2]
    One periodicity has been proposed for the mid-amble transmission in 11bd.
  Composition [3]
    To reduce mid-amble overhead, compressed mid-amble has been introduced.
In this contribution, we further investigate the performance of mid-amble by considering both mid-amble periodicity and composition.

## Slide 3: Composition of mid-amble
As provided in [3], according to mid-amble design criteria, the mid-amble can be constructed in variety of ways as follows.
  Option 1 : with normal LTF
  Option 2 : with 2x compressed LTF
    Configures using only a half of LTF time sequences
    Has better efficiency
  Option 3 : with repeated 2x compressed LTF
    Configures using the repetition of 2x compressed time sequences
    Has a same efficiency as option 1, but better performance.

## Slide 4: Periodicity
In [1], one long periodicity for mid-amble that provides reliable performance in C2C channel was suggested.
  It only considered the mid-amble constructed with normal LTF.
But, as described in previous slide, mid-amble can be constructed by using the variable design criteria because structure of mid-amble is not yet decided.
Periodicity which provides the best performance and better efficiency may vary depending on the composition of mid-amble.
So, in next slides, we evaluate the performance and goodput of 11bd transmission according to mid-amble composition and periodicity.

## Slide 5: Simulation settings
Bandwidth : 10MHz
OFDM numerology:
  11ac 20MHz DC2
CP size : 1.6us
Number of data bits: 300 Bytes
Coding : LDPC
C2C channel with Doppler
  Rural LoS, Highway LoS, Highway NLoS
CFO : 20ppm in 5.9GHz
Midamble periodicity and composition
  Periodicity(M) : 2/4/8
  Normal, 2x compressed, Repeated 2x compressed
GoodputSNR = maxMCS {(Rate(MCS)*(1-PER(MCS,SNR)))*M/(M+1)}

## Slide 6: Rural LoS
2x-rep-MP8 has a good throughput overall
MP = mid-amble periodicity

## Slide 7: Highway LoS
Overall 2x-rep-MP8 have a good performance.
  Up to 25dB range, it has a good throughput.
At the high SNR, 2x-rep-MP4 can achieve the highest throughput.
Goodput figure

## Slide 8: Highway NLoS
2x-MP4 with repetition has a good throughput at all range.
Due to efficiency, MP4 case has a better throughput than MP2 case.
Goodput figure

## Slide 9: Discussion
Overall, 2x-compressed mid-amble with repetition has a better throughput than other compositions (i.e., normal and 2x-compressed ) in various C2C channels.
  Even though 2x-rep compressed mid-amble has no gain from efficiency aspect, it has better performance due to the improvement of channel estimation.
As shown in previous slides, it is hard to provide good performance by using the one periodicity regardless of channel conditions.
  To achieve high throughput, we can apply the one long periodicity that guarantees the supporting of high MCS.
    by using 8 as a periodicity, satisfactory performance can be achieved.
  On the contrary, in the poor channel such as highway NLoS, for the reliable transmission, it needs to define another short periodicity which provides good performance.
    When 4 is used as a periodicity, we checked that it has a good throughput.

## Slide 10: Conclusion
In this contribution, we further investigate the performance of mid-amble by considering the various composition of mid-amble and periodicity .
  2x compressed mid-amble with repetition has better throughput than both 2x compressed only and normal.
    By using the unified composition for mid-amble, it does not require the additional signaling and it can be implemented simply.
  To provide a good performance regardless of channel condition, we can consider the two periodicities for mid-amble.
    As the periodicities for mid-amble of 11bd, we can consider the following values
      4 for good channel status
      8 for poor channel status
  And, the periodicity for 11bd PPDU should be included in NGV-SIG.

## Slide 11: SP1
Do you agree that mid-amble for 11bd is composed of 2x compressed mid-amble with one repetition ?
Y/N/A

## Slide 12: SP2
Do you agree to add the followings into the section 3 of 11bd SFD?
  ‘The two periodicities for midamble are used in 11bd’
    ‘Periodicity is 4 and 8’
Y/N/A

## Slide 13: SP3
Do you agree to add the followings into the section 3 of 11bd SFD?
  ‘NGV-SIG field contains the periodicity of mid-amble ’
Y/N/A

## Slide 14: Reference
[1] IEEE 802.11-19-0740/r2 , Performance evaluation of Mid-amble, Dongguk Lim
[2] IEEE 802.11-19-684/r0, Prashant Sharma
[3] IEEE 802.11-19-685/r2, Midamble Compression, Prashant Sharma