## Slide 1: The use of no LBT for DRS is not justified by history
1 July 2019
Authors:
Name | Company | Phone | email
Andrew Myles | Cisco | +61 418 656587 | amyles@cisco.com

## Slide 2: The history of Short Control Signalling supports proposals to ban no LBT & restrict short LBT
Executive summary
  Today’s workshop will hear multiple presentations related to the use of short LBT access by LAA/NR-U
  This presentation examines the history of no LBT access for short control signalling in EN 301 893 by LAA/NR-U
  The history of Short Control Signalling supports the proposal to ban no LBT & restrict short LBT in the future

## Slide 3: Today’s workshop will hear multiple presentations related to the use of short LBT access by LAA/NR-U
  LAA (and now NR-U) makes use of short LBT for access for DRS frames
    There are proposals for NR-U to use short LBT access for other purposes too
  The use of short LBT for access means NR-U is able to send DRS frames at a particular time, which is convenient for NR-U operation
    It is not clear that this is actually necessary because DRS frames can also be sent using Cat 4 LBT access
  However, the use of short LBT for access essentially gives DRS frames “super high” priority access … which means other systems (including Wi-Fi) will obtain less access than otherwise expected or fair
  There has recently been intense discussion (without consensus) in IEEE 802.11 WG, 3GPP RAN1 and ESTI BRAN on whether the use of short LBT based access for DRS frames should be restricted
  A number of presenters today are expected to provide their perspective on this question ….

## Slide 4: This presentation examines the history of no LBT access for short control signalling in EN 301 893
  The use of short LBT for DRS access has been justified in 3GPP RAN1 partly by European rules (as documented in EN 301 893) that allow limited use of no LBT access for short control signalling
    The FCC does not have equivalent rules because the FCC favours allowing the industry to sort out such issues
    The FCC approach has worked well up until now in 2/4/5GHz because the only stakeholder is Wi-Fi
  This justification raises at least two relevant and interesting questions:
    Why was the rule allowing the limited use of no LBT for short control signalling introduced into EN 301 893?
    Does the reason for its introduction into EN 301 893 justify its continuing use for DRS (or other short control signalling frames) in LAA/NR-U?
  This presentation examines the historical context of the no LBT for short control signalling rule into EN 301 893

## Slide 5: The history of EN 301 893 provides insight on the use of no LBT for short control signalling
Investigation of history of Short Control Signalling in EN 301 893
  Special access for Short Control Signalling was not addressed up to EN 301 893 v1.5.1 (2008)
  EN 301 893 v1.6.1 (2011) seems to have introduced no LBT access for Short Control Signalling to enable ACK’s
  EN 301 893 v1.7.1 (2012) introduced a precedent for tighter restrictions on access rules for Short Control Signalling
  EN 301 893 v2.1.1 (2017) refinements negate the need for special access for Short Control Signalling

## Slide 6: Special access for Short Control Signalling was not addressed up to EN 301 893 v1.5.1
  Up to EN 301 893 v1.5.1 (2008) there is no mention of Short Control Signalling or special access for Short Control Signalling
  There is also no reference to any version of IEEE 802.11

## Slide 7: EN 301 893 v1.6.1 introduced no LBT access for Short Control Signalling to enable ACK’s
  EN 301 893 v1.6.1 (2011) is the first version that refers to both no LBT access for Short Control Signalling and IEEE 802.11n/ac
  It appears that no LBT access for Short Control Signalling was introduced to enable 802.11 ACK’s with no LBT
    The description of no LBT access for Short Control Signaling uses an ACK as an example of a frame that could be sent with no LBT
    No LBT access was necessary for ACKs because EN 301 893 v1.6.1 did not define a COT, which is what enables ACKs with no LBT in EN 301 893 v2.1.1
    There is no evidence no LBT was introduced to allow special access for DRS-style frames
  EN 301 893 v1.6.1 set the no LBT threshold for Short Control Signalling at 10% of airtime
    It is not known why 10% was chosen; probably “finger in the air”

## Slide 8: EN 301 893 v1.7.1 established a precedent for tighter restrictions on special access rules
  EN 301 893 v1.7.1 (2012) continues referring to both no LBT for Short Control Signalling and IEEE 802.11n/ac
  EN 301 893 v1.7.1 also reduced the no LBT threshold for Short Control Signalling threshold from 10% to 5% of airtime
    It is not definitely known why it was reduced to 5%
    Presumably it was agreed that 10% was unnecessarily high to support ACKs
  The reduction in the no LBT threshold for Short Control Signalling demonstrates that such requirements can be made more restrictive
    Contrary to recent assertions by participants of 3GPP RAN1 that requirements can never be made more restrictive

## Slide 9: EN 301 893 v2.1.1 refinements negate the need for special access for Short Control Signalling
  EN 301 893 v2.1.1 (2017) referred to both no LBT for Short Control Signalling and IEEE 802.11
    v2.1.1 provides for access by ACKs as part of the COT
  EN 301 893 v2.1.1 did not change the no LBT access for Short Control Signalling threshold of 5% of airtime
    However, there was very little consideration of the appropriateness of the 5% threshold at the time because of the urgency of enabling the use of 802.11ac in Europe
  The introduction of the COT concept into v2.1.1 means that the main, original purpose of no LBT access for Short Control Signalling is no longer relevant
    ACKs are now handled within COTs

## Slide 10: The history of Short Control Signalling supports the proposal to ban no LBT & restrict short LBT
Conclusions incorporating historical insight
  No LBT for Short Control Signalling is no longer required in EN 301 893 to satisfy the original purpose …
  … and other work presented today shows the use of short LBT for DRS has an adverse affect on other users
  This suggests that it is reasonable to ban or restrict the use of no LBT (or short LBT) for Short Control Signalling …
    Except possibly a grandfathering provision for LAA
  … supported by a good historical precedent for refining and further restricting access for Short Control Signalling over time