## Slide 1: Enhanced Resource Allocation Schemes for 11be
Date: 2019-06-12
Authors:
Name | Affiliations | Address | Phone | Email
Jianhan Liu | Mediatek |  |  | jianhan.liu@mediatek.com
Yongho Seok |  |  |  | 

## Slide 2: Outline
In the HE WLAN based on IEEE 802.11ax standard, each non-AP station (STA) can only be assigned with a single resource unit (RU).
We show that such restrictions on RU allocations significantly reduce the spectral efficiency and the network throughput in some scenarios.
We propose the enhanced RU allocation schemes for 11be that allows multiple contiguous and non-contiguous RUs assigned to a single STA.

## Slide 3: One RU per User Degrades Spectral Efficiency
This constraint degrades the spectral efficiency when number of users are small.
  For example, when a 20MHz channel is assigned to two users, according to current 11ax spec., the center 26tone-RU must be wasted. (more than 10% spectral efficiency loss).
  For Example, two users in 80MHz transmission, if one user is allocated to 242-tone RU, then the other user can only use 484-tone RU. There are 242-Tone RU and a 26-tone RU are wasted (more than 25% spectral efficiency loss).
Not Used
Not Used

## Slide 4: One RU per User Wastes BW in preamble Puncture
For preamble puncture cases due to radar signals (for DFS channels), if the transmission is to a single user, then only primary 20MHz can be used if radar signals is detected in the secondary 20MHz channel.
  In this case, if the BSS bandwidth is 80MHz, then 40MHz BW are wasted, which is 200% spectral efficiency degradation.
  In this case, if the BSS bandwidth is 160MHz, then 140MHz BW are wasted, which is 700% spectral efficiency degradation.

## Slide 5: One RU per User Also Hurts the Diversity Gain
For example, in a 80MHz MU transmissions, the channel profile of user 1 is as shown in figure 3, it is better to allocate the RUs located on [0:20] MHz and [60:80] MHz. Therefore the frequency diversity cannot be fully exploited in such transmissions.

## Slide 6: LTE allows multiple RBs allocated to one User
Resource Block (RB) in LTE is similar to RU in IEEE 802.11 for WLAN.
LTE allows multiple RBs (contiguous and non-contiguous) allocated to one user.
  To enhance the WLAN performance to be comparable to cellular systems, WLAN needs to have enhanced RU allocation schemes that allow multiple RUs to be allocated to one user

## Slide 7: Straw Poll #1
Do you support to allow more than one Resource Units (RUs) to be assigned to a single STA in 11be?
  Coding and interleaving schemes for multiple RUs assigned to a single STA are TBD.
  Maximum number of RUs (>1) assigned to a single STA is also TBD.

## Slide 8: Motion #1
Move to add the following text into 11be SFD:
  11be shall allow more than one Resource Units (RUs) to be assigned to a single STA
    Coding and interleaving schemes for multiple RUs assigned to a single STA are TBD.
    Maximum number of RUs (>1) assigned to a single STA is also TBD.