## Slide 1: Consideration on Multi-AP Sounding
Date: 2019-08-09
Authors:
Name | Company | Address | Phone | Email
Kosuke Aio | Sony Corporation |  |  | Kosuke.Aio@sony.com
Yusuke Tanaka |  |  |  | Yusuke.YT.Tanaka@sony.com
Ryuichi Hirata |  |  |  | Ryuichi.Hirata@sony.com
Thomas Handte |  |  |  | thomas.handte@sony.com
Dana Ciochina |  |  |  | dana.ciochina@sony.com

## Slide 2: Introduction
Multi-AP Coordination is one of the candidate features for 11be[1]
There are many Multi-AP coordination schemes as follows:
  Joint Transmission (JTX) [2]
  Coordinated Beamforming (CBF) [2]
  Coordinated Spatial Reuse [3]
  Coordinated OFDMA [4]
Multi-AP sounding protocol will be necessary for JTX and CBF.
  Multi-AP sounding protocol has been proposed in [5] [6]
In this presentation, some points about Multi-AP Sounding protocol are discussed.

## Slide 3: Recap : Multi-AP Sounding Protocol
Multi-AP Sounding Protocol in [5][6]
  AP1(Master AP) transmits Sounding Trigger frame to AP2 (Slave AP)
  AP1 and AP2 transmit EHT NDPA and EHT NDP synchronously
    EHT NDPA (NDP Announcement) is the same frame among APs.
    EHT NDP has different EHT-LTFs by Tx antennas of all APs.
  AP1 collects all BF/CQI feedback information to control coordination.
AP1
AP2
STA1
STA2
STA3
STA4
: associated STA
: unassociated STA
Example of Multi-AP Sounding Protocol
AP1
AP2
STAs
EHT
NDP
time
time
time
BFRP
Trigger
EHT
NDPA
Sounding
Trigger
BF/CQI Feedback
BF : Beamforming
CQI : Channel Quality Indication

## Slide 4: Discussion Points
(A) Proper Sounding Protocol for JTX / CBF
  JTX and CBF have each Pros/Cons., so TGbe should support both.
    JTX : High Throughput Gain, but strict synchronization and backhaul requirements [7].
    CBF : Not strict synchronization and backhaul requirements, but lower throughput gain than JTX [8].
  Slide 3 seems to be focused on JTX. What are proper sounding protocols for JTX and CBF respectively?
(B) How to Reduce Feedback Information
  If AP collects feedback information of all links (from all APs to all STAs), overhead of reporting BF feedback will become a serious problem.
  Considering it, feedback information (num. of links) should be limited. How shall AP reduce feedback information?

## Slide 5: (A) Proper Sounding Protocol for JTX/CBF
NDP Transmission
  As for JTX, synchronized transmission will be necessary.
    Considering synchronization (CFO/SFO/timing offset), independent NDP transmission will degrade performance of JTX [7]
  As for CBF, independent transmission will be better.
    An AP makes steering matrix independently, so synchronized NDP transmission will be unnecessary. Independent will be easier.
NDP
NDP
AP1
AP2
STAs
Time
Time
Time
Independent
NDP
NDP
AP1
AP2
STAs
Time
Time
Time
Synchronized

## Slide 6: (A) Proper Sounding Protocol for JTX/CBF
Feedback Information Collection
  As for JTX, one AP will have to collect feedback information of all links
    Multi-AP need to make steering matrix together, so all estimated channel state should be collected to the one AP (maybe Master AP)
  As for CBF, each AP will have to collect feedback information of each link
    An AP makes steering matrix independently, so the AP need only estimated channel state from itself to STAs.
Each AP collects feedback of each link
AP1 collects feedback of all links
AP1
AP2
STAs
time
time
time
BFRP
Trigger
BF/CQI Feedback of all links (AP1-STAs & AP2-STAs)
AP1
AP2
STAs
time
time
time
BFRP
Trigger
BFRP
Trigger
BF/CQI Feedback
of AP1-STAs
BF/CQI Feedback
of AP2-STAs

## Slide 7: (A) Proper Sounding Protocol for JTX/CBF
Observation and Proposal
  Multi-AP Sounding Protocol would be designed for JTX and CBF respectively.
  Therefore, AP should be able to use both properly depending on coordination schemes.
    In that case, Sounding Trigger and/or NDPA should indicate a coordination scheme, JTX or CBF.
Multi-AP Sounding Protocol for CBF
Multi-AP Sounding Protocol for JTX
AP should be able to use both properly

## Slide 8: (B) How to Reduce Feedback Information
Consideration Point : AP can reduce feedback information from non-overlapping STAs.
  Overlapping STAs can get large coordination gain, so they need to report feedback information of multi links : multi-APs - itself.
  Non-overlapping STAs won’t get large coordination gain due to low interference level from non-associated AP. So they need to report feedback information of only one link : associated AP - itself.
AP1
AP2
STA1
STA2
STA3
STA4
STA with large coordination gain
coverage area

## Slide 9: (B) How to Reduce Feedback Information
How shall AP get to know which STAs are non-overlapping?
Approach.1 : Radio Measurement before sounding
  AP will operate the Radio Measurement in advance.
    Radio Measurement Procedure is Section 11.11 in IEEE802.11-2016.
  STA may have to wait long time until some frame (such as Beacon) is received from non-associated AP.
Approach.2 : New Measurement by using NDP
  AP will collect some information about NDP reception and get to know which STAs are in overlapping area or not.
  Only short frame exchanges will be necessary.
Considering overhead, Approach.2 would be better.

## Slide 10: (B) How to Reduce Feedback Information
Proposal Method
  After NDP transmission, AP collects only CQI feedback of all links first, then determines resource allocation of BF feedback based on the CQI.
    Overlapping STAs (STA2&3) are allocated wide band resource for because of reporting more informative feedback (AP1&AP2 – STA)
    Non-overlapping STAs (STA1&4) are allocated narrow band resource because of reporting less informative feedback. (AP1– STA or AP2 - STA)
AP1
AP2
STA1
STA2
STA3
STA4
EHT
NDP
BFRP
Trig.
BF Feedback of AP1–STA1
time
time
time
time
time
time
CQI
Feedback
Sounding
Trigger
EHT
NDPA
STA1
STA2
STA3
STA4
f
Example of Multi-AP Sounding Protocol for JTX
BF Feedback of AP2–STA4
BF Feedback of AP1&AP2–STA2
BF Feedback of AP1&AP2–STA3
wide
narrow
BFRP
Trig.

## Slide 11: (B) How to Reduce Feedback Information
Calculation Result of Sounding Processing Time
Environment
2 APs have each 4 antennas
4 STAs have each 2 antennas
NDP Frame
BW 80MHz, MCS 0
HE PPDU with 4x+3.2us LTF and 3.2us GI
Feedback Frame
BW 80MHz, MCS 0
HE PPDU with 1x+0.8us LTF and 0.8us GI
BW 80MHz, MCS 0
(9,7) for compressed feedback
Subcarrier Grouping = 4
Other Frames
BW 20MHz, MCS 0
HE PPDU with 1x+0.8us LTF and 0.8us GI
If all STAs are in overlapping area, processing time is prolonged due to additional frame. Otherwise, processing time decreases dramatically with short Trig./Feedback.
Chart: Sounding Procedure Time
| 0 | 2 | 4
TGax Sounding Protocol | 6.596 | 6.596 | 6.596
Proposal Sounding Protocol | 6.796 | 5.04 | 3

## Slide 12: Summary
This contribution discussed some points about Multi-AP sounding protocol.
For NDP transmission and feedback, AP should be able to use protocol for both coordination scheme, JTX and CBF.
For reducing feedback information, collecting only CQI feedback before collecting BF feedback is effective for JTX and CBF both.

## Slide 13: Reference
[1] 11-18-1231-01-0eht-eht-draft-proposed-par
[2] 11-18-1926-02-0eht-terminology-for-ap-coordination
[3] 11-19-0801-00-00be-ap-coordination-in-eht
[4] 11-18-1547-00-0eht-technology-features-for-802-11-eht
[5] 11-18-1439-00-0eht-distributed-mu-mimo
[6] 11-19-0804-00-00be-multi-ap-transmission-procedure
[7] 11-19-0811-01-0eht-coordinated-null-steering-for-eht
[8] 11-19-0779-00-00be-performance-investigation-on-multi-ap-transmission
[9] 11-18-1510-01-0eht-ap-coordinated-beamforming-for-eht

## Slide 14: Appendix. Impact on Sounding Procedure Time
Data Transmission Efficiency V.S. Sounding Interval
When short sounding interval is needed to track large channel fluctuation, transmission efficiency will increase greatly by reducing feedback information. Even if there wouldn't be non-overlapping STA, impact on the transmission efficiency will be negligible.
Chart: Sounding Interval [ms]
| 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
TGax | 0.3404 | 0.56027 | 0.6702 | 0.73616 | 0.78013 | 0.81154 | 0.8351 | 0.85342 | 0.86808
Proposal(non-overlapping STA = 0) | 0.3204 | 0.54693 | 0.6602 | 0.72816 | 0.77347 | 0.80583 | 0.8301 | 0.84898 | 0.86408
Proposal(non-overlapping STA = 2) | 0.496 | 0.664 | 0.748 | 0.7984 | 0.832 | 0.856 | 0.874 | 0.888 | 0.8992
Proposal(non-overlapping STA = 4) | 0.7 | 0.8 | 0.85 | 0.88 | 0.9 | 0.91429 | 0.925 | 0.93333 | 0.94
・Data Transmission Efficiency = 1 – Sounding Processing Time / Sounding Interval
・Sounding Processing Time equals the result in Slide 11