## Slide 1: 20 MHz transmission in NGV
Date: 2019-09-15
Authors:
Name | Affiliation | Address | Phone | Email
Yujin Noh | Newracom |  |  | yujin.noh at newracom.com

## Slide 2: Background
For 11bd, advanced PHY candidates have been considered to achieve higher throughput.
FRD&SFD Motion #4 passed [1]
  “In 20MHz bandwidth, L-STF, L-LTF, and L-SIG for 10MHz PPDU are duplicated as shown in the figure below.”
There may be two options [2] for 20 MHz OFDM numerology.
  Opt. 1: define tone plan over entire 20 MHz bandwidth
  Opt. 2: 11bd 10 MHz + 11bd 10 MHz
In this contribution, with some methods proposed, show simulation results of PAPR of L-STF, L-LTF, L-SIG and data portion in NGV 20MHz PPDU based on Opt. 1 (e.g. 11ac 40MHz DC2 based).

## Slide 3: PAPR (Peak-to-Average Power Ratio)
PAPR is well-known to be high when sequence is duplicated in frequency domain.
  Given L-STF, L-LTF, and L-SIG for 10MHz PPDU repeated at legacy portion in 20 MHz PPDU, it is obvious that being simply repeated causes high PAPR for legacy portion of the preamble
Low PAPR value is important in reducing implementation cost of Tx Power Amplifier (PA) and Rx dynamic range related function blocks.
  PAPR could be a nice guideline on actual backoff and dynamic ranges that the implementations need to consider

## Slide 4: Simulation Configuration
99.9% PAPR
  The max power is set to a value of top 99.9%
8x oversampled time domain signal
GI considered as part of the OFDM symbol
L-SIG PAPR
  All combination of values in R1-R4 (RATE field) and R5-R16 (LENGTH field)
Data PAPR
  40 MHz 11ac DC2 (downclocked by 2) based
  Random values applied to more than 100,000 data OFDM symbols with MCS0, MCS2, MCS4, MCS6 and MCS8 (256QAM ¾)

## Slide 5: Options
Considering no legacy devices (e.g. 11n, 11ac and 11ax) in the specially assigned channels, different options can be taken into account.
  Legacy gamma vector with {1, +j}
  Phase rotation in MCS0 DCM (Dual Carrier Modulation)
  CSD (Cyclic Shift Delay)
  etc

## Slide 6: Legacy gamma vector with {1, +j}
Simple way to reuse what we have used (11n-like approach)
  + 1 is multiplied to lower 10 MHz subchannel
  +j is multiplied to upper 10 MHz subchannel
PAPR simulation shows L-SIG is identified as bottleneck of 20 MHz PPDU transmission.
  PAPR of data portion is even better than PAPR of L-SIG field.
PAPR values here could be used as reference for further analysis.
PAPR [dB] (99.9%, 8x oversampled) in 20 MHz |  | 
L-STF | L-LTF | L-SIG (Median)
5.2497 | 5.7927 | 9.3806
1.7dB

## Slide 7: Phase rotation in MCS0 DCM
It is accepted to mitigate the PAPR issues for DCM MCS 0 in 11ax and 11bd [1]
  + 1 is multiplied to lower 10 MHz subchannel
  (-1)k is multiplied to upper 10 MHz subchannel
    k: subcarrier indices
Generally providing improved PAPR over L-STF, L-LTF and L-SIG comparing to reference PAPR values
Legacy portion (especially L-SIG) is not a bottleneck anymore comparing to data portion.
PAPR [dB] (99.9%, 8x oversampled) in 20 MHz |  | 
L-STF | L-LTF | L-SIG (Median)
4.8133 (5.2497) | 5.8799 (5.7927) | 6.9529 (9.3806)
gamma vector
{1, +j}

## Slide 8: CSD (Cyclic Shift Delay) 1/2
Cyclic delayed sequence applied to 10 MHz subchannel.
  + 1 is multiplied to lower 10 MHz subchannel
  is multiplied to upper 10 MHz subchannel
    k: subcarrier indices
Depending on TCS, some CSD values provide improved PAPR over L-STF, L-LTF and L-SIG comparing to reference PAPR values
 | PAPR [dB] in 20 MHz (99.9%, 8x oversampled) |  | 
CSD (ns) (TCS) | L-STF | L-LTF | L-SIG (Median)
-25 | 5.0489 | 5.7085 | 9.228
-50 | 4.3818 | 5.5877 | 8.5107
-75 | 3.8746 | 4.6096 | 8.0954
-100 | 3.5696 (5.2497) | 5.1641 (5.7927) | 7.3959 (9.3806)
-125 | 4.6851 | 5.3532 | 7.3918
-150 | 5.0674 | 5.8687 | 7.5948
-175 | 5.1405 | 5.6444 | 7.6878

## Slide 9: CSD (Cyclic Shift Delay) 2/2

## Slide 10: PAPR bottleneck of 20 MHz NGV PPDU
Gamma vector [+1, +j] does not seem to give any PAPR benefits
Phase rotation in DCM+MCS0 improves PAPR of legacy portion meaningfully.
  Prominently reduced PAPR of L-SIG
CSD generally provides reasonable PAPR values
  -100ns picked as an example
PAPR [dB] (99.9%, 8x oversampled) | L-STF | L-LTF | L-SIG (Median) | 20 MHz NGV-DATA
[ 1, +j ] Phase rotation | 5.2497 | 5.7927 | 9.3806 | 7.7349
Phase rotation in DCM+MCS0 | 4.8133 | 5.8799 | 6.9529 | 
CSD -100ns | 3.5696 | 5.1641 | 7.3959 | 

## Slide 11: Summary
20 MHz phase rotation {+1, +j} seems not to provide any benefits in terms of PAPR reduction
  PAPR simulation shows L-SIG is identified as bottleneck of 20 MHz PPDU transmission.
  PAPR of data portion is even better than PAPR of SIG field
11bd gives the great opportunity not to have PAPR bottleneck in L-SIG of legacy portion for 20 MHz operation.
  Phase rotation in DCM+MCS0 seems good.
    Simple implementation
    Already accepted in 11ax to reduce PAPR in DCM+MCS0 and HE-SIG-B in 11bd and 11ax
Currently, given OFDM numerology and format of 20 MHz PPDU not decided yet, further investigations are required.

## Slide 12: SP
Based on so-far simulation results of PAPR, which option(s) do you prefer for 20 MHz transmission in 11bd?
  Opt.1: legacy gamma vector with {1, +j}
    Y/N/A
  Opt.2: phase rotation in DCM (Dual Carrier Modulation) + MCS0
    Y/N/A
  Opt.3 : CSD (Cyclic Shift Delay)
    Y/N/A

## Slide 13: Reference
[1] 11-19/0514r6 Motion Booklet for IEEE 802.11 TGbd
[2] 11-19/0686r2 PHY Numerology Discussions