## Slide 1: Upper Layer Operation of Adjacent Channel Detector
Date: 2019-07-14
Authors:
Onn Haran, Autotalks

## Slide 2: Recap #1 – Introduction
Adjacent channel transmissions create mutual harmful interferences
The ability to utilize all channels is important to enablement of additional V2X use-cases
A simple mitigation scheme was presented in [1] and simulated in [2]: defer transmission while adjacent channel energy is detected
Outcome: Adjacent channel activity doesn’t interfere to nearby vehicles and not impacting latency
July 2019
Onn Haran, Autotalks

## Slide 3: Recap #2 – Adjacent Channel Detector
The receiver is detecting adjacent channel while tuned to its own channel. Not adding another receiver
The out-of-band emissions of lower and upper adjacent channels are observed
  Criteria would be “detection of strong signal shaped like OOB mask”
  Target energy could be aligned with ED threshold (-62dBm)
Onn Haran, Autotalks
Main Ch.
Adjacent Ch.
Observable OOB
(0MHz, -26dB)
(0.5MHz, -32dB)
(5MHz, -40dB)
(10MHz, -50dB)

## Slide 4: Operation flow
July 2019
Onn Haran, Autotalks
Upper layer decision
PHY/MAC
Adjacent channel(s) detection
CCA
PHY/MAC informs upper layer that adjacent channel transmission is detected
Upper layer decides if to defer transmission
  Upper layer considers aspects like channel load, packet latency, etc…

## Slide 5: Upper layer already deals with medium contention
Onn Haran, Autotalks
Synchronous transmission after IEEE1609.4 channel switching would create contention
IEEE1609.4 expects a solution but doesn’t describe it
“The specific approach that a device uses to avoid start-of-time slot contention is not specified in this standard.”

## Slide 6: Same concept can add adjacent channel detection
Onn Haran, Autotalks
Future upper layer standard can define guidelines for transmission deferral
Solution description can remain undescribed
Adjacent channel reception

## Slide 7: Straw Poll
Do you agree that 802.11bd shall include detector of adjacent channel reception?
Y:
N:
A:
July 2019
Onn Haran, Autotalks

## Slide 8: References
  [1] Simulation of multi-channel interference (IEEE802.11-19-320/r0)
  [2] Multi-channel interference mitigation (IEEE802.11-19-48/r0)
  [3] Adjacent channel detector (IEEE802.11-19-716/r1)
July 2019
Onn Haran, Autotalks