## Slide 1: LC MAC submission – follow up
Date: 2019-07-15
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: Abstract
This submission is follow-up of 757r2 [1]
We propose several MAC features for supporting PHYs and satisfying PAR
We also evaluate it with MAC simulator

## Slide 3: RTS/CTS
STAs cannot hear each other in normal LC BSS, which can lead to collision at UL transmission
  We may use RTS/CTS to resolve UL collision
However, RTS/CTS has some disadvantages such as overhead and latency
  Transmission for RTS and CTS frame consumes over 100 usec
We evaluate RTS/CTS performance in LC environment

## Slide 4: Simulation result for RTS/CTS in LC
Simulation Setting
  STAs are hidden each other
  Single BSS (No OBSS interference)
Simulation parameter
  BW: 20 MHz
  AP-STA distance: 5 meters
  MCS is fixed: MCS 7 (65 Mbps)
  MPDU size: 1500 bytes
  Number of STAs: 2 ~ 8 STAs
Traffic model
  Constant Bit Rate
  DL: 5 ~ 20 Mbps, UL: 1 Mbps
Metric
  Throughput
  Latency: Time taken for frame to enter the queue and successfully send out

## Slide 5: Simulation results

## Slide 6: Simulation results
RTS/CTS shows enhanced performance in only 8 STAs case
However, RTS/CTS only increases latency in 2 STAs and 4 STAs case
  Latency increase is even greater in UL
 |  | Tput [Mbps] |  | Latency [msec] | 
 |  | No RTS/ CTS | RTS/ CTS | No RTS/ CTS | RTS/ CTS
DL | 2 STAs | 20.0 | 20.0 | 1.59 | 2.16
 | 4 STAs | 10.0 | 10.0 | 3.47 | 4.07
 | 8 STAs | 4.4 | 5.0 | 663 | 10.3
UL | 2 STAs | 1.0 | 1.0 | 2.81 | 6.18
 | 4 STAs | 1.0 | 1.0 | 12.1 | 20.4
 | 8 STAs | 0.24 | 1.0 | 25.6 | 39.5

## Slide 7: RTS/CTS signaling
As we can see in simulation results and well-known fact, RTS/CTS has advantages only in dense environments
  RTS/CTS can increase latency in sparse network without any performance enhancement and latency increase is even greater in UL
It is desirable to use RTS/CTS in UL transmission only in dense environments
  However, it is difficult for a STA to recognize the current environments because the STAs are hidden each other
We may need to define a MAC signal for the AP to decide whether to use RTS/CTS on the STA

## Slide 8: RTS/CTS signaling
A STA shall use RTS/CTS before receiving any RTS/CTS signal for the AP
  This could protect the UL transmission from other associated STAs
If the STA received any RTS/CTS signal, it shall follow the RTS/CTS rule as indicated
If the AP determines that the current network is sparse, the AP can make STAs use RTS/CTS optionally
If the AP determines that the current network is dense, the AP can make STAs use RTS/CTS all the time
There are two methods for this signal
  Option 1: Broadcast method
  Option 2: Unicast method

## Slide 9: RTS/CTS signaling: Option 1
Signal for RTS/CTS usage in UL is transmitted in Beacon frame
Beacon period is divided into two durations
  RTS/CTS duration: A STA shall use RTS/CTS in UL
  Non-RTS/CTS duration: A STA can transmit a data frame without RTS/CTS
Duration setting can be changed in per a beacon or multiple of it

## Slide 10: RTS/CTS signaling: Option 2
AP can transmit signal for RTS/CTS off in MAC header of DL data
  The STA that received the signal can transmit a data frame without RTS/CTS
Signal for RTS/CTS on is similar way

## Slide 11: Multi-color operation
Followings are defined in other spec for efficient operation in wide-band and multiple channels
  BSS channel selection in TGac
  Social channels in WFA
If we define some channels with particular purposes, it would be helpful for LC to operate in wide-band
  Discovery channel
  Channel for specific PHY
  High data rate only channel

## Slide 12: Summary
We addressed and reviewed several MAC features for designing LC MAC
  RTS/CTS signal
  Multi-color operation

## Slide 13: References
[1] 11-19-0757-02-00bb-lc-mac-submission.pptx

## Slide 14: Straw poll
Do you agree to define a MAC signal that the AP can order the non-AP STA(s) to use RTS/CTS mandatory or not
Y N A