## Slide 1: Preamble Design Consideration for 11be
Date: 2019-07-09
Authors:

## Slide 2
Introduction
In [1], a concept of using common header with an auto-detection scheme for future amendments of 802.11, starting from 11be, was proposed
  We call “future amendments of 802.11, starting from 11be” as “11ax+” in this document
In general, this is a right direction for forward compatibility
  During the design of the preamble for 11ba PPDU, the similar issue was brought up and discussed
On the other hand, when designing a new preamble for 11ax+, it may be beneficial to keep some useful features in legacy (i.e., non-11ax+) protocols and allow legacy devices (e.g., 11ax) to understand part of 11ax+ PHY signals so that those devices can coexist nicely with 11ax+ devices for the benefit of overall network performance
In this contribution, we consider a specific feature in 11ax, which is TXOP signaling in SIG-A, and discuss how the network can benefit from sharing them among 11ax and 11ax+ devices and suggest a design choice

## Slide 3: Recap: 11ax SIG-A
In 11ax, the HE-SIG-A field contains some information (e.g., MCS) that typically provided in PHY header, and also contains other information that typically provided in the MAC header, e.g., TXOP, transmission direction, BSS color, spatial reuse
The main advantages of keeping some of the MAC information in PHY header:
  Low latency
  High reliability
With these advantages, the 11ax network and devices can benefit from
  Low power consumption
  Low probability of collision
  Low OBSS interference
  High flexibility

## Slide 4: TXOP in PHY Header
In 11ax, TXOP is explicitly signaled in the preamble for all PPDU types, B0 ~ B6 of HE-SIG-A2 (see figure in Appendix slide)
There are several benefits to signal TXOP in PHY header
  Allow reliable TXOP protection
  The unintended devices may go to power save mode without decoding MAC header
  The unintended OBSS devices can start listening to signals in their own BSS for quick response when it is possible
It would be desirable if 11ax+ PHY SIG can carry the same TXOP information and be understood by 11ax devices such that they can keep silent when a set of 11ax+ devices are operating
  Unintended 11ax devices, by checking the future-SIG-A field, can set NAV based on TXOP field so that they will not introduce interference to 11ax+ transmissions
  Some potential new features, e.g., HARQ, in 11ax+ that require more reliable UL/DL information exchange can benefit from it

## Slide 5: 11be Preamble Design Recommendation
To enable the capability mentioned above, we may need to
  Keep L-STF, L-LTF, L-SIG and RL-SIG as the same as 11ax
    High reliability and early detection for 11ax and 11ax+
  Keep B0-B6 in SIG-A2 for TXOP signaling as the same as 11ax HE-SIG-A2
L-STF
L-LTF
L-SIG
LENGTH%3 != 0
RL-SIG
11ax+:
8
8
4
4
Future-SIG-A1
4
BPSK
Future-SIG-A2
4
BPSK
BPSK
BPSK
Same as 11ax
B0~B6 for TXOP

## Slide 6: Conclusion
Since the 11ax and 11ax+ devices may coexist in the same or overlapping networks, it would be desirable to design the preamble for 11be such that it will keep some nice features in 11ax and, if possible, make some signals understandable to 11ax devices
  Those signals may include TXOP, SR, BSS Color, etc.
Notes: Remove SR

## Slide 7: Reference
[1] 11-19/1021r1 Preamble Design Harmonization

## Slide 8: Appendix: 11ax SIG-A fields