## Slide 1: Implicit sounding overhead analysis
Date: 2019-07-14
Authors:
Name | Affiliation | Address | Email
Sigurd Schelstraete | Quantenna Communications | 1704 Automation Parkway, San Jose, CA 95131, USA | sschelstraete@quantenna.com
Imran Latif |  |  | ilatif@quantenna.com
Debashis Dash |  |  | ddash@quantenna.com
Huizhao Wang |  |  | hwang@quantenna.com

## Slide 2: Introduction
Current 802.11 sounding protocols are based on sounding followed by explcit sounding feedback
These explicit protocols can take up a lot of airtime
Implicit sounding [1, 2] has been suggested as a way to reduce sounding overhead
This submission provides an analysis of overhead incurred by different sounding schemes

## Slide 3: Current sounding protocols
SU-type feedback
MU-type feedback

## Slide 4: Content of HE compressed Beamforming frame
Exact number of bits depends on channel dimensions
  Nc: #feedback streams
  Ns: #sounded streams
  Na: # angles in V-matrix compression (see next slide)
  bf, by: compression parameters
Only for MU-type feedback

## Slide 5: Values of Na
Number of angles (Na) as function of Nc and Nr
  802.11ax only defines up to Nr = 8
  802.11be may go up to Nr = 16

## Slide 6: Implicit sounding
Implicit sounding has been proposed as an alternative
  Beamformer requests NDP from Beamformee
    This allows estimation of the BFee  BFer channel
    Derive BFer  BFee channel from this estimate
  Requires calibration at AP side [3]
  Potential to reduce airtime overhead
Basic scheme:

## Slide 7: Implicit sounding (2)
Can be extended to receive multiple NDPs simultaneously
  Either multiplexed in MU-MIMO or e.g. tone-interleaved
  Sounded clients should have similar receive powers
    If not, multiple successive implicit soundings can still be used

## Slide 8: Additional considerations
Power differences between UL and DL
  Client transmit power can be lower than AP transmit power
    Could reduce the quality of the channel estimate
  This can be compensated for by repeating the training signals

## Slide 9: Some examples: overhead vs. frame

## Slide 10: Observations on explicit feedback
MU (OFDMA) does not always provide significant improvement for high-dimensional cases
  OFDMA does not reduce the amount of airtime needed for data transmission
  When protocol overhead is not dominant, MU sounding feedback does not provide much improvement
  MU feedback may be worse than SU feedback because of OFDMA inefficiencies in spectrum allocation and padding
MU-type feedback is not the ultimate solution for reducing sounding overhead

## Slide 11: Simulation results
Numerical examples to estimate time needed for sounding and feedback exchange
Assumptions:
  #sounding streams: 4, 8, 16
  NRX: 1, 2, 4
  Number of users: 4, 8
  Ng: 4
  MCS: 2
  BW: 80 MHz
  HE-LTF repeated 4 times for implicit sounding
  Assume OFDMA for MU-type feedback
  HE-LTF mode: 2x, GI: 0.8 msec

## Slide 12: Four different schemes simulated
“SU sounding”
“Implicit (successive)”
“MU sounding”
“Implicit (MU)”

## Slide 13: Numerical data – sounding and feedback absolute time

## Slide 14: Analysis
Explicit sounding takes up significant airtime for high-dimensional channels
Not much difference between successive SU soundings and MU-type sounding (OFDMA) for high-dimensional channels
Even with repeated training symbols, airtime taken by implicit sounding is an order of magnitude lower

## Slide 15: Numerical data – sounding and feedback relative overhead
What really matters is the total airtime overhead of channel sounding
  Needs to be considered in network context. Different scenarios will yield different answers
To allow us to quantify overhead, we use the following metric:
  Sounding overhead relative to single frame transmission
  overhead if we sounded the channel right before transmission and used the results only for precoding of the subsequent frame
  Not necessarily directly representative of network overhead, but allows quantitative comparison between sounding schemes

## Slide 16: Numerical data – sounding and feedback relative overhead (2)
Data

## Slide 17: Analysis
Overhead is extremely high for high-dimensional channels (8 or 16 sounded streams)
Overhead of implicit channel sounding is significantly lower
  Even low enough to allow per-packet sounding

## Slide 18: Conclusions
Implicit channel sounding offers significant potential for sounding overhead reduction
Proposal:
  Add Implicit sounding as an optional sounding mechanism for reducing sounding overhead
  Maintain Explicit sounding as the mandatory mechanism for backwards compatibility

## Slide 19: Straw Poll
Do you agree to add Implicit Channel Sounding as an optional sounding mechanism in 802.11be?

## Slide 20: References
[1] MU sounding improvements, IEEE 802.11-18/1191
[2] Implicit Channel Sounding in IEEE 802.11, IEEE 802.11-19/0768
[3] Implicit Channel Sounding in IEEE 802.11 (Feasibility Study), IEEE 802.11-19/0767