## Slide 1: Performance aspects of Multi-link operations
Date: 2019-07-01
Authors:
Name | Affiliations | Address | Phone | Email
Dmitry Akhmetov | Intel |  |  | 
Notes: September 2012

## Slide 2: Motivation for Multi-link operation.
New wireless devices are expected to have multi-band/channel capabilities
These new devices will/may be able to operate on different channels/band independently
  Independent channel access
  Independent TX / RX operation
  Unified TX/RX buffers for smooth and speedy operations
Benefits
  Increased/improved throughput, better load handling
  Improved end-to-end latency
  Data/mgmt plane separation
  Potential for link aggregation
  Enable new use cases
STA 1
STA 2
Link 1
Link 2

## Slide 3: Multi-link operation benefits
Obvious throughput performance numbers
  Mediatek in their simulations claim throughput gain of up to 2x-5x gain depending on link load & configuration
  Qualcomm in their simulations claim 1.1x-2.3x depending on links load
  Simple math says you can have 2x more water over 2 pipe than over 1 pipe
    Scales linearly with number of pipes
  Our internal simulations show the same 2x throughput gain over two links
    2x in ideal case
    Less with extra load on each link
Expected delay gain
  Theoretically up to 2x reduction of ETE delay but practically less
STA 1
STA 2
Link 1
Link 2

## Slide 4: Multi-link operation assumptions and classification
Assumptions
  A multi-link capable device perform channel access on multiple channels independently
  A multi-link device after obtaining TXOP on multiple bands/channels can transmit frames to the receiver(s) over multiple links
Classification
  Synchronous operation
  Asynchronous operation
  Semi-Asynchronous operation
  Restricted operations

## Slide 5: Classification: Completely synchronous
Existing 80+80 type operation
Good old “where is my secondary channel” style
  Perform contention on primary channel
  Do energy detect on secondary
    If IDLE – transmit over two channels
    If BUSY – transmit on primary only
band 1
band 2
AP1
AP2
3
2
1
0
TXOP
2
1
0
TXOP
busy
busy
TXOP
TXOP
3
2
1
0
busy

## Slide 6: Classification: Completely asynchronous
Perform contention independently on both links
Transmit/receive independently on both links
band 1
band 2
AP1
AP2
3
2
1
0
TXOP
9
8
7
2
1
0
busy
6
TXOP
TXOP
busy
3
2
1
0
5
4
4
3
2
1
3
0
TXOP
TXOP
2
1
0

## Slide 7: Classification: Semi-asynchronous
Perform contention independently
If one channel/link won contention it can invite another link into the transmission opportunity
  If second link is in IDLE/Contention state – transmit jointly
  Otherwise transmit using one link only
band 1
band 2
AP1
AP2
3
2
1
0
TXOP
9
2
1
0
busy
8
TXOP
TXOP
busy
3
2
1
0
7
6
7
6
5
TXOP
TXOP
TXOP
4
3
2
1
0
4

## Slide 8: DL case. Simulation setup.
AP1 and AP2 on separate non-overlapping channels with 1 associated STA each
SU HE, 2x2x80, MCS11
BSS load: UDP traffic in DL direction with load of
  Percentage of MCS11 @ 2x2x80 rate (of ~1.2Gbps) : 25% - 300Mbps, 50% - 600Mbps and 100% - 1.2Gbps
1 to 10 OBSSes with bidirectional UDP traffic with total load pre OBSS of 10% of MCS11 at each channel
  Each OBSS consist of 1 AP and 1 STA
TXOP limit of 5.4ms
  Randomized TXOP limit for OBSS, uniformly distributed between 1ms and 5.4ms
  No TXOP bursting
Metrics of interest
  Throughput
  # of synchronous/asynchronous operations and ratio of the two
    Synchronous operation – simultaneous transmission start on both links

## Slide 9: Naming convention
Single
  Single link operation
Sync
  Single link 80+80 type operation
Async
  Fully asynchronous operation
Join
  Semi-asynchronous operation

## Slide 10: Single link vs Multi-link. DL case

## Slide 11: Single link vs Multi-link. DL case

## Slide 12: Single link vs Multi-link. DL case

## Slide 13: Chances of synchronous operation.
Notes: This is going to be changed to show % of “synchronous operations”

## Slide 14: DL / UL case. Simulation setup.
AP1 and AP2 on separate channels with 1 associated STA each
SU HE, 2x2x80, MCS11
BSS load: symmetrical UDP traffic in DL and UL direction with total BSS load of
  Percentage of MCS11 @ 2x2x80 rate (of ~1.2Gbps)
    25% - 300Mbps, 50% - 600Mbps and 100% - 1.2Gbps
1 to 10 OBSSes with bidirectional UDP traffic with load of 10% of MCS11 at each channel
  Each OBSS consist of 1 AP and 1 STA
TXOP limit of 5.4ms
  Randomized TXOP limit for OBSS, uniformly distributed between 1ms and 5.4ms
  No TXOP bursting
Metrics of interest
  Throughput
  # of synchronous/asynchronous operations and ratio of the two
    Synchronous operation – simultaneous transmission start on both links

## Slide 15: Single link vs Multi-link. DL/UL mix case

## Slide 16: Single link vs Multi-link. DL/UL mix case

## Slide 17: Single link vs Multi-link. DL/UL mix case

## Slide 18: Chances of synchronous operation, DL / UL mix case.

## Slide 19: Intermediate conclusion
2 links is definitely better than 1 link
With lightly loaded networks 2x gain can be achieved
The gain decreases with the increase of a load
Semi-asynchronous operation outperform on average all other modes
Chances for synchronous operations (concurrent) on two bands (i.e. to obtain channel at the same time) are not high
  Quickly dropping to ~5% and below as the load increases

## Slide 20: Complicated life of a device with co-located radios
May need to impose constraints on concurrent TX/RX operations on different bands
  For, example, interference across links/radios - TX on band 1 can impact radio on band 2 (and vice versa).
  Devices radio capabilities / implementation may not allow for concurrent operation
No TX operation is possible on band1 if band 2 is busy with RX operation and vice versa
band 1
band 2
AP1
AP2
3
2
1
0
3
2
1
0
Tx data
Rx ack
Rx data
TXOP
TXOP
3
2
Rx
4
5
Tx data
Rx ack
Tx data
Rx ack
Tx data
Rx ack
Tx data
Rx ack
TXOP
TXOP
Tx data
Rx ack
Tx ack
Tx

## Slide 21: Simulation setup.
Traffic load, PHY config, etc. is the same as before
Semi-synchronous with restrictions mode of operation – “restricted join”
Asynchronous with restrictions mode of operation – “restricted async”
Channel access rules / TX operations restrictions/constraints
  Device has to meet the constraints by truncating or deferring own TX operations
      Suspend\restart backoff during possible overlapping operation
      If the other Device in TX state, limit own TX duration to match end of the other AP transmission

## Slide 22: Restricted vs Unrestricted. DL case

## Slide 23: Restricted vs Unrestricted. DL case

## Slide 24: Restricted vs Unrestricted. DL case

## Slide 25: Chances of synchronous operation

## Slide 26: Restricted vs Unrestricted. DL/UL mix case

## Slide 27: Restricted vs Unrestricted. DL/UL mix case

## Slide 28: Restricted vs Unrestricted. DL/UL mix case

## Slide 29: Chances of synchronous operation

## Slide 30: Conclusion
  For STAs without Tx/Rx constraints, asynchronized access performs very well, as expected
  For STAs that have Tx/Rx constraints, asynchronized access with restrictions preform much better than fully synchronized access
  Average performance gain from multi-link operation
    Asynchronous operation, DL case: 2.07x
    Asynchronous operation, DL / UL mix case: 2.02x
    Semi-asynchronous operation, DL case: 2.28x
    Semi-asynchronous operation, DL / UL mix case: 2.22x
    Restricted asynchronous operation, DL case: 1.91x
    Restricted asynchronous operation, DL / UL mix case: 2.09x
    Restricted semi-synchronous operations , DL case : 2.22x
    Restricted semi-synchronous operations , DL / UL mix case : 2.21x
    Completely synchronous operation, DL case: 1.27x
    Completely synchronous operation, DL / UL mix case: 1.29x