## Slide 1: Assignment of Temporary Addresses
Date: 2019-07-17
Authors:
Name | Affiliations | Address | Phone | email
Roger Marks | EthAirNet Associates | Denver, CO, USA | 1-802-capable | roger@ethair.net

## Slide 2: Abstract
This contribution provides views on the assignment of temporary addresses in IEEE 802.11. It is intended for the information and consideration of the IEEE 802 RCM TIG. This contribution is a followup to “Temporary Addresses” 2019-05-13 (IEEE 802.11-19-0884r00)

## Slide 3: Temporary Addresses in IEEE 802
IEEE 802 MAC address space is half global, half local
  Global: EUI-48 based on OUI-48; typically permanent
  Local: typically temporary
Temporary addresses can serve many different purposes
Temporary addresses may be useful in 802.11
Vital to ensure that the address types are distinguishable
Foundation of distinguishable local addresses is established in IEEE Std 802 (per 802c-2017 amendment)

## Slide 4: Assignment Protocols, per IEEE Std 802
An address assignment protocol assigning local MAC addresses to devices on a LAN should ensure uniqueness of those addresses.
When multiple address assignment protocols operate on a LAN without centralized administration, address duplication is possible, even if each protocol alone is designed to avoid duplication, unless such protocols assign addresses from disjoint address pools.
Administrators who deploy multiple protocols on a LAN in accordance with the SLAP will enable the unique assignment of local MAC addresses within the LAN as long as each protocol maintains unique assignments within its own address subspace.

## Slide 5: Address Assignment Protocols
See IEEE Project P802.1CQ (“Multicast and Local Address Assignment”) in IEEE 802.1 TSN Task Group
  https://1.ieee802.org/tsn/802-1cq/
Pure random – no duplicate detection
  Create an address and go
  Simple
  Requires huge address space to avoid collisions
Client/server
  Address assignment upon request
  Avoids collisions; operates in a small address space
Peer-to-peer claiming
  Propose an address and check for duplication

## Slide 6: Privacy
Permanent addresses can limit privacy
Privacy is enhanced by use of temporary addresses
  True for random addresses
  True also for assigned addresses (e.g. DHCP)
Not all devices have privacy requirements
  e.g. infrastructure

## Slide 7: A Shared Space
The IEEE 802 address space is a shared one
In 802.11, the address space is shared by, e.g.
  APs
  Mobile phones
  Desktop computers
  Industrial equipment
  Televisions
  Printers….
The addressing requirements may vary.
  e.g. varying privacy requirements
Some address protocols support privacy, authentication, etc. [6]

## Slide 13: Summary
The local address space is huge and valuable.
Wireless LANs serve many purposes.
In a single wireless LAN, the address space is shared by many types of devices with different needs.
Let’s make room for multiple schemes to flourish and serve multiple purposes.

## Slide 14: References
[1] R. Marks, “Local MAC Addresses in the Overview and Architecture based on IEEE Std 802c,” 2017-09-13 (IEEE 802.11-17/1466r01)
[2] IEEE Std 802c: IEEE Standard for Local and Metropolitan Area Networks: Overview and Architecture – Amendment 2: Local Medium Access Control (MAC) Address Usage (2017-06-15)
[3] IEEE Project P802.1CQ, Multicast and Local Address Assignment <https://1.ieee802.org/tsn/802-1cq>
[4] R. Marks, A. de la Oliva, S. McCann, and M. Hamilton, “MAC Address Policy ANQP,” 2019-07-08 (IEEE 802.11-19/0286r7)
[5] R. Marks, “Illustrations of Local MAC Address Policy ANQP Proposal,” 2019-07-16 (IEEE 802.11-19-1307r00)
[6] R. Marks, “Temporary Addresses,” 2019-05-13 (IEEE 802.11-19-0884r00)