## Slide 1: Virtual BSS for Multi-AP Coordination Follow-up
Date: 2019-09-15
Authors:

## Slide 2: TGbe Multi-AP Coordination
Multi-AP Coordination is a candidate feature being discussed in TGbe group
There are many categories of multi-AP coordination including joint processing, coordinate OFDMA, null forming, coordinated beamforming, AP selection, etc.
In both downlink and uplink, the AP(s) used may vary dynamically based on link quality, load balancing, etc. [1][2][3][4]

## Slide 3: Multi-AP Coordination Requirements
Seamless exchange of frames between STA and coordinating APs without negotiation overhead
  Simultaneous connectivity with multiple APs
Secure connection between STA and coordinating APs
  Single authentication and association state
  Encryption for different flavors of multi-AP transmission
In this presentation, we focus on the authentication and association

## Slide 4: 802.11 Authentication Recap
Network discovery
802.11 open authentication
802.11 association
802.1X/SAE/FILS authentication
  Skipped if pre-shared keys
  Master session key generated
  Master keys for unicast (PMK) and group addressed (GMK) frames at AP and STA
4-way handshake
  AP and STA confirm they have same PMK
  Temporal keys generated (PTK, GTK, IGTK)

## Slide 5: 802.11r Mobility Domain Recap (1/2)
Protocols for reducing security overhead in roaming
Assumes WLAN Controller securely connected to APs
Full authentication performed at initial association with mobility domain
Fast BSS transition (FT) key hierarchy
  PMK-RO at WLAN controller, separate PMK for each AP
WLAN Controller
AP 1
AP 2
STA
Mobility
Domain
WLAN
Controller
AP 1
AP 2

## Slide 6: 802.11r Mobility Domain Recap (2/2)
Full authentication during initial association with mobility domain
  PMK-RO generation at WLAN controller
  PMK-R1s derived and distributed to APs
4-way handshake
  Temporal keys generated with only the associated AP
Fast transition protocols
  802.11 authentication frames enriched with new IEs
  Temporal keys generated with target AP
Is 802.11r sufficient for EHT Multi-AP?
  No simultaneous connection to multiple APs
  However, we can extend/re-use FT protocols

## Slide 7: Virtual BSS
Infrastructure BSS with a group of APs coordinated by V-BSS coordinator
Seamless transmission of data frames to and from multiple APs
  Presented in July meeting [3]
  Dynamic AP selection by STA and V-BSS Coordinator
  Transparent data reception
Single association and authentication state maintenance
  Focus of this presentation

## Slide 8: Virtual BSS Initial Association
  Virtual BSS operation advertised in Beacons, Probe Response, (Re) Assoc Response
  Open authentication and association performed with a specific AP of Virtual BSS
    Association Request indicates request to join the Virtual BSS
  Association Response includes V-BSS Coordinator key holder ID
    Used to generate PMK at STA and V-BSS Coordinator similar to 802.11r PMK-R0
  Temporal key generation depends on the Virtual BSS architecture
    Partition of functionalities between the V-BSS Coordinator and APs
  Virtual BSS Authentication modes
    Option 1: Temporal key generation with V-BSS Coordinator
    Option 2: Temporal key generation with individual APs
  Selected mode needs to be indicated to STAs joining the Virtual BSS
    Example: Association Response

## Slide 9: Option 1: Temporal Key generation with V-BSS Coordinator
Temporal keys generated between STA and V-BSS Coordinator using PMK-Coordinator
V-BSS Coordinator performs data encryption and decryption
APs serve as a relay forwarding packets to and from V-BSS coordinator and STA
Derives PTK

## Slide 10: Option 2: Temporal Key generation with individual APs
PMK-AP derived from PMK-Coordinator and distributed by V-BSS Coordinator to APs
STA can generate temporal keys with multiple APs of Virtual BSS
  802.11r protocols can be extended for the key generation with the individual APs
Separate keys maintained for each AP
  Corresponding keys used for communication between STA and AP
Dynamic AP selection limited to the subset with whom temporal keys are generated

## Slide 11: Multi-AP Coordination Capability
Category | Temporal keys with V-BSS Coordinator | Temporal keys with individual APs
Coordinated OFDMA |  | 
Coordinated Beamforming |  | 
Null Forming |  | 
Joint AP Transmission |  | X
In joint AP transmission, multiple APs transmit exact same data to STA

## Slide 12: Further Consideration
Security assessment of Virtual BSS Authentication modes
Addressing for transparent data reception
Secure channel between the V-BSS Coordinator and APs
Data flow between the STA and Virtual BSS

## Slide 13: Summary
To achieve seamless transmission of frames between STAs and APs participating in Multi-AP Coordination, security framework needs important consideration
Presented Virtual BSS association protocol
Depending on Virtual BSS architecture partition, temporal key generation can be performed directly with V-BSS Coordinator or with individual APs

## Slide 14: References
[1] 11-19/1019, “Virtual BSS for Multi AP Coordination”
[2] 11-19/0089, “Distributed MU-MIMO Architecture Design Considerations”
[3] 11-19/0804, “Multi-AP Transmission Procedure”
[4] 11-19/1129, “Consideration on Multi-AP Coordination”