## Slide 1: Harmonization for 20MHz Channel Access
Date: 2019-09-16
Authors:
Name | Affiliation | Address | Phone | Email
Insun Jang | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | insun.jang@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com

## Slide 2: Introduction
There have been several proposals for 20MHz channel access [1]-[4]
  However, any agreements have not been reached
  With this document, we consider harmonization on 20MHz channel access based on members’ opinion/discussion, thus leading to consensus

## Slide 3: Current Status
Common Preference
  Reducing complexity: Use of a single radio (RF chain, or receiver)
  Two 10MHz sub-channels exist in a 20MHz channel
  Fairness on two 10MHz sub-channels consisting 20MHz channel
    Needs to consider trade-off between fairness and transmission opportunity of 20MHz bandwidth PPDU (i.e., performance of 20MHz transmission)
From our common view, the following channel access is not preferred
  That shall use dual or more radios
  This approach will be excluded in following slides

## Slide 4: Details for Common Preference
  From “Use of a single radio” and “Two 10MHz sub-channels in a 20MHz channel”, we can draw a conclusion that preamble detection (PD) sensing is used in at least one 10MHz sub-channel
    It means an 11bd STA is capable of setting NAV in at least one 10MHz sub-channel
    20MHz channel access shall use a backoff counter
  From “Fairness on two 10MHz sub-channels”, we can draw a conclusion that two 10MHz sub-channels use the same sensitivity level
  Same sensitivity level would be -85dBm or lower (TBD) (from Motion #6 [6])
Discussion
Points

## Slide 5: NAV Setting for Two 10MHz Sub-Channels
  Option 1: NAV setting only for one 10MHz sub-channel
  It would provide fairness equally for one 10MHz sub-channel
  Like legacy Wi-Fi system using wide bandwidth, one 10MHz sub-channel (where NAV is not set) uses guard interval (GI) detection [5] or energy detection (ED)
  If -85dBm or lower set to them can provide fairness properly to STAs over the channel at the expense of 20MHz transmission
  Option 2: NAV setting for both of 10MHz sub-channels
  It would provide fairness equally for two 10MHz sub-channels
  However, it cannot ensure that NAV setting for both is always possible
    Assuming two 10MHz sub-channels are A and B, during decoding NAV of PPDU in channel A, NAV of another PPDU incoming on channel B cannot be decoded, i.e., cannot set NAV
We prefer Option 1: Because Option 1 can provide the proper fairness by relaxing the sensitivity threshold and sensing interval, and can have a simple implementation while Option 2 has the concern that the case two NAVs cannot be set can occur

## Slide 6: How to Do Back-off Decrement
  Option 1: Based on the channel state of one 10MHz sub-channel
  It follows the backoff procedure of Legacy Wi-Fi system, but AIFS is used instead of PIFS
  Backoff counter decreases depending on the channel state of one 10MHz sub-channel
  When the back-off counter becomes zero and another 10MHz sub-channel was idle during AIFS interval immediately preceding the start of the TXOP with -85dBm or lower receive sensitivity threshold, 20MHz PPDU is transmitted using two 10MHz sub-channels

## Slide 7: How to Do Back-off Decrement (Cont’d)
  Option 2: Based on the channel state of two 10MHz sub-channels
  It modifies Option 1 with the consideration of additional channel state
  Backoff counter decreases depending on the channel state of two 10MHz sub-channels
  Basic Procedure
    The backoff counter decreases when both of 10MHz sub-channels are idle
    When the back-off count becomes zero, 20MHz PPDU is transmitted using two 10MHz sub-channels
    More details are needed to be defined

## Slide 8: Discussion on How to Do Back-off Decrement
  In Option 1, an 11bd STA performs EDCA channel access only based on the state of a 10MHz sub-channel without the consideration of 10MHz STAs operating in another 10MHz sub-channel
  It would be unfair to the 10MHz STAs
  Option 2 can provide better fairness to the 10MHz STAs
We prefer Option 2 for providing fairness to STAs operating in both of 10MHz sub-channels as much as possible

## Slide 9: Opportunistic 10MHz Transmission
We don’t have strong opinion on opportunistic 10MHz transmission (i.e., 10MHz fallback)
Some concerns should be considered, e.g.,
  Adjacent Channel Interference (ACI)
  Mismatch between upper layer’s indication (i.e., 20MHz transmission) and decisions in 11bd
If some concerns are still unresolved, then it would be better not to permit opportunistic 10MHz transmission

## Slide 10: How to Set two 10MHz sub-channels
  As in [1], an 11bd STA can set two 10MHz sub-channels upon request from upper layer
  According to 11p and IEEE 1609, operating channels for channel switching and data transmission are indicated from upper layer using the channel information (e.g., Channel identifier as a parameter which includes Country String, Operating class, Channel Number)
However, we haven’t determined a specific channel access including the role of two 10MHz sub-channels
  We would determine how to set two 10MHz sub-channels after resolving the channel access method

## Slide 11: Summary
  We considered harmonization on 20MHz channel access based on members’ opinion/discussion, thus leading to consensus
  Specifically, we divided into two points, i.e., Common preference and Discussion point
  For discussion point, we considered 1) NAV setting for two 10MHz sub-channels and 2) how to do back-off decrement

## Slide 12: SP #1
Do you agree to add the following text into 11bd SFD?
  A 20MHz channel includes two contiguous 10MHz channels
  20MHz channel access shall use sensing and backoff procedure for both of 10MHz channels
  20MHz channel access shall use only one backoff counter
  Two contiguous 10MHz channels shall use the same receive sensitivity level
Y/N/A: 19/0/7

## Slide 13: SP #2
Do you agree to add the following text into 11bd SFD?
  20MHz channel access performs a backoff procedure based on the channel states of two contiguous 10MHz channels
    The backoff counter decreases when two contiguous 10MHz channels are idle
      Idle states are checked by TBD sensing methods (e.g., Packet detection, GI detection, energy detection)
    More details are TBD
Y/N/A: 18/0/3

## Slide 14: References
[1] 802.11-19/1103r0, 20MHz Channel Access in 11 bd: Follow-up
[2] 802.11-19/1156r0, 20MHz channel usage options
[3] 802.11-19/1105r0, Study on 20MHz Channel Access Schemes
[4] 802.11-19/1076r0, medium access with 20MHz BW
[5] 802.11-10/0744r1, Improved CCA for 80 and 160 MHz BSSs
[6] 802.11-19/0514r6, Motion Booklet for IEEE 802.11 TGbd