## Slide 1: Further discussion for 11be preamble
Date: 2019-09-16
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Jinmin Kim |  |  |  | Jinmin1230.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Sept. 2019

## Slide 2: Introduction
11be preamble is under discussion.
  In [1 ~ 5], following issues were introduced and discussed.
    Backward compatibility and coexistence
      Including of L-preamble ( L-STF , L-LTF and L-SIG ) in 11be preamble
    Packet classification
      Indication using the PHY identifier (i.e., information bits) / RL-SIG / signature sequence.
    Range extension
      RL-SIG can be used to support the coverage extension such as 11ax.
    Contents and configuration of SIG field
In this contribution, we investigate how to differentiate the received PPDU when RL-SIG is assumed in 11be PPDU and take a look at the consideration for configuration of 11be SIG field to support the auto-detection.

## Slide 3: Recap : 11be preamble
As shown in [3], 11be PPDU can be composed as follows
  For coexistence with legacy devices, L-Preamble should be included in 11be PPDUs.
    By using the L-preamble in 11be PPDU, it can prevent the collision with legacy devices on the channel during 11be transmission.
  In addition, by including the RL-SIG in the 11be PPDU, we can expect the followings.
    It enables to support the comparable coverage with 11ax.
    It can guarantee reliable transmission when small RU size is used for transmission.
L-SIG
EHT-SIG
L-STF
L-LTF
RL-SIG
…

## Slide 4: RL-SIG
Assuming RL-SIG is included in 11be PPDU, 11be devices can progress the auto-detection which has been adopted in 11ax.
Auto-detection with RL-SIG
  First step : Repetition check
    As introduced in [6], multiple ways in frequency domain can be considered
  Second step : L-SIG contents check
    Parity check = OK
    Rate check = 6Mbps
    Length field (mod 3) = ?
  By MRC of L-SIG and RL-SIG, enable range extension.
Repetition check
MRC & Contents check
Legacy detection
(11n/11ac/11a)
Received PPDU
N
N
Y
11ax or 11be

## Slide 5: Auto-detection (1/3)
By using the symbol modulated with BPSK after L-SIG and RL-SIG, 11be devices can distinguish whether received PPDU is 11be format or 11n/11ac format.
  RL-SIG in 11be PPDU does not impact the detection of 11n/11ac PPDU.
For the distinction of PPDU between 11ax and 11be, we can consider the following options for length field of L-SIG.
  Option 1: length mod 3 != 0
  Option 2: length mod 3 = 0

## Slide 6: Auto-detection (2/3)
Option1
  Due to using of equal RL-SIG with11ax, it requires the additional method such as PHY identifier(or fixed information bits) to differentiate the 11be PPDU.
    it may be included in symbol follows the RL-SIG.
      For example, it can be included in EHT-SIG fields
  So, 11be devices can differentiate whether received PPDU is 11be PPDU or not after decoding of symbols that include the PHY identifier (or fixed information bits).
    It is not easy to identify PPDU formats early.
  On the other hands, 11ax devices always treat the 11be PPDU as an 11ax PPDU and they will try to keep decoding subsequent fields (i.e., HE-SIG).
    11ax devices can wait for duration which is indicated in length field after the fail of validation check for HE-SIGA.
L-SIG
EHT-SIG
L-STF
L-LTF
RL-SIG
…
Length mod 3 != 0

## Slide 7: Auto-detection (3/3)
Option2
  Both 11ax devices and 11be devices can easily decide that it is not an 11ax PPDU by using the value of the length field.
    After checking the length field, 11ax jumps back to the legacy state machine. i.e., 11a/11n/11ac, if length mod 3 is zero.
  And, we can further identify 11be PPDU from 11ba PPDU. (if needed)
    By using another repetition check, 11be can distinguish whether the 11be or 11ba.
      Performing of repetition check with RL-SIG and one symbol after RL-SIG.
L-SIG
EHT-SIG
L-STF
L-LTF
RL-SIG
…
Length mod 3 = 0

## Slide 8: Comparison
 | Option 1 | Option 2
Classification method | Identifier | Similar way with conventional (i.e. 11ax)
length field | Mod 3 != 0 | Mod 3 = 0
Backward compatibility (Detecting legacy PPDU) | Yes* | Yes*
Extensibility | Good | Not flexible
Early detection | Relatively late (depending on SIG field design) | Relatively early
* : assuming proper design on SIG fields

## Slide 9: Consideration for EHT SIG
To use the PHY identifier for the packet detection, it should be indicated as early as possible.
However, generally, the SIG fields(ex., VHT-SIG, HE-SIGA) are configured with two OFDM symbols.
  The number of symbol for 11be SIG field may be larger than two.
So, after finishing of decoding of two symbols if EHT-SIG consists of two OFDM symbols, we can confirm the PHY identifier for the indication of PPDU format.
  It can cause the late detection.
L-SIG
EHT-SIG
L-STF
L-LTF
RL-SIG
Time
EHT-SIG
…
2 symbol
11be detected

## Slide 10: Configuration of SIG field
For the early indication and reasonable timing, SIG field can be composed of two parts.
  The first part(e.g., SIG1) can consist of one symbol containing 26 data bits.
    As contents for 26 data bits, PHY identifier, CRC, tail bit and other contents can be included in this part.
      CRC or Tail bits may be omitted.
  The second part(e.g., SIG2) can consist of two or more symbols.
    The second part also includes the common control information , CRC and tail bit for data bits.
  Each part shall be encoded at the rate, R=1/2, be interleaved, be mapped to a BPSK constellation, separately.
L-SIG
EHT-SIG1
L-STF
L-LTF
RL-SIG
EHT-SIG2
…
1 symbol
11be detected
2 symbol or more

## Slide 11: Summary
For the coexistence with legacy devices (i.e., 11a, 11n, 11ac, and 11ax), 11be PPDU should include the legacy preamble (i.e., L-STF, L-LTF and L-SIG).
We take a look at the auto-detection method when RL-SIG is included in 11be PPDU.
  RL-SIG does not impact to auto-detection of legacy devices.
  For the distinction between PPDUs, the value of length field in L-SIG , as well as PHY identifier, can be considered.
  The PHY identifier can provide scalability to differentiate the next wi-fi, but more time may be required for packet classification.
For the early indication of PHY identifier and reasonable timing for detection, we can consider the EHT-SIG field that can be composed of two parts.
  First part can consist of one symbol including the identifier.
  The second part can consist of two or more symbols.

## Slide 12: SP1
Do you agree that 11be PPDU shall include the legacy preamble (i.e., L-STF ,L-LTF and L-SIG) for coexistence with legacy PPDUs(i.e., 11a,11n,11ac,11ax)?

## Slide 13: SP2
Do you agree that the preamble of 11be PPDU includes repeated L-SIG after L-SIG?
Y:39/N:11/A:30

## Slide 14: SP3
Which option do you prefer to classify the 11be PPDU from other PPDU?
  Option 1 : described in slide 6
    RL-SIG including the length field set to mod3 != 0
    Bit information for 11be packet indication
  Option 2 : described in slide 7
    RL-SIG including the length field set to mod3 = 0
    Two repetition check (if classification with 11be is needed)

## Slide 15: SP4
Do you agree that the PHY identifier(or information bits) indicating the PPDU type(e.g., 11be and next ) is included in SIG field of 11be PPDU?

## Slide 16: Motion 1
Move to add the following text into the 11be SFD
  11be PPDU shall include the repeated L-SIG after L-SIG
  Move : Dongguk Lim
  Second :

## Slide 17: Reference
[1] IEEE 802.11-19/1021r1, Preamble Design Harmonization
[2] IEEE 802.11-19/1099r1, Preamble structure in 11be
[3] IEEE 802.11-19/1142r0, Discussion on the preamble for 11be
[4] IEEE 802.11-19/1214r0, Preamble Design Consideration for 802.11be
[5] IEEE 802.11-19/1085r0, high-level-eht-preamble-structure
[6] IEEE802.11-15/0579r2, 802.11ax Preamble Design and Auto-detection

## Slide 18: Appendix

## Slide 19: Preamble Auto-Detection for legacy
Preamble for legacy