## Slide 1: 802.11be Preamble and Auto-Detection
Date: 2019-09-15
Authors:

## Slide 2: Introduction
Previously, we share our views on 11be preamble structure [1]. In this contribution, we further give an analysis on three options of auto-detection for 11be.
Several methods can be considered for auto-detection of 11be
  Using different patterns of RL-SIG
    mask the RL-SIG by a polarity sequence [2]
  Using a signature symbol [3]
  Detecting BPSK/QBPSK [4]
Three options of auto-detection for 11be are analyzed:
  Give simulation results for these three options
    PER
    Miss detection
    False detection
  Show the observations and conclusions

## Slide 3: Recap: Auto-Detection
Auto-detection is implemented in the dashed rectangle. The main methods include detecting RL-SIG, detecting BPSK/QBPSK, checking SIG, etc.

## Slide 4: Three Options (1/2)
    Options
  Opt 0: Add a masked RL-SIG
  Opt 1: Add a masked RL-SIG and detect the modulation type (QBPSK) of the 1st symbol after the masked RL-SIG
  Opt 2: Add a masked RL-SIG and a signature symbol
    Note
  The red color on the right side represents that the corresponding modules are utilized for auto-detection
Here we consider three options.

## Slide 5: Three Options (2/2)
 | Detect RL-SIG | Check combined-SIG | Check BPSK/QBPSK | Check signature
Opt 0 | √ (+Mask) | √ |  | 
Opt 1 | √ (+Mask) | √ | √ (QBPSK) | 
Opt 2 | √ (+Mask) | √ |  | √
Options
Modules
Detection modules
  Detect RL-SIG (by correlation values)
  Check combined-SIG (rate, length mod 3, parity)
  Detect BPSK/QBPSK
  Check signature
  Note that:
  All these options use combined-SIG for SIG checking (rate, length, parity)
  In Opt 0, 1 and 2, RL-SIG is multiplied by a polarity sequence to form a masked RL-SIG
  Signature design
  Here we compare 12 pre-defined bits as an example
The used modules of different options are shown here

## Slide 6: Simulation Configurations
Bandwidth | 20 MHz
Channel model | TGn/TGac
UL/DL | DL
Channel condition | NLOS
Antennas | 1x1
CFO | 20 ppm
To show the performance of different options, we simulate them. Some simulation configurations are shown here.

## Slide 7: PER Performance
Compared with only decoding L-SIG, decoding combined-SIG achieves a better PER performance because of the combination of L-SIG and RL-SIG.

## Slide 8: Miss Detection
Here we show the performance on miss detection of different options. The performance of the first two options are mainly limited by checking combined-SIG, while the performance of Opt 2 is mainly limited by checking the signature.

## Slide 9: Miss and False Detection (Opt 0)
This figure shows the miss/false detection performance of Opt 0.

## Slide 10: Miss and False Detection (Opt 1)
This figure shows the miss/false detection performance of Opt 1. Obvious improvements in false detection can be achieved by detecting QBPSK.

## Slide 11: Miss and False Detection (Opt 2)
  The performance of miss detection is mainly limited by the signature PER. A much better performance of false detection is achieved by Opt 2

## Slide 12
Observations
Option 1
  Opt 1 has almost the same miss detection performance as Opt 0.
  Obvious improvements in false detection can be achieved by detecting QBPSK.
  Option 2
  Opt 2 uses a pre-defined signature field to do auto-detection. The contents of the signature can be further discussed (e.g. standard version). Suggest to include CRC and Tail bits in the signature symbol to provide early detection.
  The performance of miss detection is mainly limited by the signature PER.
  A much better performance of false detection is achieved by Opt 2.

## Slide 13
Conclusions
According to our observations, we propose the following format for auto-detection in 11be
  L-SIG + RL-SIG (variant) + signature symbol (QBPSK),
  which ensures both the miss detection and false detection performance.

## Slide 14: Straw Poll
Do you agree to apply the following auto-detection methods for 11be:
  L-SIG + RL-SIG variant + signature symbol (QBPSK).
  RL-SIG variant is different from RL-SIG in 11ax. Exact RL-SIG variant details are TBD.
  Signature symbol contents are TBD.

## Slide 15
[1] IEEE 802.11-19/1099r0 preamble structure in 11be
[2] IEEE 802.11-19/1142 Discussion on the Preamble for 11be
[3] IEEE 802.11-15/0643r0 auto-detection with signature symbol
[4] IEEE 802.11-10/0549r2 TGac Preamble Auto-Detection Comparisons
[5] IEEE 802.11-19/1214r0 Preamble Design Consideration for 802.11be
[6] IEEE 802.11-19/1021r1 Preamble Design Harmonization
[7] IEEE 802.11-19/1085r0 High-level EHT Preamble Structure
References