## Slide 1: Auto-Detection in 11be
Date: 2019-11-10
Authors:
Name | Affiliation | Address | Phone | Email
Hyobin Yim | Newratek |  |  | hb.yim at newratek.com
Si-Chan Noh | Newratek |  |  | sc.noh at newratek.com
Yujin Noh | Newracom |  |  | yujin.noh at newracom.com

## Slide 2: Introduction
To support 11be, the basic requirements is backward compatibility and coexistence with legacy device
In [1], [2], EHT preamble design criteria is discussed
  Simple implementation
  Support future device extend-ability
We consider the signature symbol which has been previously investigated in [3], to classify between legacy PPDU and 11be format including further future amendments
In this contribution, with simulation results, the signature symbol is taken into account to detect 11be format

## Slide 3: Signature Symbol in EHT-SIG
RL-SIG in 11be PPDU format is under discussion
Signature symbol
  Signature sequence (e.g., 3-10 bits) in [2], [3]
  Reserved bits or control bits (e.g., 2-9 bits)
  CRC can include 8 bits
  Tail 6 bits
Number of cases of different signature sequence successfully classify the future device
  Fixed n bits for signature sequence support PPDU format
L-STF
L-LTF
L-SIG
EHT-SIG
Signature symbol
EHT-SIG
RL-SIG

## Slide 4: RL-SIG in 11be PPDU
Assuming RL-SIG is included in 11be PPDU, 11be devices follow the same auto-detection method which has been adopted until 11ax
After conduct the legacy auto-detection method until 11ax, the 11be devices can classify the PPDU format between 11ax and 11be by checking the signature sequence
In this contribution, we consider the same length field of L-SIG in 11be format as 11ax
  Length mod 3!==0
Repetition Threshold > α
MRC & Contents check
Legacy
Detection
Received PPDU
N
N
Y
11be
Signature
Sequence
check
Y
11ax
11a
11n
11ac
N

## Slide 5: Simulation Configuration
General configuration:
  1-4 TX, 1 RX, 1 SS
# of channel realizations: 10,000
DNLOS, UMi-NLOS channels
  Channel power distribution with the total power normalized to 1.
Signature symbol
  64 FFT, 0.8 us GI, MCS0
  10 or 4 signature sequence bits, 2 or 8 reserved bits
  8 CRC bits, 6 tail bits
Impairments
  Carrier Frequency Offset : fixed 20 ppm
Rx processing:
  Actual timing
  CFO estimation and compensation in preamble portion

## Slide 6: TGac D NLOS (11)
10 bits in Signature sequence
Probability of false alarm is 10-3 without CRC check
Probability of false alarm is below 10-4 with 8-bit CRC check
CRC check may reduce false alarm rate of 11ax PPDU

## Slide 7: TGac D NLOS (11)
4 bits in Signature sequence
Probability of false alarm is 10-1 without CRC check
Probability of false alarm is below 10-3 with 8-bit CRC check
CRC check may reduce false alarm rate of 11ax PPDU

## Slide 8: TGac D NLOS (21)
10 bits in Signature sequence
This scheme shows no serious degradation or other noticeable aspects in multi-antenna transmissions
  Without CRC: Compared to 11, the 21 has approximately 0.7 dB gain @ 10-1
  With CRC : Compared to 11, the 21 has approximately 0.7 dB gain @ 10-1
  0.7 dB
  0.7 dB

## Slide 9: TGac D NLOS (21)
4 bits in Signature sequence
This scheme shows no serious degradation or other noticeable aspects in multi-antenna transmissions
  Without CRC: Compared to 11, the 21 has approximately 0.5 dB gain @ 10-1
  With CRC : Compared to 11, the 21 has approximately 0.7 dB gain @ 10-1
  0.5 dB
  0.7 dB

## Slide 10: UMi-NLOS (11)
10 bits in Signature sequence
Probability of false alarm is 10-3 without CRC check
Probability of false alarm is below 10-4 with 8-bit CRC check
CRC check may reduce false alarm rate of 11ax PPDU

## Slide 11: UMi-NLOS (11)
4 bits in Signature sequence
Probability of false alarm is 10-1 without CRC check
Probability of false alarm is below 10-3 with 8-bit CRC check
CRC check may reduce false alarm rate of 11ax PPDU

## Slide 12: UMi-NLOS (41)
10 bits in Signature sequence
This scheme shows no serious degradation or other noticeable aspects in multi-antenna transmissions
  Without CRC: Compared to 11, the 41 has approximately 1 dB gain @ 10-1
  With CRC : Compared to 11, the 41 has approximately 1 dB gain @ 10-1
  1 dB
  1 dB

## Slide 13: UMi-NLOS (41)
4 bits in Signature sequence
This scheme shows no serious degradation or other noticeable aspects in multi-antenna transmissions
  Without CRC: Compared to 11, the 41 has approximately 1 dB gain @ 10-1
  With CRC : Compared to 11, the 41 has approximately 1 dB gain @ 10-1
  1 dB
  1 dB

## Slide 14: Summary
Signature symbol is simple implementation technology to classify 11be and future standards
  Select the signature sequence to detect each format is TBD
The Signature sequence check seems to provide reasonable performance to meet the auto-detection probability

## Slide 15: Reference
[1] 11-19/1085r0 High-level EHT Preamble Structure
[2] 11-19/1021r1 Preamble Design Harmonization
[3] 11-15/0643r0 Autodetection with Signature Symbol

## Slide 16: APPENDIX

## Slide 17: 11be and Legacy Format Detection
11n-GF: HT-SIG1 QBPSK
11n-HT: LENGTH%3==0, HT-SIG1 and HT-SIG2 QBPSK
11ac VHT: LENGTH%3==0, VHT-SIGA1 BPSK, VHT-SIGA2 QBPSK
11ax SU/MU/TB: LENGTH%3!==0, RL-SIG, HE-SIGA1 and HE-SIGA2 BPSK
11ax ER SU: LENGTH%3!==0, RL-SIG, HE-SIGA1 BPSK, HE-SIGA2 QBPSK
11be EHT: Signature sequence check
L-STF
L-LTF
L-SIG
DATA
HT-STF
HT-SIG1
HT-SIG2
L-STF
L-LTF
L-SIG
HT-STF
HT-LTF
HT-SIG1
HT-SIG2
HT-LTFs, HT-DATA
VHT-LTFs, VHT-SIGB, VHT-DATA
VHT-SIGA1
L-STF
L-LTF
L-SIG
VHT-SIGA2
L-STF
L-LTF
L-SIG
RL-SIG
HE-SIGA1
HE-SIGA2
HE-SIGB, HE-STF, HE-LTF, HE-DATA
L-STF
L-LTF
L-SIG
RL-SIG
HE-SIGA1
HE-SIGA2
HE-SIGA, HE-SIGB, HE-STF, HE-LTF, HE-DATA
11a
11n-HT
11n-GT
11ac-
VHT
11ax-
SU/MU/TB
11ax-
ER SU
L-STF
L-LTF
L-SIG
RL-SIG
Signature
EHT-SIG, EHT-STF, EHT-LTF, EHT-DATA
11be-
EHT
QBPSK
BPSK
VHT-STF
HT-LTFs
HT-DATA
L-STF
L-LTF
L-SIG
Signature
EHT-SIG, EHT-STF, EHT-LTF, EHT-DATA
11be-
EHT