## Slide 1: Frame aggregation for NGV
Date: 2019-09-10
Authors:

## Slide 2: Background
Presented basic frame aggregation concept in May presentation 802.11-19/0375
Strawpoll showed strong support for frame aggregation in 802.11bd (17y/0n/9a)
Discussion on specific details about frame aggregation for OCB had no conclusion, but lots of folks had ideas and opinions.

## Slide 3: High level concept
Visualization of non-aggregated and aggregated frames

## Slide 4: The situation
802.11p-2010 introduced the OCB operating mode and used the 802.11a PHY.
  As such, there is no frame aggregation in 802.11p.
802.11bd is an amendment to 802.11md + more
  As such, the specification can inherit all the frame aggregation schemes from 802.11n, 802.11ac, 802.11ad, 802.11ax, etc.
  However, this task group should ensure they work with OCB and make any updates needed to clarify this.

## Slide 5: Evaluation
Keep in mind that OCB works with both broadcast unacknowledged applications as well as pairwise unicast acknowledged applications.
The two main types of aggregation are:
  A-MSDU
    See 802.11-2016 § 10.12 A-MSDU operation
  A-MPDU
    See 802.11-2016 § 10.13 A-MPDU operation
Both types of aggregation currently have limitations that will affect their use in 802.11bd.

## Slide 6: Various statements from 10.12 A-MSDU operation [1]
The Address 1 field of an MPDU carrying an A-MSDU shall be set to an individual address or to the GCR concealment address.
...
The following rules apply to the transmission of an A-MSDU:
  — A non-DMG STA that has a value of false for dot11HighthroughputOptionImplemented shall not transmit an A-MSDU.
  — A non-DMG STA shall not transmit an A-MSDU to a STA from which it has not received a frame containing an HT Capabilities element.
Summary:
A-MSDU doesn’t work for broadcast
Requires exchange of capabilities
A-MSDU requires block ACK

## Slide 7: Various statements from 10.13 A-MPDU operation
A STA indicates in the Maximum A-MPDU Length Exponent field in its HT Capabilities element
...
A STA shall not transmit an A-MPDU in an HT PPDU that is longer than the value indicated by the Maximum A-MPDU Length Exponent field in the HT Capabilities element received from the intended receiver.
...
A STA that is neither an AP nor a mesh STA shall not transmit an A-MPDU containing an MPDU with a group addressed RA.
Summary:
Should work for broadcast OCB with minimal updates.
Need to clarify block ack behavior for broadcast (i.e. unacknowledged)
The main capabilities exchanged are to do with maximum lengths.

## Slide 8: More about A-MPDU from 802.11ac
802.11ac introduced the concept of a “VHT single MPDU”.
Basically all VHT frames are transmitted with the A-MPDU frame structure even if they only carry one MPDU.
Should 802.11bd use this approach, requiring A-MPDU for all NGV transmissions?

## Slide 9: Specific Capabilities for NGV
A-MPDU Parameters field of the HT Capabilities element (802.11-2016 §9.4.2.56.3) [1]
VHT Capabilities Information field of the VHT Capabilities element (802.11-2016 §9.4.2.56.3)
NGV Capabilities
  This TG needs to choose reasonable values and define fixed value for the above parameters for NGV STAs

## Slide 10: Things for 11bd to do
Add/change text to enable A-MDPU for broadcast OCB modes (10.13).
Add/change text to enable A-MSDU for unicast OCB modes (10.12).
Update the maximum PPDU length in clause 10.14 with a statement containing appropriate value for 10MHz channels used by 802.11bd.
Broadcast OCB doesn’t allow for exchange of HT Capabilities of VHT Capabilities, so a specific fixed set of capabilities needs to be specified. Need to define these “NGV Capabilities” as a fixed set of capabilities so all NGV STAs know what can be transmitted/received by other NGV stations. (i.e. max number of MxDU in an A-MxDU, max length, etc.)
Another consideration is that TGbc “Enhanced Broadcast Services” may also be working on the issue of aggregation for group-addressed/broadcast frames (within a BSS). May need to coordinate aggregation for broadcast BSS (11bc) with broadcast OCB (11bd).

## Slide 11: Straw poll 1
Should 802.11bd amendment enable at least one of A-MSDU or A-MPDU operation to work for broadcast OCB?
Yes
No
Abstain

## Slide 12: Straw poll 2
Should 802.11bd amendment enable both A-MSDU and A-MPDU operation to work for unicast OCB?
Yes
No
Abstain

## Slide 13: References
IEEE Std 802.11-2016
802.11-19/0375