## Slide 1: Wakeup Radio in ITS band
Date: 2019-09-10
Authors:

## Slide 2: Background
802.11ba [2] has developed a low power wake-up radio
  Design is that the main (complex OFDM) radio sleeps and a companion low power radio monitors for a simpler on-off keying (OOK) wake-up signal.
  This enables the station to remain in a ‘listening’ mode with much lower power usage.
Applications that use 802.11 in OCB mode typically require ‘100% listening’ and thus traditional duty cycle type power saving mechanisms can’t be used.
Using the 802.11ba wakeup radio in an OCB mode is a potential way to save power in NGV devices.
Power saving enables 802.11bd to target battery powered stations for pedestrians, cyclists and other vulnerable road users.

## Slide 3: Use cases for OCB wake-up radio
V2X use cases were presented and agreed in 802.11ba. See document 802.11-17/0406r4 [1].
Slightly updated versions of these are presented in the following 4 slides.

## Slide 4: Use Case 1: Wake Up Infrastructure-to-Pedestrian (V2P) Radio
Scenario
  Pedestrian carrying portable device with V2P capability.
  To conserve power, the V2P mode (802.11bd radio) isn’t always operating.
  Roadside infrastructure such as an intersection sends WUR wake-up frame.
  Pedestrian device wakes up and operates 802.11-OCB based V2P
Wakeup operation
  ITS infrastructure sends WUR wake-up trigger frame
  Pedestrian device wakes up and operates 802.11bd radio
Requirements
  Low power and low latency

## Slide 5: Usage Model 1: Wake Up Infrastructure-to-Pedestrian (V2P) Radio
Environment
Vehicles, Road Infrastructure and Pedestrian/Cyclist carried device.
Applications
Trigger other devices to turn on (or off) automotive safety radio operation
Traffic Conditions
802.11-OCB traffic, 802.11 traffic depending on channels used
Use Case
Pedestrian/cyclist approaches dangerous intersection or moving vehicle
Infrastructure sends WUR wakeup frame
Pedestrian/cyclist carried device turns on automotive safety radio operation (802.11-OCB)
Challenges and requirements
Operation outside the context of a BSS
Addressing as broadcast/unicast
If used in 5.9GHz band, coexistence, channel choice

## Slide 6: Use Case 2: WUR Vehicle-to- Pedestrian (V2P)
Scenario
  Pedestrian carrying portable device.
  Oncoming vehicle sends WUR wake-up trigger frame containing ITS information.
Wakeup operation
  Vehicle sends WUR wake-up trigger frame
  Pedestrian device receives and decodes ITS related information in the WUR wake-up trigger frame
Requirements
  Low power and low latency
  WUR trigger frame contains small amount of information

## Slide 7: Usage Model 2: WUR Vehicle-to- Pedestrian (V2P)
Environment
Vehicles, Road Infrastructure and Pedestrian/Cyclist carried device.
Applications
Transmit Intelligent Transportation System (ITS) related information to very low power devices
Traffic Conditions
802.11-OCB traffic, 802.11 traffic depending on channels used
Use Case
Vehicle approaches pedestrian/cyclist
Vehicle transmits WUR wakeup frame
Pedestrian/cyclist receives ITS related information
Challenges and requirements
Operation outside the context of a BSS
Addressing as broadcast/unicast
If used in 5.9GHz band, coexistence, channel choice
Vendor Specific element an option in WUR Wakeup Trigger Frame

## Slide 8: Notes on Wake-up Radio
The Wake-up radio signal is not designed to carry data.
  It should be used to wake-up the station and any data should subsequently be delivered via the primary radio.
  This needs to be taken into account in designing OCB applications that use Wake-up radio.
  Open question whether some signalling information can be part of the wake-up trigger. (e.g. a small bitmap of information)

## Slide 9: Things for 802.11bd to do
The following two gaps have been identified in 802.11ba D3.1
  Specifying WUR in OCB mode (current draft is for use within a BSS only)
  Specifying WUR in 5.9GHz band (current draft is for 2.4GHz and 5GHz only)
802.11ba is trying to get to sponsor ballot and finish their draft
  Highly unlikely that 802.11ba will address OCB and 5.9Ghz.
There is an opportunity for 802.11bd to build upon the work in 802.11ba and add those two missing pieces.
Power saving will increase the uses of 802.11bd

## Slide 10: Straw poll 1
Should 802.11bd consider mechanisms for power saving in NGV?
Yes
No
Abstain

## Slide 11: Straw poll 2
Should 802.11bd amendment enable WUR for OCB in 5.9GHz?
Yes
No
Abstain

## Slide 12: References
1) 802.11-17/0406r4
2) IEEE 802.11ba D3.1

## Slide 13: Appendix A
Example WUR frame using Vendor-Specific Type, OUI/CID would indicate OCB

## Slide 14: Appendix B
Same as previous, but with security enabled

## Slide 15: Appendix C
Example variable-length (VL) WUR frame using next reserved “Type”.
Assign next available reserved Type value for OCB WUR (eg. 5)

## Slide 16: Appendix D
Example fixed-length (FL) WUR frame by assigning one of the reserved “Type” values for OCB WUR.
27 bits available to be defined
Assign next available reserved Type value for OCB WUR (eg. 5)