## Slide 1: Frame type
Date: 2019-09-08
Authors:

## Slide 2: Abstract
This presentation describes a comparison between Data frame and Public Action frame for eBCS.

## Slide 3: Introduction
eBCS contents can be delivered in
  Data frames
  Public Action frames
Which is better?

## Slide 4: Comparison in REVmd 2.0
Existing rate selection procedures for both Data frame and Public Action frame is described in 10.6.5.
Existing maximum sizes of Data frame and Public Action frame are described in Table 9-25.
No significant differences between Data frame and Public Action frame.

## Slide 5: Implementation Difficulty
In Linux:
  Management frames can be transferred from kernel to user land even in State 1.
    Of course, implementing in kernel is not so difficult.
  Processing Data frames in State 1 is more difficult to implement.
Hardware (WLAN chipset)
  Some chipsets transfer Management frames to kernel (device driver) in monitor mode even in State1. They do NOT transfer Data frames in State 1.

## Slide 6: Additional Functional Requirement
3.x Transmission function
TGbc R3.x.x: 802.11bc amendment shall use Public Action frame to deliver both data and management information.