## Slide 1: Forward Compatibility for WiFi Preamble Design
Date: 2019-09-15
Authors:
Name | Affiliations | Address | Phone | Email
Sameer Vermani | Qualcomm |  |  | 
Alice Chen |  |  |  | 
Bin Tian |  |  |  | 
Youhan Kim |  |  |  | 
Notes: September 2012

## Slide 2: Abstract
Traditionally, WiFi preamble design has only focused on backward compatibility
These slides are a continuation of the ideas proposed in [1], and propose to bring forward compatibility to WiFi preambles (in the main-stream WiFi bands) starting with 802.11be
  Desire to solve the auto-detection issue for all future standards starting with EHT, once and for all
  Better coexistence than just L-SIG based deferral among future generations of 802.11 through universal fields

## Slide 3: Introduction
Historically, 802.11 preambles of every PHY version contain following types of information
  Information needed by intended receivers
    E.g., Nss, MCS, Coding etc.
  Basic Co-existence info for by-standers of previous PHY versions
    L-SIG duration
  Richer Co-ex info (medium re-use or power save) for by-standers of current PHY version
    E.g., BSS Color, UL/DL bit and TxOP fields in 802.11ax
Hitherto, information of type 3 is not understood by previous generations
  E.g., 11ac devices do not understand BSS Color and TxOP in SIG fields of 802.11ax packets
  Only basic L-SIG duration based co-existence is achieved
Better future compatibility starting with 802.11be
  Richer co-existence among future WiFi versions starting with 11be
    E.g. 11be devices will respond in a more sophisticated way (compared to just L-SIG based deferral) to the PHY version(s) after that

## Slide 4: Forward compatibility: Universal Fields (1)
Fix the preamble ‘structure’ across multiple 802.11 generations for at-least a few symbols after legacy preamble
  Starting with EHT
  ‘Structure’ here means the number of OFDM symbols and encoding method
  Legacy preamble and a ‘Pre-SIG’
Have some universal fields in the ‘structurally-common’ preamble section for all standards, EHT and beyond
  Version independent fields whose presence is independent of the standard version (11be/bf/bg…)
    All devices compliant with EHT or beyond standards can count on this information being present
    At a known location in Pre-SIG
  For example BSS Color, TxOP etc
Legacy preamble
(may include RL-SIG)
Common structure for EHT and beyond
802.11be preamble
Pre-SIG
Pre-SIG contains
universal fields
at certain fixed locations

## Slide 5: Forward compatibility: Universal Fields (2)
We think of universal fields as fields satisfying the following properties
  Presence and location is independent of PHY version
    Same for 11be/11bf/11bg etc…
  Mainly used for better co-existence among 802.11 generations starting from 11be
    Should be useful for by-stander devices of multiple generations
Based on above, good candidates for universal fields are
  PHY Format Identifier (Same as PHY Version Identifier proposed in [1])
    Value of the format identifier field differentiates between different WiFi versions starting with EHT
    Auto-detection problem of multiple WiFi generations gets solved together
  TxOP duration
  BSS Color
  UL/DL flag
PPDU type (MU/SU/Trigger-based/ER/) may not be a good candidate for universal fields because
  Every PHY version might have a different set of PPDU types
  This information is mainly useful for intended receivers and not by-standers

## Slide 6: Thoughts on the Pre-SIG field -I
Ideally, the universal information should be localized to just the pre-SIG
  Don’t want universal fields to be scattered in multiple parts of the preamble
One symbol does not seem to be enough
  If we have BSS Color (>=6 bits), TxOP (>=7 bits), UL/DL flag and PHY Format Identifier (>=3), adds up to a minimum of 17 bits
  With CRC (>=4 bits) and 6 bits tail, already exceeds the bit carrying capacity of 1 symbol
Three symbols (encoded together) might become a performance bottle neck (in outdoor channels)
Two symbols seems to achieve a reasonable balance
L-STF
L-LTF
L-SIG
EHT SIG fields
RL SIG
Pre- SIG
Common structure for EHT and beyond

## Slide 7: Thoughts on the Pre-SIG field -II
Pre-SIG will be sent on 26 data tones (just like HE-SIG-A)
  Extra tones will be added to L-SIG and RL-SIG for channel estimation
  Leaving aside tail and CRC, 2 symbols offer a bit carrying capacity of <=42 bits
42 bits seems like an overkill for universal fields alone
  Need to manage preamble overhead; can’t be profligate with bits in preamble
    Try to keep extra overhead of 11be to one symbol
  Can incorporate version dependent fields (e.g. MCS, Nss etc) in the pre-SIG
Propose a mix of universal and version-dependent fields in a 2 symbol pre-SIG
  ER mode (need for which is TBD) may need a longer pre-SIG
L-STF
L-LTF
L-SIG
EHT SIG fields
RL SIG
Pre- SIG
2 symbols jointly encoded.
Contains universal and
version dependent fields
Common structure for EHT and beyond

## Slide 8: Summary
We proposed to bring future compatibility to WiFi preambles starting with 802.11be
  Solve the auto-detection issue for multiple standards starting with EHT, together
  Better coexistence than just L-SIG based deferral among future generations of 802.11
Have a structurally common portion of the preamble for multiple WiFi generations starting with 802.11be
  Legacy preamble followed by a Pre-SIG
  The Pre-SIG contains universal fields which are version independent
Proposed a 2 symbol Pre-SIG with a mix of universal (version independent) and version dependent fields

## Slide 9: Straw-poll 1
Do you agree with introducing “universal fields” in the EHT preamble ?
  The intent of the universal fields is to allow for certain “version independent” content for better co-existence among future 802.11 generations
  The exact field definition, location and number of bits are TBD

## Slide 10: Straw-poll 2
Do you agree to incorporate a PHY format identifier field as one of the universal fields in the EHT preamble?
  The intent is to simplify auto-detection for future 802.11 generations
  Size of this field is TBD

## Slide 11: Straw-poll 3
Do you agree to have a 2 OFDM symbol long, jointly encoded SIG field in the EHT preamble immediately after RL-SIG ?
  This SIG field will have universal fields
  Extended Range Mode is TBD
  The name for this field can be chosen in future based on consensus in the group

## Slide 12: Straw-poll 4
Do you agree that the SIG field immediately after the RL-SIG will be sent using 52 data tones and 4 pilot tones per-20MHz?

## Slide 13: Straw-poll 5
Do you agree that the SIG field immediately after the RL-SIG can have some version dependent fields as well?

## Slide 14: Motion 1
Move to add the following to the spec-framework document
  There shall be a 2 OFDM symbol long, jointly encoded Universal-SIG(U-SIG) field in the EHT preamble immediately after the RL-SIG
    The U-SIG will contain version independent fields. The intent of the version independent content is to achieve better co-existence among future 802.11 generations.
    In addition, the U-SIG can have some version dependent fields
    The size of the U-SIG for the case of an Extended Range Mode (if such a mode were to be adopted) is TBD
    The U-SIG will be sent using 52 data tones and 4 pilot tones per-20MHz

## Slide 15: References
[1] Sameer Vermani et al, “Preamble Design Harmonization” , IEEE Document 11/19-1021r1