## Slide 1: Power Consideration for Multi-link Transmissions
Date: 2019-09-11
Authors:
Name | Company | Address | Phone | Email
Rojan Chitrakar | Panasonic Corporation |  |  | rojan.chitrakar@sg.panasonic.com
Lei Huang |  |  |  | 
Yanyi Ding |  |  |  | 
Yoshio Urabe |  |  |  | 

## Slide 2
Overview
Operating multiple radios to enable multi-link transmissions may substantially increase the power consumption of multi-link capable devices which may be a concern for battery powered non-AP Multi-link devices.
We look into the issue of idle listening and suggest a possible solution to reduce power consumption.

## Slide 3
Power Consumption Assumptions
The 802.11ax Simulation Scenarios [4] specifies the following power state parameters:
Power State parameters |  |  | 
Average Current Consumption [mA] Voltage = 1,1V, Band = { 2.4 GHz, 5 GHz }, NSS = { 1 }, Number of TX/RX antennas = { 1 }, TX power per antenna = { 15 dBm } |  |  | 
Power State | Bandwidth = { 20 MHz } | Bandwidth = { 40 MHz } | Bandwidth = { 80 MHz }
Transmit | 280 mA | 280 mA | 280 mA
Receive | 100 mA | 140 mA | 200 mA
Listen | 50 mA | 60 mA | 75 mA
Shallow Sleep | 0.9 mA | 0.9 mA | 0.9 mA
Deep Sleep | 0.09mA | 0.09mA | 0.09mA
Power consumption in all active states can be expected to increase multiple folds for Multi-link devices.
  Idle listening on multiple links may constitute significant ratio of a non-STA Multi-link device’s power footprint.
Active states

## Slide 4
Discussions
In light traffic load conditions, STAs affiliated with a non-AP Multi-link device (MLD) can be expected to be in the idle listen mode for most of the time.
Even though a non-AP MLD is capable of multi-link transmissions/receptions, the actual duration of its multi-link communication may be low.
Only listening on a single link when not engaged in multi-link communication may result in significant power savings for non-AP MLDs.

## Slide 5
A potential solution: Configuration
For a non-AP Multi-link device (MLD), one supported link is assigned (by the AP MLD) as the primary link*.
  The primary link may be assigned during Association or post-association.
  The primary link is used as the default link for synchronization (e.g. to receive Beacon frames) as well as non-data frames TX/RX.
  The primary link may be re-assigned by the AP MLD at any time.
  The non-AP MLD only listens on the primary link during idle periods.
The other links may be designated as secondary links*.
  The secondary links are used for high throughput TX/RX (e.g. by link aggregation or link transfer) .
  The secondary links are disabled or in PS doze state during idle periods.
*Note1: An AP MLD may have multiple primary links as a deployment choice. Different non-AP MLDs may be assigned to different primary links for load-sharing etc.
*Note2: Actual names may be changed.

## Slide 6
A potential solution: TX/RX
The AP MLD uses the primary link to indicate an upcoming multi-link transmission (DL/UL).
  AP MLD may also indicate the involved secondary links and the transmission time.
The non-AP MLD activates the indicated secondary link/s.
AP MLD schedules the multi-link transmission at the indicated time.
The non-AP MLD de-activates the secondary link/s after completion of the multi-link transmission or after a certain timeout duration.
Multi-link Announcement frame
OFF/Doze
Legend:
ACK/BA frame
Beacon frame
DL
UL
ON
6 GHz
(160 MHz)
5 GHz
(80 MHz)
2.4 GHz
(40 MHz)
Primary Link
Secondary Link - 1
Secondary Link - 2
t
f

## Slide 7
TBTT
Beacon Interval
Simple Numerical Comparison
Idle listening in three links vs single link:
Assumptions:
  Each link operating on a 20 MHz channel
  10% RX and 10% TX opportunity in one Beacon Interval (BI).
  Beacon TX in all 3 links.
1) Three links:
Power State | Bandwidth = 20 MHz
Transmit (TX) | 280 mA
Receive (RX) | 100 mA
Listen (L) | 50 mA
Shallow Sleep (SS) | 0.9 mA
Deep Sleep (DS) | 0.09mA
TBTT
Beacon Interval
2) Single link:
STA listens on all 3 links
STA only listens on link-1. Other links in SS.
35.5% savings in this simple example.
Beacon RX
Multi-link RX
Multi-link TX

## Slide 8
Conclusion
In this contribution, we discussed the power consumption issue of non-AP Multi-link devices.
  We highlighted that idle listening may constitute significant ratio of a non-AP Multi-link device’s power footprint.
  Only listening on a single link when not engaged in multi-link communication may result in significant power savings.
We also shared a potential solution whereby a non-AP MLD is assigned a primary link.
  The non-AP MLD only listens on the primary link during idle periods.

## Slide 9: References
IEEE 802.11-17/1184r1 – Follow up discussions on Throughput Enhancement
IEEE 802.11-19/823r0 – Multi-link aggregation
IEEE 802.11-19/0821r1 – Multi-link Operation Discussion
IEEE 802.11-14/980r16 – TGax Simulation Scenarios

## Slide 10
Straw Poll 1
Do you support that a non-AP Multi-link device (MLD) that has more than one enabled links may only listen to a single link during idle periods?
  Y/N/A