## Slide 1: Channel Access Design for Synchronized Multi-Links
Date: 2019-09-07
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Guogang Huang |  |  |  | 
Yuchen Guo |  |  |  | 
Yifan Zhou |  |  |  | 
Yiqing Li |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
There are two types of multi-links (ML) base on the capability of simultaneous TX/RX on different links
  Synchronized ML
  Asynchronized ML
Q-async or similar concept is mentioned in other presentations. The concept is more complex, for simplicity we didn’t discuss it here;
The channel access in asynchronized MLs could be independent, it is simple to design;
The transmissions in multiple links are need to be synchronized in synchronized MLs, and many issues need to be considered for channel access;
All the following slides are discussed for synchronized ML.

## Slide 3: TXOP setup
A ML device transmits TXOP initial frames (e.g. RTS) on the links that are idle at the time when backoff is finished;
  It doesn’t touch the channel access details. E.g. single primary channel or multiple primary channels; and how to backoff.
TXOP could only be set up on the links that successfully get response frames (e.g. CTS) when the responses are needed;
  In below example, RTS send on 3 links, but TXOP only set up successfully on link1 and 4.
RTS
CTS
Data
BA
Data
…
RTS
Busy
…
RTS
CTS
Data
BA
Data
…
Link 1
Link 2
Link 3
Link 4
TXOP
Backoff finished

## Slide 4: TXOP setup
Different TXOP initial frames may be sent on different links;
  The end times of initial data should be aligned if responses are needed.
RTS
CTS
Data
BA
Data
…
RTS
…
Data (ACK)
BA
Data
BA
Data
…
Link 1
Link 2
Link 3
Link 4
TXOP
Backoff finished
CTS to Self
Data (ACK)
…
Data (No ACK)
Link 5
Link 6
Link 7
Data
BA
Data
…
Data
BA
Data
…
…
OR

## Slide 5: Primary 20MHz sub-channel and BW on each link
No matter single primary channel, or multiple primary channels for ML, each link may has a primary 20MHz sub-channel;
  It will be convenient to support dynamic bandwidth negotiation, otherwise receiver side will needs multiple decoder in each link
TXOP bandwidth on each link is base on bandwidth negotiation on its own link;
RTS
CTS
Data
BA
Data
…
RTS
CTS
Data
BA
Data
…
Link 1
Link 2
TXOP
RTS
RTS
RTS
CTS
RTS
P 20MHz
P 20MHz

## Slide 6: Problem Statement
Example:
  Non-AP ML device (MLD)1 only obtains link 1 after backoff finished, and transmits PPDU 1 to AP MLD; Later, non-AP MLD 2 sends PPDU2 on link 2 to the same AP MLD during the transmission period of PPDU1;
  AP MLD can not replies BA for PPDU 1 in link 1 in this case
A simple solution is single primary channel for synchronized ML, which we more preferred;
For multiple primary channels in synchronized ML, several solutions are shared for discussion in following slides.
PPDU 1
BA
Link 1
PPDU 2
Link 2
Non-AP MLD 1
Non-AP MLD 2
AP MLD
?
Busy

## Slide 7: Intra BSS solution 1
When non-AP MLD2 receives PPDU 1 on link 1 and identifies it as an intra-BSS PPDU, the non-AP MLE2 defers EDCA contention on link 2 after the TXOP set by PPDU 1;
PPDU 1
BA
Link 1
PPDU 2
Link 2
Non-AP MLD 1
Non-AP MLD 2
AP MLD
AIFS
TXOP

## Slide 8: Intra BSS solution 2
When non-AP MLD2 receives PPDU11 and identifies it as an intra-BSS PPDU, the non-AP MLD2 immediately start EDCA contention on link 2. When transmits PPDU21 on link2, its end time should be aligned with the end time of PPDU11;
Non-AP MLD2 doesn’t know the end time of PPDU12, so it needs to first decode the preamble of PPDU12 to get the PPDU length, and then aligns the end times of PPDU22 and PPDU12.
PPDU 11
BA
Link 1
PPDU 21
Link 2
Non-AP MLD 1
Non-AP MLD 2
AP MLD
AIFS
TXOP
PPDU 12
BA
BA
PPDU 22
BA

## Slide 9: Inter BSS solution
When non-AP MLD2 receives PPDU 1 and identifies it as an inter-BSS PPDU, the non-AP MLD2 starts EDCA contention immediately;
The time that identifies PPDU1 as an inter-BSS PPDU could be
  The end time of PHY preamble of PPDU1, or
  The end time of first MPDU in PPDU1, or;
  others.
PPDU 1
BA
Link 1
PPDU 2
Link 2
Non-AP MLD 1
Non-AP MLD 2
AP MLD
AIFS
Pre-amble

## Slide 10: Summary
Some rules for TXOP setup in synchronized ML are discussed;
One problem of multi-link transmission is showed, and several potential solutions are prepared for discussion.

## Slide 11: Straw Poll 1
Do you agree that the medium access mechanism in each link may be different from the existing medium access mechanism, the mechanism is TBD. And there is a primary 20MHz sub-channel in each of the multiple links to support dynamic bandwidth negotiation in that link?
  Yes
  No
  Abstain