## Slide 1: VHT LO Leakage Requirement
Date: 2019-09-11
Authors:
Name | Affiliations | Address | Phone | Email
Matthew Fischer | Broadcom | 250 Innovation Dr, San Jose, CA 95134 |  | Matthew.fischer@broadcom.com
Jun Zheng |  |  |  | 
Jason Tseng |  |  |  | 
Ron Porat |  |  |  | 
Vinko Erceg |  |  |  | 

## Slide 2: Abstract
VHT LO Leakage limits are unrealistic when accounting for reduced TX power situations
Other proposed amendments account for reduced total TX power in a manner that is realistic
This document proposes a relaxation of the VHT LO Leakage limits under certain conditions

## Slide 3: VHT LO Leakage Specification
REVmd_D2.4 -- 21.3.17.4.2 Transmit center frequency leakage

## Slide 4: VHT dBr Calculation
VHT dBr
  When RF LO is at the center of the PPDU BW
Constant dBr requirement across all TX power
  When RF LO is at the center of the PPDU BW
BW | 20 | 40 | 80 | 160
NST | 56 | 114 | 242 | 484
-10log10(NST) | -17.48 | -20.57 | -23.84 | -26.85

## Slide 5: TGax Draft 2.4 LO Leakage Specification
27.3.18.4.2 Transmit center frequency leakage

## Slide 6: TGax Effective dBr Requirement
Leakage power = max(P – 32, -20)
dBr = max(P – 32, -20) - P
  P > 12, dBr = P – 32 – P = -32
  P < 12, dBr = -20 - P

## Slide 7: Comparison of Current dBr Requirements

## Slide 8: Proposed Changes
REVmd_D2.4 -- 21.3.17.4.2 Transmit center frequency leakage
TX LO leakage shall meet the following requirements for all formats and bandwidths except 80+80 MHz where the RF LO falls outside both frequency segments:
— When the RF LO is in the center of the transmitted PPDU BW, the power measured at the center of transmission BW using resolution BW 312.5 kHz shall not exceed the maximum of the average power per-subcarrier of the transmitted PPDU and -20 dBm, or equivalently, max(P-10log10(NST), -20 ), where P is the transmit power per antenna in dBm, and NST is defined in Table 21-5 (Timing-related constants).
— When the RF LO is not at the center of the transmitted PPDU BW, the power measured at the location of the RF LO using resolution BW 312.5 kHz shall not exceed the maximum of -32 dB relative to the total transmit power and –20 dBm, or equivalently max(P – 32, -20) , where P is the transmit power per antenna in dBm, and NST is defined in Table 21-5 (Timing-related constants).
For an 80+80 MHz transmission where the RF LO falls outside both frequency segments, the RF LO shall follow the spectral mask requirements as defined in 21.3.17.1 (Transmit spectrum mask).
The transmit center frequency leakage is specified per antenna.

## Slide 9: Similar Issue for HT Specification
PROPOSED CHANGE:
19.3.18.7.2 Transmit center frequency leakage
For VHT STAs the requirements on transmitter center frequency leakage are defined in 21.3.17.4.2 (Transmit center frequency leakage); otherwise, the requirements are defined in this subclause.
The transmitter center frequency leakage shall follow 17.3.9.7.2 (Transmitter center frequency leakage) for all transmissions in a 20 MHz channel width. For transmissions in a 40 MHz channel width, the center frequency leakage shall not exceed max(P - 20, -20) dBm–20 dB relative to overall transmitted power, or, equivalently, 0 dB relative to the average energy of the rest of the subcarriers. For upper or lower 20 MHz transmissions in a 40 MHz channel, the center frequency leakage (center of a 40 MHz channel) shall not exceed max(P – 17, -20)–17 dB relative to overall transmitted power, or, equivalently, 0 dB relative to the average energy of the rest of the subcarriers. The transmit center frequency leakage is specified per antenna.

## Slide 10: 11a Subclause
17.3.9.7.2 Transmitter center frequency leakage
Certain transmitter implementations might cause(#229) leakage of the center frequency component. Such leakage (which manifests itself in a receiver as energy in the center frequency component) shall not exceed max(P – 15,-20) dBm-15 dB relative to overall transmitted power or, equivalently, +2 dB relative to the average energy of the rest of the subcarriers. The data for this test shall be derived from the channel estimation phase.

## Slide 11: Comparison of dBr Requirements After the Proposed Changes

## Slide 12: Straw poll #1
Do you support the proposed change to Draft P802.11REVmd_D2.4
  21.3.17.4.2 Transmit center frequency leakage
  19.3.18.7.2 Transmit center frequency leakage
  17.3.9.7.2 Transmitter center frequency leakage
  as described in 11-19-1561-01-000m-VHT-LO-Leakage-Requirement?
  YES
  NO
  ABS

## Slide 13: References
[1] Draft P802.11REVmd_D2.4
[2] Draft P802.11ax_D4.3