## Slide 1: Simulation results with bit-loading for the LC-optimized PHY
Date: 2019-09-16
Authors:

## Slide 2: Abstract
This contribution contains simulation results in support of the bit-loading feature supported by the LC-optimized PHY.

## Slide 3: Overview
Adaptive bit-loading is a new feature in the LC-optimized PHY.
In this contribution, “flat” bit-loading using fixed MCS over all subcarriers is compared to adaptive bit-loading (according to [1])
Target: PER < 10-3
Approach:
  Same data rate in both, fixed and adaptive modes of operation
  What is the required SNR for fixed bit-loading?
  What is the required SNR for adaptive bit-loading?
[1] Fischer, R. F., & Huber, J. B. (1996, November). A new loading algorithm for discrete multitone transmission. In Proceedings of GLOBECOM'96. 1996 IEEE Global Telecommunications Conference (Vol. 1, pp. 724-728). IEEE.

## Slide 4: LC-optimized PHY configuration
Base configuration:
G.9991 PHY, sub-carrier spacing 195.3125 kHz, sample rate 1 GHz, OFDM symbol duration 5120 ns, CP length 320 ns, DC gap 4.59 MHz
Bandwidth settings:
  942 active subcarriers (183.98 MHz used bandwidth)
  410 active subcarriers (80.32 MHz used bandwidth)
  205 active subcarriers (40.39 MHz used bandwidth)
Mean number of bits/active subcarrier: 4 and 6 for both, fixed and adaptive mode
FEC: LDPC, rate: 5/6, block length: 4320 (960) bits

## Slide 5: Simulation setup
Frontend models (band-pass filter): See doc. 11-19/187r4
Additional narrow-band LED model for some simulations
Signal power is measured at the red circle. SNR is set by adjusting noise power in the following AWGN block accordingly. The impact of the Rx model on SNR is assumed to be neglibible, as the used bandpass cutoff frequency exceeds the signal bandwidth.
+ LED model
(low pass filter)

## Slide 6: Channel Models – Time Domain
Enterprise Conference Room S3-D1
  Pronounced LOS peak
  Some diffuse multi-path components
Industrial Wireless D7 (overall)
  No pronounced peak
  Energy spread over 3 main components

## Slide 7: Channel Models – Frequency Domain
Enterprise Conference Room S3-D1
  Low pass <45 MHz
  Flat with some ripple >45 MHz
Industrial Wireless D7 (overall)
  Low pass <30 MHz
  Deep fades >30 MHz

## Slide 8: Additional LED model
Measurement (solid) and approximation (dashed) as presented in doc. 19-1208r0
Approximation from left figure (dashed red) and digital filter fit (solid blue)
Second order IIR filter
Matlab code (SOS form):
g_led = 0.003078294298992;
sos_led = [1,2,1,1,-1.83703636178762,0.849349538983590];

## Slide 9: Enterprise Conference room channel, 184 MHz, 4 bits/SC
Simulation length: 10,000 FEC blocks
Bit error rate
Block error rate

## Slide 10: Industrial Wireless channel, 184 MHz, 4 bits/SC
Simulation length: 10,000 FEC blocks
Bit error rate
Block error rate

## Slide 11: Enterprise Conference room channel, 184 MHz, 4 bits/SC, FEC block length 960 bits
Simulation length: 10,000 FEC blocks
Bit error rate
Block error rate

## Slide 12: Industrial Wireless channel, 184 MHz, 4 bits/SC, FEC block length 960 bits
Simulation length: 10,000 FEC blocks
Bit error rate
Block error rate

## Slide 13: Enterprise Conference room channel, 184 MHz, 6 bits/SC
Simulation length: 10,000 FEC blocks
Bit error rate
Block error rate

## Slide 14: Industrial Wireless channel, 184 MHz, 6 bits/SC
Simulation length: 10,000 FEC blocks
Bit error rate
Block error rate

## Slide 15: Enterprise Conference room channel, 80 MHz, 4 bits/SC
Simulation length: 5,000 FEC blocks
Bit error rate
Block error rate

## Slide 16: Enterprise Conference room channel, 80 MHz, 4 bits/SC + LED model
Simulation length: 5,000 FEC blocks
Bit error rate
Block error rate

## Slide 17: Enterprise Conference room channel, 40 MHz, 4 bits/SC
Simulation length: 2,000 FEC blocks
Bit error rate
Block error rate

## Slide 18: Enterprise Conference room channel, 40 MHz, 4 bits/SC + LED model
Simulation length: 2,000 FEC blocks
Bit error rate
Block error rate

## Slide 19: Summary
We have studied the benefits of adaptive bit-loading in the LC-optimized PHY by means of simulations according to the evaluation framework in TGbb.
In the conference room scenario, there is minor gain.
But in the industrial scenario, there is significant gain (around 3 and 5 dB with long and short block size) for adaptive compared to fixed bitloading.
When using an additional LED model, which is realistic for energy-efficient operation of non-AP STAs, adaptive bitloading leads to error-free operation.
The use of adaptive bitloading enables efficient operation of LC over critical channels, like in industrial scenario or when using low-energy LED frontends.