## Slide 1: Preamble Design Consideration for 11be follow-up
Date: 2019-11-08
Authors:

## Slide 2: Introduction
In [1], a concept of using common header with an auto-detection scheme for future amendments of 802.11, starting from 11be, was proposed
In [2], [3], a common header field immediately following the RL-SIG, were proposed
During the presentation of [2], questions were raised on how 11ax receiver will behave receiving such common header field.
In this contribution, we try to answer the question and provide an example by examining the specified procedures for an 11ax receiver.

## Slide 3: Current 11ax receive procedures (1/2)
In 11ax D5.0 27.3.21
Under 11 ax formats corresponding to L_LENGTH%3==1
  “The PHY entity shall check CRC of the HE-SIG-A field. If the CRC check is valid, the PHY entity shall report TXOP, BSS Color and check Format field, and continue to receive HE-STF. The PHY entity shall report to the MAC entity the predicted duration of the TXOP in the HE-SIG-A field”
  If the HE-SIG-A field(#Ed) indicates a reserved HE-SIG-A indication, the PHY shall issue the error condition PHY-RXEND.indication(FormatViolation) primitive and maintain PHY-CCA.indication(BUSY, channellist) primitive for the predicted duration of the transmitted PPDU derived from the LENGTH field in L-SIG as defined in Equation (27-134)
Under 11 ax formats corresponding to L_LENGTH%3==2 and HE-SIG-A2 is QBPSK
  The PHY entity shall check CRC of the HE-SIG-A field. If the CRC check is valid, the PHY entity shall report TXOP, BSS Color, and continue to receive HE-STF. The PHY entity shall report to the MAC entity the predicted duration of the TXOP in HE-SIG-A.
  If the HE-SIG-A field indicates a reserved HE-SIG-A indication, the PHY shall issue the error condition PHY-RXEND.indication(FormatViolation) primitive and maintain PHY-CCA.indication(BUSY, channellist) primitive for the predicted duration of the transmitted PPDU derived from the LENGTH field in L-SIG as defined in Equation (27-134) unless it receives a PHY-CCARESET.request primitive before the end of the PPDU for instance during spatial reuse operation as described in 26.10 (Spatial reuse operation).

## Slide 4: Current 11ax receive procedures (2/2)
Under 11 ax formats corresponding to L_LENGTH%3==2 and HE-SIG-A2 is BPSK
  The PHY entity shall check CRC of the HE-SIG-A field(#Ed). If the CRC check is valid, the PHY entity shall report TXOP, BSS Color, and continue to receive HE-SIG-B. The PHY entity shall report to the MAC entity the predicted duration of the TXOP in the HE-SIG-A field
  If the HE-SIG-A field indicates a reserved HE-SIG-A indication, the PHY shall issue the error condition PHY-RXEND.indication(FormatViolation) primitive and maintain PHY-CCA.indication(BUSY, channellist) primitive for the predicted duration of the transmitted PPDU derived from the LENGTH field in L-SIG as defined in Equation (27-134) unless it receives a PHY-CCARESET.request primitive before the end of the PPDU for instance during spatial reuse operation as described in 26.10 (Spatial reuse operation).
Observations:
  11ax PHY reports TXOP_DURATION, BSS_COLOR to the MAC layer when HE-SIG-A CRC is valid, independent of a reserved/non-reserved HE-SIG-A indication.
  The PHY-RXEND.indication(FormatViolation) primitive stops 11ax receiver decoding the rest of the PPDU
  After 11ax receiver detects an ER-SU or MU PPDU format PPDU with a reserved HE-SIG-A indication, the MAC layer is allowed to base on the reported BSS_COLOR to issue a CCARESET.request and perform SR operation.

## Slide 5: HE-SIG-A extension by using reserved bits
11ax has already built in a future-proofing mechanism to allow non-reserved values in the reserved fields in HE-SIG-A
  An 11ax STA follows the Trigger frame instructions to set the reserved field in HE-SIG-A of TB-PPDU
    The HE_SIG_A2_RESERVED parameter is set to the value of the UL HE-SIG-A2 Reserved subfield in the Common Info field of the Trigger frame (26.5.2.3.3)
Observations:
  An AP supporting a future PHY version may instruct 11ax STAs to set certain values to the reserved field in the HE-SIG-A of TB-PPDU
  Such setting should not cause any issue to the operations (e.g. NAV setting, intra-PPDU power save, spatial reuse) of an existing 11ax STA, which is not the intended receiver of the PPDU.
    This is consistent with the requirements cited in the previous 2 slides, i.e. PHY-RXEND.indication(FormatViolation) primitive is issued, and useful info (BSS Color, TXOP) passed up to MAC

## Slide 6: Example (1/2)
11ax+ PPDU can be received by 11ax receiver as an UL MU PPDU (L_LENGTH%3==2, EHT-SIG-A2 BPSK), with an HE-SIG-A reserved indication. To do this, the 11be transmitter sets HE-SIG-A field:
  EHT-SIG-A1 B0=UL
    11ax+ receiver may ignore this field
  EHT-SIG-A1 B5-B10=BSS color of the 11be PPDU
    11be BSS_COLOR may have more than 6 bits but may share common 6 bits with 11ax
  EHT-SIG-A1 B11-B14=spatial reuse restrictions of the 11be PPDU
  EHT-SIG-A2 B0-B6=TXOP_DURATION of the 11be PPDU
  One or more reserved bits/values in the HE-SIG-A can be used to signal to 11ax+ receiver that the PPDU is a 11ax+ PPDU
The remaining bits can be used for 11be signaling, such as a PHY version identifier
The 11ax+ STA would not mistaken this PPDU as a 11ax UL MU PPDU
  The reserved bit/values (possibly together with the UL flag), indicating this is an EHT(common) header for 11ax+ PPDU.

## Slide 7: Example (2/2)
When 11ax receiver receives this PPDU
  PHY reports BSS_COLOR, TXOP_DURATION to the MAC layer, (27.3.21)
    Because the STA does not receive a frame with a Duration field in the PPDU, so NAV is set based on TXOP_DURATION (26.2.4)
    If the BSS_COLOR is the same as the STA’s BSS color, intra-BSS NAV may be set (26.2.2, 26.2.4)
    If the BSS_COLOR is not the same as the STA’s BSS color, basic NAV may be set (26.2.2, 26.2.4)
  PHY issues PHY-RXEND.indication(FormatViolation) primitive and maintain PHY-CCA.indication(BUSY, channellist) primitive for the predicted duration of the transmitted PPDU derived from the LENGTH field in L-SIG (27.3.21). PHY stops decoding the rest of the PPDU.
  An OBSS 11ax STA may perform CCA reset and perform SR operation based on the BSS_COLOR, SPATIAL_REUSE RXVECTOR parameters (27.3.21, 26.10)
  An intra-BSS non-AP 11ax STA may perform intra-PPDU power save (26.14.1) by observing the UL flag, BSS_COLOR parameters

## Slide 8: Comparison
 | LENGTH%3!=0 with ax compatible design | L_LENGTH%3=0
Power Save | 11ax STA may go to intra-PPDU power save during EHT-PPDU by observing BSS Color UL/DL | Pre-11be STAs decode the entire EHT-PPDU as an 11a PPDU
Early detection | 11be+ STAs detect the PHY version 2 symbols after RL-SIG | 11be+ STAs detect the PHY version 1 or 2 symbols after RL-SIG
Protection | EHT+ PPDU can be used for protection/NAV setting in 6GHz band 11ax STAs can set NAV by EHT+ PPDU in 2.4/5GHz | Protection from pre-11be STAs cannot be done with EHT PPDUs Non-HT PPDU may not always be correctly classified as inter/intra-PPDU (e.g. CTS/ Ack from the associated AP may end up updating basic NAV)
Spatial reuse | 11ax STA may perform SR during ongoing OBSS EHT+ PPDU (see existing requirements on slide 2/3) | 11ax STA cannot perform SR during ongoing OBSS EHT+ PPDU

## Slide 9: Conclusion
Since the 11ax and 11ax+ devices may coexist in the same or overlapping networks, it would be desirable to design the preamble for 11be such that it will keep some nice features in 11ax and, if possible, make some signals understandable to 11ax devices
  Those signals may include TXOP, SR, BSS Color, etc.
If HE-SIG-A CRC is valid, the current 11ax PHY does not throw away the TXOP_DURATION, BSS_COLOR information, although it issues PHY-RXEND.indication(FormatViolation) primitive due to reserved values. This primitive stops 11ax receiver from further decoding the PPDU
The EHT PPDU may be used to set NAV in 6GHz band
The 11ax STAs may perform SR or intra-PPDU power save in the EHT PPDU duration, and understand TXOP_DURATION(NAV) set by the PPDU
Notes: Remove SR

## Slide 10: Reference
[1] 11-19/1021r1 Preamble Design Harmonization
[2] 11-19/1214r0 Preamble Design Consideration for 11be
[3] 11-19/1085r0 High-level EHT Preamble Structure

## Slide 11: SP1
Do you prefer an EHT-SIG design that enables 11ax STAs to acquire the TXOP and BSS color information?

## Slide 12: Appendix: 11ax SIG-A fields

## Slide 13: Appendix: Example of 11ax+ PPDU received by 11ax STAs without PHY-RXEND.indication(FormatViolation)
The 11be transmitter sets L_LENGTH%3==1:
  Future-SIG-A1 B0=1 (format)
  Future-SIG-A1 B2=UL
  Future-SIG-A1 B6-B7=’00’ (MCS MSB, DCM)
  Future-SIG-A1 B8-B13=BSS color of the 11be PPDU
  Future-SIG-A1 B14=1 (reserved)
  Future-SIG-A2 B15-B18=spatial reuse restrictions of the 11be PPDU
  Future-SIG-A2 B0-B6=TXOP_DURATION of the 11be PPDU
  Future-SIG-A2 B8=0 (LDPC Extra symbol)
  Future-SIG-A2 B11-B12=1~2 (a factor)
  Future-SIG-A2 B23=1 (PE disambiguity)
  Future-SIG-A2 B14=1 (reserved)
  Other bits can be used for 11be signaling
AP or 11ax+ receiver uses PE disambiguity=1 and a factor=1,2 to tell it is a 11ax+ PPDU
Bits not reusable by 11ax+ (9)
Bits useful to 11ax+/11ax (17)
Bits reusable by 11be (16)