## Slide 1: Coordinated AP Time/Frequency Sharing in a Transmit Opportunity in 11be
Date: Nov 2019
Name | Affiliation | Address | Phone | Email
Lochan Verma | Qualcomm Inc. |  |  | lverma@qti.qualcomm.com
George Cherian |  |  |  | 
Menzo Wentink |  |  |  | 

## Slide 2: Introduction
Multiple APs in vicinity of each other can coordinate and share between themselves their time/frequency resource within a TXOP
Frequency resource sharing i.e., CAP (Coordinated AP) OFDMA is a procedure wherein an AP that wins the medium access partitions its entire frequency resource and shares the smaller frequency chunks with its neighbor APs for the duration of the TXOP
Time resource sharing i.e., CAP TDMA is a procedure wherein an AP that wins the medium access partitions the duration of TXOP and shares its entire frequency resource for the small TXOP duration chunks with its neighbor APs
Intuitive gains: worst case-latency improvement; throughput fairness
Outline
  Concept introduction
  Assumptions
  Transmission sequence

## Slide 3: Introduction: CAP OFDMA
Compared to EDCA, in CAP OFDMA the TXOP Owner (AP that wins the medium access) shares smaller frequency resource chunks with other APs for the entire TXOP duration within the TXOP
  E.g., below shows 4 APs, each with 80MHz BW
AP1,AP2,AP3,AP4 transmissions maintain orthogonality

## Slide 4: Introduction: CAP TDMA
Compared to EDCA, in CAP TDMA the TXOP Owner shares entire frequency resource for the small TXOP duration chunks with other APs within the TXOP
  E.g., below shows 4 APs, each with 80MHz BW

## Slide 5: Assumptions for CAP OFDMA/TDMA
All APs in a CAP TX belong to the same ESS
An AP does not manage OBSS STAs
APs participating in a CAP TX are in range of each other
APs participating in a CAP TX not required to have the same P20
No pre-assigned Master AP or pre-assigned AP groups
  Does not preclude a Master AP, if a deployment chooses to
TXOP Owner orchestrates the time/frequency sharing in a TXOP
TXOP Owner in CAP OFDMA shares its frequency resource in multiples of 20MHz channels with other participating APs
No backhaul coordination between APs assumed, but over-the-air coordination
  Does not preclude backhaul coordination, if a deployment chooses to

## Slide 6: An example of CAP TX Phases
TXOP Owner orchestrates the time/frequency sharing in a TXOP
TX Ind & Req (Indication and Request)
  Neighboring APs learn of TXOP gained by TXOP Owner (Indication)
  TXOP Owner learns of neighboring AP’s intent to participate in a CAP TX (Request)
Schedule Allocation
  TXOP Owner tells participating APs their allocated subchannels, allocated TXOP duration, and TX start time
  Participating APs can tell their clients the allocated subchannels, allocated TXOP duration, and TX start time
Data TX
  Participating APs transmit on their respective allocated subchannels for the allocated TXOP duration beginning at the TX start time

## Slide 7: TX Ind & Req Phase and Schedule Alloc Phase
CTI & CTAS are non-HT DUP Trigger frame variant
  APs in vicinity not required to be on the same P20
CTR uses TB PPDU; transmitted by the APs in the vicinity of TXOP Owner
APs that are dst of CTAS, transmit CTLS that is non-HT DUP frame
CTI-CTR and CTAS-CTLS are SIFS interval separated
CTI: CAP TXOP Indication frame
CTR: CAP TXOP Request frame
CTAS: CAP TXOP AP Schedule frame
CTLS: CAP TXOP Local Schedule frame

## Slide 8: More on Frames in Schedule Alloc
CTAS frame: non-HT DUP Trigger frame variant
  Carries mapping for APID to subchannel, allocated TXOP duration, and TX start time
  APID can be MAC Addr (BSSID)
CTLS: Indicate subchannel allocation, allocated TXOP duration, and TX start time to respective BSSs
  Use non-HT DUP PPDU
    TA set to Special (predefined) value of (Multicast) MAC addr
    RA: Broadcast
  Doesn’t require all participating APs on the same P20
  Payload contains IE(s) indicating mapping for APID (i.e., BSSID)
  to subchannel mapping, allocated TXOP duration, and TX start time

## Slide 9: Data TX in CAP OFDMA
TXOP Owner and participating APs transmit on their respective BW chunks
Each sync FDMA TX composed of OFDMA for different users of that AP
  Sync FDMA here implies that each of the AP1, AP2, and AP3 transmit a PPDU that is orthogonal to each other

## Slide 10: Data TX in CAP TDMA
TXOP Owner and participating APs TX only for the allocated duration
Each TDMA transmission is composed of OFDMA for different users of that AP. Figure shows CAP TDMA with 4 APs and BW = 80 MHz
SIFS separation b/w participating AP transmissions

## Slide 11: SP #1
Do you support that the 802.11be defines a procedure for an AP to share its frequency/time resources of an obtained TXOP with a set of APs?
  Set of APs is TBD
  Including a mechanism to disable sharing by any STA
Y / N / A ::

## Slide 12: SP #2
In all modes of operation wherein an AP shares its frequency resource with a set of APs, the AP shall share its frequency resource in multiples of 20MHz channels with a set of APs in an obtained TXOP?
  PPDU format of the transmission on the shared resource is TBD
Y / N / A ::

## Slide 13: SP #3
In all modes of operation wherein an AP shares its frequency/time resource of an obtained TXOP with a set of APs,
  Define a mechanism for the TXOP owner AP to solicit feedback from neighboring APs
    Neighboring APs learn of TXOP gained by TXOP Owner (Indication)
    TXOP Owner learns of neighboring AP’s intent to participate in a CAP TX (Request)
Y / N / A ::

## Slide 14: SP #4
In all modes of operation wherein an AP shares its frequency/time resource of an obtained TXOP with a set of APs,
  Define a mechanism for the TXOP owner AP to schedule resources with neighboring APs such that:
    TXOP Owner tells participating APs their allocated subchannels, allocated TXOP duration, and TX start time
    Participating APs can tell their clients the allocated subchannels, allocated TXOP duration, and TX start time
Y / N / A ::

## Slide 15: SP #5
In all modes of operation wherein an AP shares its frequency/time resource of an obtained TXOP with a set of APs,
  Define a mechanism for the TXOP owner AP to initiate data transmission by participating AP such that:
    Participating APs transmit on their respective allocated subchannels for the allocated TXOP duration beginning at the TX start time
Y / N / A ::

## Slide 16: SP #6
The TX Indication and Request Phase (see SP #3) and Schedule Allocation Phase (See SP #4) shall include following frame exchanges
  The frame names are subject to change
CTI: CAP TXOP Indication frame
CTR: CAP TXOP Request frame
CTAS: CAP TXOP AP Schedule frame
CTLS: CAP TXOP Local Schedule frame