## Slide 1: Multi-AP backhaul analysis
Date: 2019-09-13
Authors:

## Slide 2: Introduction
Joint transmission (JT) has been extensively discussed as a candidate technology for 11be
  Gains from shared antenna resources
  Gains from independent maximum power limits in each of the APs
Joint operation consists of two main phases
  Information sharing: data to be sent jointly is sent from master AP to slave APs
  Joint transmission: all APs simultaneously send (shared) data to the target STAs
The performance gains of joint transmission have been simulated in numerous submissions [2-9]
The effect of information sharing (a.k.a. backhaul) has only received limited attention [1, 10]

## Slide 3: Observations on backhaul
Information sharing (backhaul) needs to provide a rate at least as high as the combined MU rate
  Amount of data exchanged during information sharing is equal to amount of data sent during joint transmission
  [1] establishes backhaul rates for certain example MU configurations
    It does not analyze how actual backhaul rate affects effective data rates
Backhaul rate is a function of distances/link quality between master AP and slave APs
  Independent of joint transmission
  Worst Master-slave link determines possible rate

## Slide 4: Goals of this submission
Provide quantitative analysis of impact of backhaul rate
Discuss in-channel vs. off-channel backhaul
Establish expectations for backhaul rates

## Slide 5: Impact of in-channel backhaul on effective throughput
One joint transmission involves the following exchanges:
Backhaul adds to the total time needed for every MU transmission  effective rate is lower than joint MU rate
Effective rate depends on:
  : MU rate
  : backhaul rate
NOTE: We’ll ignore other protocol overhead (sounding/trigger/…)

## Slide 6: Impact of in-channel backhaul on effective throughput (2)
We get:
  Time needed to send data bits at backhaul rate
  Effective data rate:

## Slide 7: Effective Throughput
In-channel backhaul always reduces the effective throughput (unless is infinite)
= yields an effective throughput of
  It’s not sufficient to have a backhaul rate as high as the MU rate!
  Backhaul rate should be much higher than to avoid degradation of the effective throughput
NOTE: A similar result applies to joint BF

## Slide 8: Example (1)
Two 4x4 APs (80 MHz), sending a total of 6 SS, MCS 7 ( = 2162 Mbps)
only ≈ 1 Gbps, even for aggressive backhaul rate (4 SS, MCS9)
Gains from joint transmission are entirely lost to backhaul overhead

## Slide 9: Example (2)
Four 4x4 APs (80 MHz), sending a total of 12 SS, MCS 7 ( ≈ 4400 Mbps)
Dramatic reduction in effective throughput, even for aggressive backhaul rate (4 SS, MCS9)
Impact of backhaul grows as grows

## Slide 10: Notes on in-channel backhaul
In-channel backhaul leads to dramatic reduction in effective throughput
Backhaul rate should be significantly exceed the combined MU data rate
Effect gets worse for higher number of APs (higher )
  doesn’t grow with number of APs, but does

## Slide 11: Off-channel backhaul
Data and backhaul in different Wi-Fi channels
  Could be different BW
Two scenarios
  Reuse antennas, i.e.: same antennas are used to do backhaul in off-channel as are used for in-channel MU transmission
  Separate set of dedicated antennas for backhaul

## Slide 12: Off-channel backhaul with antenna reuse
During backhaul, no MU transmission possible
  Identical dependency on as for in-channel backhaul!
Off-channel backhaul does not solve the issue if antennas are shared

## Slide 13: Off-channel backhaul with dedicated antennas
Joint transmission can deliver full as long as backhaul can keep up, i.e.
Otherwise:
Significant reduction in effective throughput even at “realistic” backhaul rates (e.g. 4SS, MCS 9)

## Slide 14: Notes on off-channel backhaul
Without dedicated backhaul resources (chains), backhaul is as limiting as in-channel backhaul
Multi-AP devices using off-channel backhaul need separate antennas/chains for backhaul and data
  In addition, should be higher than
Off-channel use should not be considered “free”
  It occupies a shared resource and makes it unavailable for others
  A multi-AP system with 80 MHz data channel and 160 MHz backhaul channel really occupies 240 MHz of spectrum
    Spectral efficiency should be figure of merit as well

## Slide 15: What is expected backhaul rate?
Joint Multi-AP operation assumes that APs are neither too close together nor too far apart
  Too close: mesh solution doesn’t make sense
  Too far: information sharing becomes severe bottleneck
Achievable rate depends on minimum rate across all AP-M/AP-S links
Optimistic Mid-range MCS ≈ 1-2 Gbps (160 MHz, 3SS)
  Higher is not realistic with wireless backhaul

## Slide 16: Wired backhaul
Maybe not be suitable for all deployment scenarios
  possibly in e.g. enterprise deployment
High rates achievable
  10 Gbps?
Effective throughput is limited in the same way as off-channel with dedicated chains:
  May be possible to achieve higher

## Slide 17: Conclusion
Backhaul in joint operation can have significant impact
  In-channel backhaul doesn’t appear practical
  Off-channel backhaul with antenna sharing doesn’t appear practical
  Best solution is an independently operating backhaul
    Off-channel wireless or wired
    Dedicated antennas/wired interface
Impact of backhaul should not be ignored
  More work is needed to address this issue
  Specifically, simulation results should include assumptions and impact of backhaul

## Slide 18: References
[1] Joint Transmissions, Backhaul and Gain State Issue, IEEE 802.11-19/1089
[2] Performance of Coordinated Null Steering in 802.11be, IEEE 802.11-19/1212
[3] Evaluation of joint transmission, IEEE 802.11-19/1092
[4] Joint BF Simulations, IEEE 802.11-19/1094
[5] Performance Investigation on Multi-AP Transmission, IEEE 802.11-19/779
[6] Multi-AP Collaborative BF in IEEE 802.11, IEEE 802.11-19/772
[7] Performance on Multi-band Operation, IEEE 802.11-19/777
[8] Joint Processing MU-MIMO Update, IEEE 802.11-19/800
[9] Comparison of CBF and JT, IEEE 802.11-19/799
[10] Joint Beamforming protocol simulation, IEEE 802.11-19/92