## Slide 1: Coordinated Beamforming/Null Steering Protocol in 802.11be
Date: 2019-09-16
Authors:
Name | Affiliation | Address | Phone | Email
David Lopez-Perez | Nokia |  |  | david.lopez-perez@nokia-bell-labs.com
Adrian Garcia-Rodriguez |  |  |  | 
Lorenzo Galati Giordano |  |  |  | 
Mika Kasslin |  |  |  | 
Olli Alanen |  |  |  | 
Enrico Rantala |  |  |  | 
September 2019

## Slide 2: Introduction
Coordinated beamforming/null steering has attracted considerable attention in previous 802.11be meetings
In this contribution, we
  review the major joint transmission/reception challenge,
  put forward coordinated beamforming/null steering, as an appealing inter-AP coordination scheme, and
  sketch a protocol to efficiently realize the coordinated beamforming/null steering gains
September 2019

## Slide 3: Coordinated beamforming/null steering as a first and handier step
Joint transmission/reception provides theoretical gains over coordinated beamforming/null steering
However, such gains may be hard to realise in practice
  Main concern: ‘For retail and carrier markets, where backhaul is over-the-air, backhaul needs higher BW than fronthaul. 80MHz joint transmission fronthaul needs 160MHz backhaul’ [19/1089]
Coordinated beamforming/null steering may offer a more appealing complexity/performance trade-off*
  Joint transmission/reception may be considered as
    An enterprise—more complex—802.11be solution, and/or
    A post-802.11be future enhancement
* A joint transmission/reception architecture can also realise coordinated beamforming/null steering
September 2019

## Slide 4: A protocol to realise coordinated beamforming/null steering
An efficient protocol is needed to realise the coordinated beamforming/ null steering gains presented in earlier contributions
  Significant throughput gains of up to 2.7x (5%-tile) [19/1212]
  We are working on enhancing our simulation results in [19/1212] with the feedback obtained in previous meetings
Such protocol requires:
  0. Semi-static inter-AP coordination establishment
  Enhanced spatial reuse opportunity (eSRO) coordination
  CSI acquisition procedure
  Coordinated inter-AP data transmission and acknowledgement with nulls
September 2019
Within TXOP

## Slide 5: Reference scenario
2 APs
  with multiple antennas each—more than STAs to serve
1 STA per AP
  with a single antenna and UL data to transmit (scheduled access)
Simultaneous access due to inter-AP coordination and null steering
September 2019
simultaneous access
null
APs listen to each other
AP1(donor)
STA21
AP2 (donee)
STA11
null
UL data
UL data

## Slide 6: Phase 0 — Semi-static inter-AP coordination establishment
Similar to the inter-BSS set in 802.11ax, we propose the inter-BSS coordination set, which
  contains the IDs of all nodes that form part of the inter-BSS coordination set,
  is configured and updated on the fly in a semi-static manner, and
  is kept in the memory of each of those nodes
Upon packet reception, a node will not discard packets from inter-BSS nodes that are included in its inter-BSS coordination set
Related proposal at [19/1019]
AP1
AP2
Inter-BSS coord_set_request
Inter-BSS coord_set_response
Example of message exchange to acquire the IDs of the AP and non-AP nodes to form an inter-BSS coordination set
September 2019

## Slide 7: Phase 1 — Enhanced spatial reuse opportunity coordination
Upon gaining a TXOP, an AP in the inter-BSS coordination set may proactively broadcast an enhanced spatial reuse opportunity (eSRO) ‘with nulling’ capabilities
  This broadcast itself does not has nulls in place during its transmission
APs willing to benefit from such eSRO shall respond, indicating the IDs of the nodes that would benefit from such interference mitigation
Related proposal at [19/1143]
donor AP1
donee AP2
spatialReuse_coordMsg
spatialReuse_coordResponse
Example of message exchange to coordinate a spatial reuse opportunity with nulls and understand which nodes can take advantage of it
My STA21 can benefit from nulling
September 2019

## Slide 8: Phase 2 — CSI acquisition procedure
Once the donor AP decides which nodes to serve/null in the inter-AP coordinated transmission, APs participating in it require the relevant CSI to place the corresponding beams/nulls
  Thanks to the inter-BSS coordination set, any AP in the set can ‘poke’ any other node in the set—even if non-connected—for such relevant CSI
  Explicit and implicit-CSI acquisition should be supported in 802.11be
Through the NDPA, the donor AP reveals/indicates the nodes participating in the subsequent inter-AP coordinated transmission
CSI acquisition may not be needed in all TXOPs
Related proposals at [19/1097] and [19/1134]
September 2019

## Slide 9: Phase 2 — Explicit CSI acquisition procedure
STA11
STA 21
NDP
NDP
TF
Feedback
Feedback
Feedback
TF
Feedback
Feedback
Feedback
NDPA
Transfer and return frames may be needed to coordinate AP1 and AP2 actions
Through the NDPA, the donor AP reveals the nodes participating in the inter-AP coordinated transmission
An AP can collect CSI from a neighbouring AP
September 2019
donor AP1
donee AP2

## Slide 10: Phase 2 — Implicit CSI acquisition procedure
NDP
TF
TF
NDP
NDP
NDP
NDPA
Transfer and return frames may be needed to coordinate AP1 and AP2 actions
NDP
NDP
Through the NDPA, the donor AP reveals the nodes participating in the inter-AP coordinated transmission
An AP can collect CSI from a neighbouring AP
September 2019
STA 21
donor AP1
donee AP2
STA11

## Slide 11: Phase 3 — Coordinated inter-AP DATA TX and ACK with nulls: An uplink-uplink example
Similar to the spatial reuse parameter (SRP) framework in 802.11ax,
  The donor AP uses an enhanced TF to advertise the enhanced spatial reuse opportunity (eSRO) ‘with nulling’ during its uplink reception
  The donee AP
    contends for the channel
    transmits a basic TF once its counter reaches zero
    its uplink reception and downlink acknowledgement must be within the TXOP of the donor node and sync with them
  Note that STAs of the slave AP could also content for the channel
Null steering is used to make sure that inter-AP communications do not interfere each other (see next slide)
September 2019

## Slide 12: Phase 3 — Coordinated inter-AP DATA TX and ACK with nulls: An uplink-uplink example
September 2019
TF
ACK
eTF
UL data
UL data
ACK
Contention
simultaneous access
null1
APs listen to each other
AP1(donor)
STA21
AP2 (donee)
STA11
null2
null3
Note: Null3 is not required if contention-based access for STA 21
Thanks to the nulls, we can have concurrent ACKs
UL data
UL data
STA 21
donor AP1
donee AP2
STA11

## Slide 13: Conclusions
September 2019
In this contribution, building on 802.11ax, we have proposed an efficient coordinated beamforming/null steering protocol
This protocol has four phases
  0. Semi-static inter-AP coordination establishment
  Enhanced spatial reuse opportunity (eSRO) coordination
  CSI acquisition procedure
  Coordinated inter-AP data transmission and acknowledgement with nulls
The proposed protocol is inline with other 802.11be proposals

## Slide 14: References
  Sammir Vermani (Qualcomm), Joint Transmissions: Backhaul and Gain State Issues, 19/1089
  David Lope-Perez (Nokia), Performance of Coordinated Null Steering in 802.11be, 19/1212
  Wook Bong Lee (Samsung), Virtual BSS For Multi AP Coordination, 19/1019
  Sungjin Park (LG Electronics), Efficient Operation for Multi-AP Coordination, 19/1143
  Ross Jian Yu (Huawei), Sounding procedure in AP collaboration, 19/1097
  Kosuke Aio (Sony), Consideration on Multi-AP Sounding, 19/1134
September 2019

## Slide 15: Straw Poll
Do you believe coordinated beamforming/null steering is an appealing feature for 802.11be and that the 802.11be TG should look into it in more detail?
  Yes
  No
  Abstain
September 2019

## Slide 16: Appendix
September 2019

## Slide 17: When is coordinated beamforming/null steering useful?
July 2019
BB
BB
BB
BB
Dense scenarios with high interference
  There must be inter-AP interference to null
  where, in addition, the served STAs enjoy high SNRs
  Placing a radiation null reduces the degrees of freedom (d.o.f.) for beamforming, and thus the beamforming gain, penalizing cell cell-edge STAs
  where, in addition, the number of spatial streams to serve is reasonably smaller than the available d.o.f. at the antenna array in the AP
  As for the Shannon-Hartley theorem, multiplexing gains are linear, while SINR gains are logarithmic in terms of capacity, and the later gains should not come at the expense of the former

## Slide 18: Coordinated null steering in 802.11be
Simultaneous access and interference mitigation at expense of beamforming gain
July 2019
802.11be with no coordinated null steering
APs with up to 16 antennas
Multiple STAs per AP to serve
Spectrum shared according to CSMA/CA
Under utilization of the array capabilities – number of spatial streams << available spatial degrees of freedom of the array
802.11be with coordinated null steering
Coordination and nulling in place to
enhance spatial reuse,
fully utilize the available spatial degrees of freedom of the array, and
mitigate OBSS interference
BB
BB
BB
BB
simultaneous access
nulls
nulls
APs listen to each other
BB
BB
URLLC
BB
BB
URLLC
AP
1
AP
2
BB
time sharing
beam
beam
APs listen to each other
BB
BB
BB
URLLC
BB
BB
BB
BB
URLLC

## Slide 19: System model
X
July 2019
Frequency/Bandwidth | 5.18GHz/80MHz (1 channel)
AP deployment | Ceiling mounted ¦ Inter-AP distance = 15m ¦ AP height = 3m
AP characteristics | AP Tx power = 24dBm ¦ 8x2 antenna array (0.5λ separation) ¦ omni antenna element ¦ NF = 7dB
STA deployment | 4 broadband STAs/AP (≈5m from AP) ¦1 low-latency STA/AP (≈3m from AP) ¦ STA height = 1m (see previous figure)
STA characteristics | STA Tx power = 15dBm ¦ 1 omni antenna ¦ NF = 9dB
Channel model | 3D spatial channel model (3GPP TR38.901 – InH [14])
Channel estimation | a) Implicit channel est. with perfect CSI (fixed pilot overhead) b) Explicit channel est. with perfect CSI (Uncompressed BF feedback)
MAC layer conf. | No EDCA ¦ No RTS/CTS ¦ TXOP = 4ms ¦ IP/MAC header overhead considered ¦ Minstrel MCS selection
PHY layer conf. | Precoder = MU ZF (with and without nulls) ¦ PHY header overhead considered ¦ Omni PLCP header ¦ 11ax MCSs

## Slide 20: Traffic models
July 2019
Broadband STAs
FTP3 traffic model [15]
File size = 0.5 MBytes
Offered traffic = [25 50 75 100] Mbit/s exponential arrival rate
Low-Latency STAs
AR traffic model [16]
File size = 32 bytes
Frequency = 10 ms
constant arrival rate
AP
1
AP
2
AP
1
AP
2
Per STA traffic
time
Mix of broadband and low-latency traffic models
Per STA traffic
time

## Slide 21: Broadband performance as function of nulls number and offered traffic
Null steering provides significant capacity gains, up to 2.7x
July 2019
Coordination and null steering provides significant throughput (TP) gains due to
  more aggressive spectrum access
  inter-AP interference mitigation
For 25Mbps/STA offered traffic,
  2 nulls provide 43% 5%-tile TP gain w.r.t. no nulling.
  Placing more nulls does not improve performance, as the number of simultaneously active STAs is low
For 100Mbps/STA offered traffic,
  2 nulls provide 76% 5%-tile TP gains w.r.t. no nulling
  3 nulls provide 2.3x 5%-tile TP gains
  4 nulls provide 2.7x 5%-tile TP gains.
  The nulling gain decreases with the number of nulls as the UEs most vulnerable to interference are nulled first
Implicit CSI

## Slide 22: Latency performance as function of nulls number and offered traffic
Null steering provides lower latencies and jitter variances
July 2019
Coordination and null steering also provide lower latencies
  due to the more aggressive spatial reuse and interference mitigation
  Further lower latencies could be achieved through reduced TXOP durations
For 100Mbps/STA offered traffic,
  with 0 nulls, 22% of the low-latency packets do not make it within the 10ms deadline
  with 4 nulls, all low-latency packets make it on time
  Further SINR increases due to more nulls do not bring substantial latency advantages, since the low-latency packets are small and utilize low MCSs
TCP/IP will benefit from the ‘narrower’ delay distributions
Implicit CSI

## Slide 23: Implicit versus Explicit CSI acquisition
Implicit CSI is desirable to make the most out of null steering
July 2019
Explicit CSI is penalized by the overhead of NDPA+NDP+TF+feedback
  This overhead grows with the number of spatial streams and nulls scheduled
  The more nulls, the larger the overhead
  With 0 nulls, implicit CSI provides 28% median TP gains w.r.t. explicit CSI
  With 2, 3 and 4 nulls, such gains are 19%, 28% and 36%, respectively
  When using explicit CSI, the gain provided by the more nulls may be lost due to CSI acquisition overhead
Offered Traffic = 100Mbps