## Slide 1: Triggered P2P Follow-up
Date: 2019-08-23
Authors:

## Slide 2: Abstract
Challenges with Direct Link transmission.
Using RDP to enable Direct Link transmission.

## Slide 3: Introduction
Direct Link transmission => A Direct Link Scheduled (“DLS”) STA communicates directly with another Direct Link Peer STA (“DLP”).
  Peer STA may not be associated to the same AP.
Benefits of Direct Link transmission [1] :
  high throughput because lower number of transmissions
  low latency due to one hop communication.
However, EDCA based Direct Link transmission causes high interference within BSS => need for AP to trigger such transmission.
AP transmits a Direct Link Announcement (DiL-A) frame with TBD format that triggers Direct Link transmission from one or more STAs.
Slide 3
Dibakar Das, Intel
AP
DiL-A
DLS STA
DLP STA
SIFS
Data
SIFS
Ack
TXOP

## Slide 4: Possible Topologies
Both STAs associated
to same AP.
Only one STA associated
to the Triggering AP.
: Non-AP STA
: AP
Case 1
Case 2
DLS
STA
DLP STA
DLS STA
DLP
STA

## Slide 5: What needs to be defined ?
Direct Link Service Discovery and setup
  Discovery of EHT TB Direct Link capability.
  EHT TB Direct Link setup between AP and non-AP STAs (associated or non-associated).
Data transmission procedure
  Specify signaling inside DiL-A and behavior of STAs participating in the Direct Link transmission.
  Ways for DLS STA to report resource allocation request to AP.
    Incl. both periodic and aperiodic allocations (e.g., airtime request).
Support for Cascaded Direct Link transmission: DLS STA may solicit transmission from DLP STA for bidirectional traffic within allocated time.
  Typical use-case: VR to console communication [2]
Notes: Discovery of EHT TDL capability:
1. Inform AP that TD peer STA wants to do P2p
2. Between the two P2P STAs they can use a new setup or TDLS or some proprietary setup (e.g., NAN).

## Slide 6: Extending RDP for DiL transmission
DL transmission requirements similar to RDP which also grants TXOP to a STA that is not TXOP initiator.
Issues in extending RDP for Triggered DL transmission:
  RD responder needs to at least transmit to the TXOP initiator in each PPDU.
    “During an RD response burst any PPDU transmitted by an RD responder shall contain at least one MPDU with an Address 1 field that matches the MAC address of the RD initiator”
  What is the Duration/ID field and NAV setting for each topology in slide 4 ?
Solution:
  Allow DLS STA to transmit to DLP STA in a PPDU that does not contain any frame to the TXOP initiator.
    The exact rules to achieve this behavior is TBD.
  Duration/ID field contains the remaining TXOP when transmitted by the AP.
DiL-A frame to DLS STA (Duration = Rem TXOP, allocated time = T)
Data to DLP STA (Duration = Rem allocated time)
Ack + Data to DLS STA (Duration = Rem allocated time)
AP
DLS STA
DLP STA
TXOP
SIFS
SIFS
SIFS
Allocated time T
Ack
Notes: In general, multiple STAs can be triggered in the same TXOP.
Either QoS-NULL/Mgt frame with No Ack for associated STAs and Ctrl frame for unassociated STAs.
  Special A-Ctrl field in frame txmitted by scheduling AP to signal time allotted to the triggered P2P STA.
  Special A-Ctrl field in frame txmitted by triggered P2P STA to signal time allotted to the peer P2P STA.

## Slide 7: Extending RDP for DiL transmission (contd.)
Two options for the Duration/ID field of frames transmitted by DLP and DLS STA.
Option 1: If both those STAs are associated to the same BSS as the triggering AP (topology 1), the Duration/ID field is set to remaining NAV duration setup by AP.
Option 2: For topology 2, the Duration/ID field of frames transmitted by those STAs signals the remaining time allotted to this STA if not in same BSS as scheduling AP.
Notes: TBD: how to handle RTS-CTS

## Slide 8: Error Recovery
AP only initiates recovery if not detected transmission within SIFS from the DiL-A frame.
Otherwise, AP does not regain control of TXOP until either the end of the allocated time to the DLS STA or receipt of a frame from that STA.
  TBD signaling.
DiL-A frame to DLS STA
Data to DLP STA
Ack + Data to DLS STA
AP
DLS STA
DLP STA
TXOP
SIFS
SIFS
Trigger P2P
End
SIFS
Frame to another STA
SIFS
…

## Slide 9: Summary
Discussed challenges with Triggered P2P operation.
Proposed extensions to baseline RDP to enable Triggered P2P operation.
Future topics of discussion: AP triggering unassociated STAs.

## Slide 10: References
11-18-1481-01-0eht-technology-for-EHT
11-18-2009-06-0rta-rta-report-draft

## Slide 11: Motivation
P2P communication can significantly reduce the load on the BSS and simultaneously the latency by a one-hop communication.
About 70% reduction in
latency/airtime possible in
the two floor home scenario
by using P2P communication among users in the same room.

## Slide 12: Pre-data phase negotiation
STA requests an AP to be scheduled for periodic or aperiodic operation.
  For periodic operation, a version of TWT can be negotiated.
  For aperiodic operation,
    Associated STA can use a QoS Data/Null frame with special signaling in A-Ctrl field containing requested duration of service.
    Unassociated STAs can use a Mgt frame containing above signaling.
Multi-AP: An STA can setup a schedule with multiple APs.
  Unicast frame in a Multi-AP set.
  Broadcast frame for APs that are not part of same Multi-AP set.