## Slide 1
Multi-link TXOP Sharing
for Delay Reduction
Date: 2019-09-16
Authors:

## Slide 2: Introduction
Three advantages of multi-link operation (MLO) have been discussed [1][2]
  Enhanced high peak throughput
  Reliable transfer
  Reduced latency and jitter
Reduced latency and jitter are the key feature of EHT devices
  Backoffs cause severe delay
  Data transmission without backoffs helps to reduce delay
  TXOP sharing techniques that avoid backoffs have been proposed in 11ac [3]
In this contribution, the concept of multi-link TXOP sharing for delay reduction is presented

## Slide 3: Legacy TXOP Sharing Technique
Downlink MU-MIMO or OFDMA
MU-BAR

## Slide 4: Multi-link TXOP Sharing in Downlink
Simultaneous (synchronous) transmission
Duplicated Block Acks:
Block acks shall be aligned to
maximize the throughput

## Slide 5: Multi-link TXOP Sharing Uplink Scenario

## Slide 6: Multi-link TXOP Sharing in Uplink
Multiple STAs can transmit simultaneously
Multi-STA Block Ack:
Let STA1 know that the sharing is over
Sharing Request:
Trigger frame based format
Detailed role is TBD

## Slide 7: UL OFDMA vs. Multi-link TXOP Sharing
UL OFDMA technique assigns RUs to each STA according to trigger frame
  The time at which the trigger frame is transmitted is strongly determined by the channel contention of the AP
Multi-link TXOP sharing can be deployed by channel contention of EHT STAs
  The channel contention by many EHT STAs may eventually reduce the delay of the entire network

## Slide 8: UL OFDMA vs. Multi-link TXOP Sharing (Cont’)

## Slide 9: Technical Consideration #1
Refusing TXOP sharing issue
  Basically, TXOP belongs to a TXOP holder
  However, in uplink scenario of multi-link TXOP sharing, AP can give the part of the TXOP to the other STAs
  TXOP holder shall be able to refuse the sharing
Two options
  Implicit refusing
  Explicit refusing

## Slide 10: Implicit Refusing
The sharing period begins after xIFS instead of SIFS
xIFS > SIFS

## Slide 11: Implicit Refusing (Cont’)
TXOP holder can refuse the sharing by just transmitting PPDUs after SIFS
SIFS

## Slide 12: Explicit Refusing
TXOP holder (STA1) lets AP know the sharing information
Trigger Frame:
Trigger frame solicits the
transmission of STA2
MAC Header:
Various sharing information is contained
e.g., sharing permission, sharing target, sharing period, and so on

## Slide 13: Technical Consideration #2
Basic NAV issue
  There are two NAVs in 11ax
  Sharing target cannot transmit data even though SR or TF is received
  Basically AP cannot know the status of basic NAVs at the other STAs

## Slide 14: Option #1
AP takes the sharing period
I
Bigger than xIFS:
It can be PIFS or DIFS according
to the refusing technique

## Slide 15: Option #2
AP allocates RUs incrementally

## Slide 16: Option #2 (Cont’)
AP returns the sharing link to the TXOP holder

## Slide 17: Conclusion
In this contribution, downlink and uplink scenarios for multi-link TXOP sharing have been proposed
Two technical issues for multi-link TXOP sharing have been discussed

## Slide 18: Straw Poll
Do you support the following definition?
  Multi-link TXOP Sharing: In multi-link transmission, one or more links shall be shared to other ACs or STAs while at least one link is utilized by the primary AC or TXOP holder
  NOTE – The frames from the other ACs or STAs may be included when at least one frame from the primary AC or TXOP holder has been transmitted
Y/N/A

## Slide 19: References
[1] 18/1231r6 EHT Draft Proposed PAR, Laurent Cariou (Intel)
[2] 19/1095r1 Multi-Link Architecture and Requirement Discussion, Yonggang Fang (ZTE)
[3] Draft P802.11REVmd_D2.3