## Slide 1
Authors:
Multi-band/Multi-channel Operation for Low Latency and Jitter
Date: 2019-09-15
Name | Affiliation | Address | Phone | Email
Liuming Lu | ZTE Corporation | No.889 Bibo Road, Shanghai, P.R.China |  | lu.liuming@zte.com.cn
Liquan Yuan | ZTE Corporation | No.889 Bibo Road, Shanghai, P.R.China |  | yuan.liquan@zte.com.cn
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 1

## Slide 2: Introduction
Multi-band/multi-channel operation has been proposed as a main candidate feature in TGbe. And at least one mode of operation capable of improved worst case latency and jitter will be defined in TGbe.[1][2]
This contribution gives some views on multi-band/multi-channel operation to improve worst case latency and jitter for the real-time transmission of RTA data.

## Slide 3: Background
Multi-band/multi-channel operation can improve the worst case latency and jitter since it uses two or more bands or channels to transmit data.
But how much multi-band/multi-channel operation can improve the worst case latency and jitter needs to be considered.
Contribution[3] has presented latency gains with multi-link aggregation, showing that adding an auxiliary link significantly improves the worst-case latency. But the latency gains seem to be not enough to support the RTA, such as virtual reality or augmented reality.
The mechanisms for multi-band/multi-channel operation, such as channel access method, admission control etc., need to be optimized to satisfy the requirements for low-latency and jitter performance.

## Slide 4: Requirements for the optimization of of multi-band/multi-channel operation
Use cases |  | Intra BSS latency/ms | Jitter variance/ms | Packet loss | Data rate/Mbps
Real-time gaming |  | < 5 | < 2 | < 0.1 % | < 1
Cloud gaming |  | < 10 | < 2 | Near-lossless | <0.1 (Reverse link) >5Mbps (Forward link)
Real-time video |  | < 3 ~ 10 | < 1~ 2.5 | Near-lossless | 100 ~ 28,000
RTA use cases and requirements (examples) [4]
Latency gain results of simulation [3]
MCS0 | 1 OBSS STA per link | 2 OBSS STAs per link | 4 OBSS STAs per link | 8 OBSS STAs per link
Multi Link (80MHz+20MHz) | 9.24 | 22.89 | 61.88 | 325.2
The latency improvement is not enough to support RTA if only depending on the multi-link operation. The combination of multi-band/multi-channel operation , time scheduling and admission control needs to be considered to further lower the latency and jitter so as to satisfy the requirements for RTA.

## Slide 5: Channel access methods for multi-band/multi-channel operation
Flexible channel access methods can be considered for multi-band/multi-channel operation. Different kinds of channel access methods can be respectively adopted for different bands or channels. TDMA/TDD-like scheduling function such as HCCA can also be considered besides CSMA/CA and triggered-based channel access method.
Channel@Band1
AP
Channel@Band2
STAs
CSMA TXOPS
CAP (Controlled Access Phase)
CSMA TXOPS
Channel@Band1
Channel@Band2
Schedulable TXOPs
TXOPs through contention

## Slide 6: Admission control for multi-band/multi-channel operation
Since admission control is a direct method to lower latency and jitter, flexible admission control strategies can be adopted for different bands or channels according the types of application, the priorities of the services, the types of STAs, etc.
Different kinds of applications can be loaded on different bands or channels. For example, the RTA data which needs low latency and jitter is controlled to be transmitted on one channel or band, and the data of best-effort applications is controlled to be transmitted on the other channels or bands.
The number of the STAs to access the channel which transmits the data of RTA applications is strictly limited to guarantee the low latency and jitter performance.

## Slide 7: Conclusions
The latency improvement is not enough to support RTA if only depending on the multi-band/multi-channel operation.
The combination of multi-band/multi-channel operation, time scheduling and admission control needs to be considered to further lower the latency and jitter so as to satisfy the requirements for RTA.
Flexible channel access methods can be considered for multi-band/multi-channel operation.

## Slide 8: References
11-18-1231-06-0eht-eht-draft-proposed-par, 802.11 EHT Proposed PAR
11-18-1233-07-0eht-eht-draft-proposed-csd, IEEE 802.11 EHT draft Proposed CSD
11-19-1081-01-00be-multi-link-aggregation-gain-analysis-latency,Multi-Link Aggregation: Latency Gains
11-19-0065-06-0rta-rta-tig-summary-and-recommendations, RTA report summary

## Slide 9
Thank you!