## Slide 1: Frame Length Indication
Date: 2019-09-09
Authors:

## Slide 2: Frame Length Discussion[1]
Frame Length Indication
  NGV PHY Header indicates MPDU length in octets.
11p PHY
Header
NGV PHY
Header
MPDU
  MPDU Delimiter indicates MPDU length in octets.
11p PHY
Header
NGV PHY
Header
Data field
MPDU Delimiter
MPDU

## Slide 3: Recap: 11ac/11ax PPDU Assumption
L-SIG is used to indicate the PPDU length:
  LENGTH field in L-SIG is no more than 4095.
  RATE field in L-SIG is 6Mbps (MCS 0).
The 11ac/11ax maximal PPDU length is 5484us.
The maximal PSDU length is decided by the maximal BW, maximal PPDU length, maximal MCS, Nss, shortest GI.

## Slide 4: 11bd PPDU, PSDU Assumption
20MHz PPDU is candidate technology for 11bd.
With 3Mbps (MCS 0), and maximal Length 4095 octets in 11p SIG, the maximal 11bd PPDU size is about 5484x2 us.
With 20MHz PPDU, 2NSS, MCS 9, and PSDU length 5484x2 us, the Data field of 11bd PPDU can carry 1063896 octets.

## Slide 5: Discussion of Length in PHY Header
If the PHY header is used to indicate the Data field length, 17 bits are required.
The length indication in PHY header is not extensible.
11p PHY
Header
NGV PHY
Header
MPDU

## Slide 6: Proposal: Frame Length in MPDU Delimiter
3Mbps in L-SIG (in 11p PHY Header part) and Length in 11p PHY Header are used to define the Tx time.
MPDU Delimiter is widely used in 11n, 11ac, 11ax and the future 11 technologies in 2.4, 5, 6 GHz bands.
It is natural to use it in 11bd.
The NGV SIG becomes shorter once MPDU delimiter is used.
11p PHY
Header
NGV PHY
Header
Data field
MPDU Delimiter
MPDU
MPDU Delimiter with EoF equal to 0
11p PHY
Header
NGV PHY
Header
Data field
MPDU Delimiter
MPDU
MPDU Delimiter
MPDU
MPDU Delimiter with EoF equal to 1

## Slide 7: Straw Poll 1
Do you support that MPDU Delimiter is used to indicate the length of frame in octets carried in 11bd PPDU?

## Slide 8: Straw Poll 2
Do you support that the RATE field in 11p PHY header of 11bd PPDU is set to 3Mbps?

## Slide 9: Reference
[1] Liwen Chu, et al, “NGV MAC Discussions”, IEEE 802.11-18/1249r1