## Slide 1
Strongest Tap FTM for PEDMG
Date: 2019-10-02
Authors:

## Slide 2: Abstract
The presentation covers comments open CIDs
  FTM measurement for strongest CIR tap for PEDMG
  excluding PDMG, due to limited use-cases (no first path AWV)
  CID #:
    1427: R2I / I2R ToA Type to distinguish b/w first vs. strongest tap FTM
    2349: option to include strongest tap FTM with new trigger field 5
This presentations shows the motivation behind these comments and proposes corresponding resolutions

## Slide 3: Motivation
ToA and optionally AOA/AOD measurements of strongest arrival path (tap) of the CIR may be required for
  precise clock offset estimation in obstructed LOS (oLOS) scenarios, e.g., for sync of wireless speakers
    synchronization of multiple wireless speakers in oLOS scenario
    strongest tap FTM provides higher SNR  more precise synchronization
  enhanced positioning in oLOS scenario
    in addition to First Path measurements perform FTM based on strongest arrival path
    unknown reflector position, but additional AOA/AOD/ToA measurements
      solve overdetermined system of equations (see next slides)  ~ 25% accuracy improvement
  simple LOS/NLOS discrimination
reflector / scatterer
RSTA
ISTA
obstacle
regular AWV
first path AWV

## Slide 4: Current method in 11az: oLOS
– 2D position
: angular reference
In case of obstructed LOS (oLOS), accuracy of , may decrease and therefore increase .
Option I: angular information at ISTA
ISTA observes: ,
RSTA provides:
ISTA calculates:
Option II: angular information at RSTA
ISTA observes:
RSTA provides: , needs to be signaled by RSTA
ISTA calculates:

## Slide 5: Proposed Extension for oLOS
scenario vector:
observation vector:
where:
  observations:
  , , using FTM based on first CIR tap
  , , using FTM based on strongest CIR tap
Exploit both best and first path information
To localize ISTA, solve:
proposed
extension
unknows: scatterer position , and ISTA position (4 unknowns in 2D)
observations:  can be solved!

## Slide 6
Simulation results
error reduction @ 90th percentile
A:
B:
C:
A
B
C
Parameters:
see appendix
A
B
C
different ToF/angular deviations
comparison between first path (LOS) only positioning vs. first + strongest path (LOS+NLOS): accuracy improvements

## Slide 7: What is missing to allow extension
ISTA requires measurements:
cannot be precisely measured
  With current FTM for PEDMG:
trigger field 1: using regular AWV
|h()|

trigger field 2: using first path AWV
|h()|

first path propagation cluster
low SNR
ToA/angular measurements may be inaccurate
best path propagation cluster
 high SNR
noise floor
noise floor
cannot be used so far!

## Slide 8: FTM for PEDMG in D1.0/1.4: Proposal
Enable ToA measurement and exchange based on strongest CIR tap
  allows estimation of TOF of strongest path, which may result from NLOS component in case of oLOS
trigger field 1: using regular AWV  first CIR tap
|h()|

noise floor
first path propagation cluster
 low SNR
best path propagation cluster
 high SNR
trigger field 1: using regular AWV
 strongest CIR tap
|h()|

noise floor

## Slide 9: Required Changes
Request: There needs to be an indication informing the receiving device the ToF of which tap it should measure
  Whether it is first tap or strongest tap
  Preferred Solution
    Use reserved bit in EDMG Header A
    Requires least changes to spec
    Easy implementation
Report: There should be an indication informing how the measurement was performed

## Slide 10: Request: Enabling Strongest Tap FTM for PEDMG – EDMG-Header-A Definition
see 29.3.3.3.2.3: Reserved bit in EDMG-Header-A for SC (EDMG-MCS field definition when Number of SS field is 0) to request first path vs. strongest path measurement: signal, if
  ToA timestamp shall be based on the strongest arrival path of the CIR or
  ToA timestamp shall be based on the first arrival path of the CIR
|h()|

|h()|

EDMG Header-A flag = 0
first path propagation cluster
best path propagation cluster
first path propagation cluster
best path propagation cluster
EDMG Header-A flag = 1

## Slide 11: Report: ToA Error Field in FTM Frame
Feedback, which tap of the CIR was used
In FTM Frame / FTM Action field format (9.6.7.33)
  use reserved bit to indicate, if the ToA timestamp was calculated
    on the first tap of the CIR (if set to 0)
    or the strongest tap of the CIR (if set to 1)

## Slide 12: SP
Do you agree to enable the request and report of ToA measurement on strongest tap as optional alternative to the ToA measurement on first tap, for PEDMG?
Yes/no/abstain

## Slide 13: References
[1] Draft P802.11az D1.0
[2] "First Path FTM SFD Text", IEEE 802.11-17/1884r1
[3] D. W. Marquardt, “An Algorithm for Least Square Estimation of Non-Linear Parameters,” Jun. 1963
[4] F. Fellhauer et al., "Non-Line-of-Sight Positioning for mmWave Communications," IEEE 19th International SPAWC Workshop, Kalamata, Greece, 2018.
[5] 11-19-1507-02-00az-clause-11-22-6-4-9-cids.docx

## Slide 14
APPENDIX

## Slide 15: Simulation Parameters
Parameters:
-grid ( margin from walls)
, in center of scenario
Room Dimensions: , corresponding to Hotel Lobby channel model scenario
Realizations: , 10 realizations per location
FTM inaccuracy:
Angular inaccuracy:
Inaccuracy of AOA/D, TOF equal for both paths
eq. (1) solved with Levenberg–Marquardt algorithm
NOTE: LOS in figure refers to noisy LOS due to obstruction