## Slide 1: CSI-based Wi-Fi Sensing: Results and Standardization Challenges
Date:10/30/2019
Authors:

## Slide 2: Wi-Fi Sensing
What is Wi-Fi Sensing? [1, 2]
  Using existing standardized 802.11-based protocols to sense and track changes in the environment
Status
  Interest in WNG July session
  TIG created in September session to further explore Wi-Fi sensing
Why Wi-Fi?
  Ubiquitous, re-use existing technology for new use cases
  Device-free, extra sensor-free, privacy-friendly
  Feasible for interesting sensing applications [3, 4, 6, etc.]
What is missing?
  Reliability, consistency and availability of CSI
  Interoperability

## Slide 3: Use Cases*
Security
  Home security – intrusion detection
  Device security – personal electronics, vehicle unlocking
Automation
  Smart home – automation, HVAC control
  Gesture recognition – smart device control, gaming
Health care
  Elderly care – fall detection
  Recuperation – gait and presence detection
Localization
  Indoor and reverse location
*Also discussed in [3-6]

## Slide 4: Standard Compliant CSI Extraction
Explicit
  CSI tracking based on CBF
  Limited resolution due to compression
Implicit
  CSI tracking based on LTF
  Overhead without existing traffic
Channel direction not crucial
  Typical use cases only track changes over time
NDPA
NDP
CBF
CSI (1->2)
STA1
STA2
Data
CSI (2->1)
STA1
STA2

## Slide 5: CSI Parameters of Significance
Resolution
  Many application require high resolution (without compression) CSI
Periodicity
  Some use cases like fall detection might need a reliable periodicity of CSI
Coverage
  Depending on the size of the monitoring location coverage is essential
  Beamforming might affect isotropic coverage
Overhead
  In order to keep airtime usage low more efficient protocol needed

## Slide 6: Standardization Challenges* (1)
TX-side Adaptations
  Examples
    BW adaptation
    TX Power adaptation
    Beamforming, Antenna selection
    Power-save mode
  Possible solution
    Standardize indicator
    Fix parameters for sensing
* Challenges that can be alleviated by standardization
Parameter
Set 1
Parameter
Set 2
CSI from Stationary Environment

## Slide 7: Standardization Challenges (2)
Sounding Overhead [7, 8]
  Examples
    Explicit sounding – periodicity control of sounding frames
    Implicit sounding – data overhead
  Possible solution
    Efficient, scheduled or solicited sounding
Interoperability
  Availability and feature parity of CSI in current HW
Echo Request
Ack
Ack
STA1
STA2
Echo Response
Example implicit sounding
in absence of background traffic
Airtime comparison for explicit sounding [7]

## Slide 8: Standardization Challenges (3)
Privacy
  Examples
    Passive sensing – overhearing active links
    Active sensing – new link based tracking
  Possible solution
    Standardized obfuscation or encryption
    Problem – backward compatibility

## Slide 9: Conclusions
Wi-Fi sensing is growing in demand with many implemented solutions indicating feasibility
Standard-compliant CSI is an existing feature that can enable numerous practical applications
Standardization can make the CSI extraction process private, efficient and improve interoperability

## Slide 10: References
[1] Wi-Fi sensing, IEEE 802.11-19/1164
[2] Wi-Fi sensing: cooperation and standard support, IEEE 802.11-19/1416
[3] Wi-Fi sensing: Usages, requirements, technical feasibility and standards gaps, IEEE 802.11-19/1293
[4] 802.11 sensing: Applications, feasibility, standardization, IEEE 802.11-19/1626
[5] Usage models for WLAN sensing, IEEE 802.11-19/1725
[6] Discussion of market potential and technical feasibility about WLAN sensing, IEEE 802.11-19/1726
[7] MU sounding improvements, IEEE 802.11-18/1191
[8] Sounding-only support during ranging, IEEE 802.11-18/1630