## Slide 1: NGV 20MHz Spectrum Mask: Leftover issues
Date: 2019-11-11
Authors:

## Slide 2: Introduction
20MHz class C spectrum mask was discussed in previous meetings [1, 2, 3].
Some points in the mask have not reached consensus in last meeting.
We re-discuss the spectrum mask @15MHz, 20MHz and 25MHz.

## Slide 3: New 20MHz Class-C Masks: Recap
  For better adjacent channel operation, similar rolloff as 10MHz class-C mask.
  Based on our measurement and Skyworks data: x > 6dB.
xdB

## Slide 4: 20MHz New Class-C mask
Motion 53 in 11-19/0514r10:
  Same spectrum roll-off as 10MHz class-C mask at first three points.
  TBD Spectrum mask definition @15MHz, 20MHz and 25MHz.
Proposal in 11-19/1473r1 for the last three points:
  Concern about the zig-zag mask not matching with PA characteristic.
  Some other points may becomes the new bottleneck.
 | Permitted power spectrum density, dBr |  |  |  |  | 
 | +/-9.5 MHz offset (+/-f1) | +/-10 MHz offset (+/-f2) | +/-10.5MHz offset (+/-f3) | +/-15MHz offset (+/-f4) | +/-20MHz offset (+/-f5) | +/-25MHz offset (+/-f6)
Class C | 0 | -26 | -32 | TBD | TBD | TBD
 | Permitted power spectrum density, dBr |  |  |  |  | 
 | +/-9.5 MHz offset (+/-f1) | +/-10 MHz offset (+/-f2) | +/-10.5MHz offset (+/-f3) | +/-15MHz offset (+/-f4) | +/-20MHz offset (+/-f5) | +/-25MHz offset (+/-f6)
Option A | 0 | -26 | -32 | -40 | -50+x | -50

## Slide 5: New Proposal
 | Permitted power spectrum density, dBr |  |  |  |  | 
 | +/-9.5 MHz offset (+/-f1) | +/-10 MHz offset (+/-f2) | +/-10.5MHz offset (+/-f3) | +/-15MHz offset (+/-f4) | +/-20MHz offset (+/-f5) | +/-25MHz offset (+/-f6)
Option 1: Proposal in 0514r1 | 0 | -26 | -32 | -40 | -50+xdB | -50
 | +/-9.5 MHz offset (+/-f1) | +/-10 MHz offset (+/-f2) | +/-11MHz offset (+/-f3) | +/-20MHz offset (+/-f4) | +/-30MHz offset (+/-f5) | 
Option 2: New proposal | 0 | -26 | -32-ydB | -50+xdB | -50 | 
Option 2: New spectrum mask definition
  Tighten the mask @11MHz of ydB to maintain ~-32dBc @10.5MHz.
  Define the mask @20MHz of xdB as proposal in 0514r1.
  Extend -50dBc to 30MHz as existing 20MHz class C mask.

## Slide 6: New 20MHz Class C Mask
    -36dBc @11MHz and -44dBc @20MHz.
    Smaller adjacent 10MHz channel interference level.

## Slide 7: 10MHz ACI Analysis
  ydB = 4 or 6, ACI power reduces.
  ydB = 4 and xdB = 6, i.e. [-36dBc -44dBc] @[11MHz 20MHz] can be a good candidate with good margin. ACI power reduces by 0.5dB

## Slide 8: Summary
Two options to define new 20MHz Class-C mask
  Option 1: same proposal as in 0514r1
    Define xdB relaxation @20MHz point
  Option 2: new proposal to tighten mask @11MHz and relax @25MHz.
    Define xdB relaxation @20MHz point
    Define ydB tightening @11MHz point
    Relax the -50dBc mark point from 25MHz to 30MHz

## Slide 9: Reference
[1] Rui Cao and etc., “PHY Numerology Discussions”, IEEE 802.11-19/0686.
[2] Rui Cao and etc., “NGV 20MHz OFDM Numerology Discussions”, IEEE 802.11-19/1072.

## Slide 10: Straw Poll 1
Do you agree that to define the new 20MHz class C spectrum mask using?
Option 1:
Option 2:
Abstain:
 | Permitted power spectrum density, dBr |  |  |  |  | 
 | +/-9.5 MHz offset (+/-f1) | +/-10 MHz offset (+/-f2) | +/-10.5MHz offset (+/-f3) | +/-15MHz offset (+/-f4) | +/-20MHz offset (+/-f5) | +/-25MHz offset (+/-f6)
Option 1: Proposal in 0514r1 | 0 | -26 | -32 | -40 | -50+xdB | -50
 | +/-9.5 MHz offset (+/-f1) | +/-10 MHz offset (+/-f2) | +/-11MHz offset (+/-f3) | +/-20MHz offset (+/-f4) | +/-30MHz offset (+/-f5) | 
Option 2: New proposal | 0 | -26 | -32-ydB | -50+xdB | -50 | 

## Slide 11: Straw Poll 2
Do you agree that the new 20MHz class C spectrum mask value at +/-f5 (20MHz) shall be defined as?
  Option 1: -44dB
  Option 2: -42dB
  Option 3: -40dB
Option 1:
Option 2:
Option 3:
Abstain:

## Slide 12: Straw Poll 3
Do you agree that the new 20MHz class C spectrum mask value at 11MHz shall be defined as?
  Option 1: -34dB
  Option 2: -36dB
  Option 3: -38dB
Option 1:
Option 2:
Option 3:
Abstain: